## Slide 1: Discussion for enhanced VoLTE Performance

## Slide 2: Potential problems for VoLTE deployment
Field test performance data for EVS/AMR WB/AMR NB
Background
  Compared to AMR-NB, AMR-WB and EVS, especially channel aware mode, is designed to have both high quality voice and perform much very robustly in poor radio conditions and therefore VoLTE coverage border changes dynamically per the used codec/terminal.
  At the moment, HO threshold for VoLTE is usually chosen per worst case and configured in eNB statically e.g. -115dBm for AMR NB has to be chosen though -120dBm can work for EVS capable UE
Potential Problem
  However, RAN at the moment is not able to have this information and consequently VoLTE call could be handed over to 2/3G CS unnecessarily via SRVCC HO though the VoLTE call can survive LTE weak coverage
ViLTE requires much higher RSRP compared to VoLTE and has the similar problem
Chart: RSRP
EVS Avg. MOS | 4.3 | 4 | 3.2 | 2.9
AMR WB23.85 Avg.MOS | 3.95 | 3.5 | 2.8 | 2
AMR NB12.2 Avg. MOS | 3.65 | 3 | 2.5 | 2
-75 -115 -119 -122
-115dBm
-118dBm
-120dBm
Chosen worst HO Threshold

## Slide 3
Potential problem for VoLTE call setup procedure
  Assuming MO UE supports EVS/AMR while MT UE is a legacy and only supporting AMR, then AMR is usually chosen for the upcoming VoLTE call.
    If the MO UE is located in LTE weak coverage, which is bad for AMR but good for EVS, the UE will move to 2/3G with RobVoLTE.
    However, CSFB to 2/3G CS could be avoided if EVS is used for MO UE while AMR is used for MT UE i.e. a transcoding in ATGW.
  Note: the transcoding is performed only when the UE is located in LTE weak coverage
b)Expected Solution
a) Legacy solution

## Slide 4
Potential problem for ongoing VoLTE call handling
b) Expected solution
  Assuming MO UE supports EVS/AMR while MT UE is a legacy and only supporting AMR, then AMR is usually chosen for the upcoming VoLTE call.
  If the MO UE is located in LTE good coverage, which is good both for AMR and EVS, AMR could be chosen for the upcoming VoLTE call.
  After a while, when MO UE moves to LTE weak coverage area, where is bad for AMR but still good for EVS
    SRVCC will be triggered and the ongoing voice will be handed over to 2/3G
    However, the UE better to stay on LTE by changing AMR to EVS rather than performing SRVCC to 2/3G CS i.e. transcoding in ATGW.
a) Legacy solution

## Slide 5
Way forward in 3GPP SA2
Except VoLTE/ViLTE, the problem should also apply to any service that may have specific requirement for radio coverage
It is proposed to use VoLTE/ViLTE as start point since these two scenarios is very clear and the associated solution should be flexible enough for any services that that may have specific requirement for radio coverage

## Slide 6: Annex: Call flows