## Slide 1
Network slicing way forward
Nokia, ZTE, Telecom Italia, KDDI, Interdigital, SAMSUNG, ETRI, KPN
3GPP TSG SA WG2#117, Oct 17 – 21, 2016, Kaohsiung City, Taiwan
S2-165696

## Slide 2: NextGen Slicing Conceptual foundations
Provide a UE with access to a portfolio of possible Network Instances offering different Control Plane and User Plane behaviours, and different Service Levels (i.e. meeting certain SLAs which are associated to the concept of Tenancy of a Network Slice)
  A Network Slice may use additional credentials and authentication protocol and authorization method than the one used to secure authenticated/authorized access to the PLMN
  Inside a Network Slice, a third level of Authentication/authorization per DNN is allowed (like today we can authenticate per APN).
A UE can access MULTIPLE Slice instances at the same time (these differ for behaviour or other attributes (e.g. service level)
  this is a departure from the eDECOR model where a UE accesses a single DEDICATED core at a time)
There is a RAN part and a Core part of the Network Slice.
In summary: Network slicing allows to model networks as a collection of Network Slice instances that UEs can access according to subscription, capabilities and configuration, using Operator and/or third party credentials.

## Slide 3: From eDECOR to NextGen Network Slicing
The main attributes of eDECOR are:
  Monodimensional and CN oriented only (one CN instance per UE modeling)
  Usage type/DCN-ID convey at the same time in unstructured way SLA and behavioural aspects
    This means that if a UE uses a standard DCN-ID/Usage type identifying a certain behaviour (e.g. massive IOT), the network operator cannot at the same time use this to point to an SLA (e.g. an SLA for the IoT devices belonging to FedEx, or to a certain Security Agency )
The Main attributes of NextGen Network Slicing are:
  Multidimensional and e2e oriented (one UE can access multiple Network Instances at the same time) Multi-tenant (some Network Slice Instances can be tenanted ) and each slice is associated to a specific Service/Usage type
    It follows we need to allow the UE to be subscribed not to a single Usage type , rather to one or more slices it may be able to access
    We may need to indicate which one are the default ones
    We may need to indicate which DNNs out of a subscribed set of DNNs can be associated to a certain slice and also which of these is default DNN when related slice is active.

## Slide 4: Which parameters do we need to make NextGen Network slicing work
eDECOR, due to its scope, just needed a single subscription parameter (usage type) and a single indicator from the UE (DCN-ID) to select the CN the UE needs to be allocated to
For Network Slicing, based on the foundations in slide 2, we need multidimensional subscription and a multidimensional indicator from the UE.
  For the purpose of this way forward we will call them with the same name, and refer to it e.g. as Multidimensional Descriptor (MDD)
  Each dimension of the MDD (which we call MDD Vector – MDDV) logically points to a Network Slice
  Each MDDV is composed of two parts:
    the Tenant ID (which points to the SLA aspect of the slice)
    The Slice Type (which identifies the type slice the UE is going to use, based on a functional Network Slice Template)
      Note: the Tenant ID and Slice type fields values in the MDDV for one slice in the HSS and in the UE are the same in the HPLMN but this may not apply in roaming case. See dedicated slide on roaming aspects.

## Slide 5: MDDV and relation to slice templates and instances
The Slice Type points to a functional template of a slice (i.e. a template that describes the specific deployable Network Functions (i.e. network functions that deliver known feature level behaviour) that are interconnected to deliver a certain Network Instance functional capabilities set. This may have standardized values or Operator specific values.
The Tenant ID points to an SLA definition which includes level of resources assigned to each function in the Slice Type-pointed slice template and/or other policies which may indicate preferential treatment of a slice marked with a certain Tenant ID field versus the others.
  It may have standard default values e.g. to “ignore the field” or other special meanings.
  This may also take regional or global standard values if certain SLAs are understood to be globally applicable for classes of users authorized to use certain slices.
  One of the SLA aspects may be whether the Tenant has dedicated resources or limits to RAN Resources usage, and if so RAN rules need to be provisioned in the RAN nodes for the tenant.
  In this solution we do not enter in the details of who or which organization a tenant can be, but we shall consider this as the party that has an agreement with the operator for an SLA. In a particular case this party is the operator itself who needs some SLA for a subscriber set or Application domain which could use multiple slice types.

## Slide 6: Why do we need a structure in the MDDV?
Example of a structured field already used in 3GPP:
  ARP contains 3 Mandatory IE's: 1. Priority Level 2. Pre-Emption Capability 3. Pre-Emption Vulnerability Priority Level - Range: 0 to 15 0 - Logical Error 1 - Highest Priority 14 - Lowest Priority 15 - No Priority Pre-Emption Capability It has 2 Enumerated Value: 1. shall not trigger pre-emption, - Cannot preempt other bearers during resource crunch 2. may trigger preemption - Can Trigget preemtion of other bearers during resource crunch Pre-Emption Vulnerability It has 2 Enumerated Value: 1. not preemptable - This bearer cannot be pre-emptable by other bearers
  These three independent spaces allow for independent setting of these and also for standardization or customisation of the Priority level independent from the other two fields.
As we have benifeted from structuring ARP, by the same token it is important to allow independence of the resource selection space and the Slice Template Selector spaces.
The Slice Type can therefore be standardised or customised independently of the Tenant ID field.
The Tenant ID can also have operator specific or Standardized values.
A flat or unconstrained MDDV space DOES NOT allow this level of flexibility in service creation and delivery and complicates standardization efforts of its logical components. It also complicates configuration, roaming agreements and inter-PLMN/intervendor Interop.

## Slide 7: Example of why it is easier to use a structured information
Example 1: the operator support 200 SLAs for RAN part of slices and 10 types of slices
  With a structured MDD we can just have 10 config entries for the slice types supported (describing the behaviour for each slice) and the 200 SLA RAN policy configuration.
  With a flat space we need up to 2000 configuration lines if each SLA allows access to all slice types (because we would need to specify the meaning of each of the potential 2000 values including the SLA and type information in a flat manner )
    Result: we have simpler RAN configuration
Example 2: we dedicate a CCNF to a Tenant ID and this tenant can use 10 slices.
  With a structured MDD, as soon as the TENANT ID field in MDD matches the Tenant ID value of the particular tenant the RAN can route to the CCNF. We just need a configuration entry in RAN
  With a flat space for NSSAI, we need 10 entries in the RAN routing table all pointing to the same CCNF
    Result: we have smaller CCNF routing in the RAN
A cell may be dedicated to a Tenant Id and so support ALL Tenant slices
A cell may be dedicated to a certain Slice type and support ALL tenants that use that slice type
RRC can reject RRC ConnectionRequests with a certain Tenant ID or Slice type upon CN request (without separation of tenant ID and slice type the CN may need to send many more values than just a single slice type or tenant ID (e.g. all NSSAI values that point to CNs optimised for a certain kind of slice!)

## Slide 8: Summary of expected UE, RAN and Core behaviours
The UE sends in RRC Connection Requests the MDDVs of the Slices it intends to use at attach time
In subsequent RRC Connection Requests the UE uses MDDVs that the network has returned in attach Accept, TAU accept or as a result as a MM procedure to update the MDDVs set.
  The UE and network can trigger MDD update procedures, see relevant sections in section 6.1.2.
  The MDDV update procedure may trigger a CCNF change but the Operator can have strategies to minimize such changes based on tuning of CCNF selection and reselection policies.
The NAS signalling is routed based on Temp ID in RRC if it is available
If Temp ID is not available in RRC :
  If Tenant ID is shared across all MDDVs then a Tenant ID only based routing rule may apply for a small set of Tenants that may need a dedicated CCNF right away without rerouting from a default CCNF.
  Otherwise, routing rules may apply to route NAS signalling to CCNFs that optimally support certain Combinations of Slice Types.
  If the RAN cannot determine a match between the MDDVs provided by the UE and a dedicated CCNF, the RAN applies default routing to a default CCNF
The CCNF selected by the RAN may reassign the UE to a more optimal CCNF according to an operator policy
NAS signalling includes the MDDV(s) of the Slices it is addressing
  The CCNF forwards NAS signalling to the Slice specific functions based on the MDDV in the NAS message. The MDDV in the NAS message also allows to isolate any procedure which was slice specific from other slices.

## Slide 9: eDECOR compatibility
For UEs that can be constrained to access a single slice at a time we could define a compatibility profile with eDECOR where the Tenant ID field is set to a well know value identifying eDECOR compatibility mode and therefore the network and subscription only consider the Slice Type field (which in this case is the only field used by the RAN to route the NAS signalling to the Core network )

## Slide 10: Roaming
In roaming case if there is no roaming agreement specific for slicing with the HPLMN, the UE may use standardised MDDVs, or
The VPLMN assigns the UE MDDV values that are PLMN specific with a precise mapping to MDDV values in the Home (in that case the UE also needs to be aware of which MDDV-H value maps to which MDDV-V). This means there needs to be a roaming agreement for slicing . UE needs to be aware of the mapping of MDDV-V to MDDV-H by configuration or by explicit mapping info when the MDDV-V is assigned by the VPLMN to the UE, or
The VPLMN has no agreement specific for slicing with HPLMN and no standardised MDDV applies: the UE is placed in default inbound roaming slice. The HPLMN CP and UP nodes are just selected based on DNN (replica of the current HPLMN routed case).

## Slide 11: Procedures
Use those documented in 6.1.2 but to be refined in normative phase
  Temp ID CN selection stands if UE provides it
  MDD based routing otherwise applies in the RAN
  Attach, TAU, SM procedures will be defined in other Key issues also so we will need to have a single design and take slicing into account
  MM and SM are separate but SM can be piggybacked on MM
  SM messages indicate the MDDVs they relate to.
Addition/removal of slices again could be based on the procedures in 6.1.2 but refined in normative phase
  We would like to allow independence of MM and SM procedures and we consider the change of slices set that are active for a UE to trigger a MM transaction. Any related SM event is either piggybacked or done separately.
  MDD can also change upon TAU (slice is supported on a per TA granularity at least).

## Slide 12: RAN part of Network Slicing
It is in scope of RAN but at least we have to be sure RRC ConnectionRequest can carry the MDDVs in use by the UE so the applicable RAN part of slices will be activated
The CCNF may need to pass to the RAN over NG2 the Information about what slices are activated for the UE and thus confirm the UE is authorized to access these.
Examples of use cases (just FYI):
  Local RAN configuration can e.g. limit the amount of resources a slice uses to e.g. 30% of the RAN node capacity (and this is enforce also at RRC connection establishment time)
  A certain slice is allocated a minimum amount of resources and this is enforced at RRC connection establishment layer at congestion time.
  A cell may be dedicated to e.g. a Tenant’s slices or a slice type or even a single slice.
  The RAN executes overload control procedures per Tenant ID or slice type or both based on CN trigger so it rejects RRC connection requests

## Slide 13: Non 3GPP support
There is dependency on the Non 3GPP support so we should keep this open for now

## Slide 14: Summary
Move forward with Option B type of solution in rel-15 (Group C is subsumed by Group B)
Agree we need to support simultaneous access to >1 Slices per UE
Agree that we want to address the aspects of tenancy/SLA and behaviour based differentiation, so we need an MDDV
Agree that we do need to allow for standardised and non standardized MDDVs
Agree that D+C may mean a structured MDDVs
Agree MM, AU, NSI selector at least are in the CCNF
Selection and change of CCNF is strictly under operator control
Agree that PLMN access, slice access, DNN access may require independent authentication&authorization.
Routing in RAN of NAS signalling can be based on Temp ID or MDD. Default routing of NAS signalling applies if no specific policy is matched in RAN.
RAN and CN part of network slice are supported (for RAN slicing to work the RRC layer needs to convey the MDD)
Slice specific functions instance selection based on MDDV and other information in the CCNF
Addition/removal of MDDVs and related network slices should be supported
Roaming support may be based on roaming agreements for slicing or based on standardized MDDV only – default behaviour is no slice applies in roaming other than an inbound roamer slice.
Non 3GPP support dependent on Non 3GPP support solution for Rel-15. The text here above is expected to apply to 3GPP RAN only for RAN-specific aspects.
Any Further Optimisations with regard to the slicing solution should be discussed in Normative phase

## Slide 15
Thanks