## Slide 1: Discussion on interconnection of IMS emergency sessions over II-NNI
TSG SA WG2 Meeting#118 NTT

## Slide 2: 1. Background
IMS emergency session request
Originating IMS network
P-CSCF
E-CSCF
LRF
IBCF
BGCF/
MGCF
For the future interconnection scenario, an emergency session request may be routed to a PSAP via IBCF through IMS or non-IMS network.
However, the interconnection of IMS emergency sessions over II-NNI/Mm interface has not taken into account in TS 23.167/TS 23.228.
Originating UE
PSTN
IMS network
Non-IMS network
Interconnection of IMS emergency sessions over II-NNI/Mn has not taken into account in TS 23.167/TS 23.228.
II-NNI
PSAP
Mm

## Slide 3: 2. Proposal
IMS network
(responsible for routing emergency requests)
It is proposed to enhance the functionalities at E-CSCF/IBCF to support the interconnection of IMS emergency sessions over II-NNI/Mm.
  An originating IMS network which does not have any direct path to the PSAPs forwards an emergency session request to other IMS network which is responsible for routing the requests to PSAPs.
II-NNI
IBCF
E-CSCF
LRF
IBCF
BGCF/ MGCF
Receives the request from an IBCF.
If the request has the routing information, the E-CSCF skips the query procedure, otherwise queries LRF to retrieve routing information.
Interconnection of emergency sessions between the IMS networks is allowed.
Originating IMS network
P-CSCF
E-CSCF
LRF
IBCF
Originating UE
PSAP
IMS Emergency session request (with routing information)
IMS Emergency session request (without routing information)
Routes the request via IBCF to IP multimedia network/IMS network.
BGCF/
MGCF