## Slide 1: Asymmetric QoS : Extending Reflective QoS scheme to support Asymmetric QoS
Jicheol Lee
2016. 11. 08
Samsung Electronics

## Slide 2: Table of Contents
Motivation
Understanding Reflective QoS (RQ)
Proposal: Extending RQ for Asymmetric QoS
Example Scenarios:
1) Person Live Broadcast, 2) Over-The-Top Video
5. Solution evaluation
6. Proposed Interim Agreement

## Slide 3: Motivation
Various OTT applications have different traffic characteristics.
  For example, person live broadcasting application requires high uplink data rate and low latency while less downlink data rate requirement.
  Conversely, the OTT HTTP video streaming service requires high downlink data rate while requiring low uplink data rate.
Operator may want to have different QoS treatment for uplink and downlink due to the different traffic characteristics.
  For example, operator may want to limit maximum bit rate or prioritize downlink traffic for the OTT video service, but not to the uplink.
  Or operator may want to limit maximum bit rate or prioritize the uplink traffic for the personal live broadcasting uplink traffic but not for the downlink traffic.
Reflective QoS is useful because we can install the uplink packet filter without control plane signaling.
  However, the usage of Reflective QoS is limited because it only apply the same QoS for uplink and downlink traffic which are usually different traffic characteristics and different QoS requirements.
It is proposed to extend Reflective QoS to support the asymmetric QoS which have different QoS requirements on uplink and downlink traffic with the same user plane marking value.
Notes: Various OTT applications have different traffic characteristics.
  예를 들어 Real-time (실시간 개인방송) 는 많은 양의 uplink bandwidth 를 요구하고 실시간으로 접속해야하는 delay 가 중요함.
  많은 양을 차지하는 Video Traffic 은 downlink 양이 필요하다.
  Web 의 경우, uplink/downlink 모두 delay budget 이 적을 수로 RTT 를 줄일수가 있다. Uplink/downlink 모두 적을 delay 를 요구하고, 경우에 따라서 downlink 는 많은 양의 밴드위드를 요구할 수 있다.
OTT application 사용을 위하여 고안된 Reflective QoS의 경우 동일한 QoS 를 지칭하게 되면, 이러한 목적을 달성 할 수 없다.
그래서, asymmetric QoS 를 제안한다.
본 제안에서는 하나의 QoS Flow ID (NG3 marking value)가 uplink 와 downlink 의 QOS 요구사항이 상이한 QoS profile 을 지칭할 수 있도록 한다.

## Slide 4: Understanding Reflective QoS (1/2)
Understanding how Reflective QoS works based on Interim agreement
  A default and pre-authorized QoS Rule(s) are provisioned during PDU session establishment
  Assuming the AS layer forward NG3 marking value (let’s call it “QoS-Flow-ID”) to the NAS layer when receiving downlink packet
Figure 1. Example UE operation of Reflective QoS
Notes: Observation
  Reflective QoS는 단말에 별도의 signaling 없이 UE 의 uplink packet filter 를 설치 할 수 있다는 장점이 있다.
  그런데, 동일한 QoS 를 적용해야한다.
  이러한 QoS 가 적용되어야할 traffic 은 OTT traffic 인데, 이러한 OTT application 들은 uplink/downlink traffic 특성(characteristics) 이 다르다. 사업자들을 이들을 위하여 다른 QoS 를 요구할 수 있다.
    예를 들어서, 사업자는 모든 OTT video traffic 을 일정한 rate 이상 제한하지만, uplink 에는 이러한 제한을 두고 싶지 않을 수 있다.
    또한, 실시간 개인 방송 (personal live broadcasting) 의 경우 특정 밴드위드를 보장하던지 혹은 너무 많은 트래픽 발생을 막기 위하여 MBR 을 적용하거나, 보다 높은 우선순위를 적용 혹은 PDB 적게하여 실시간성을 높게 하거나 할 수 있다.
  또한, 단말의 application 이 요구하여 OTT application 이 보다 높은 QOS 를 적용받고 싶어 할 수 있는데, 역시 uplink/downlink QoS 가 다를 수 있다.
In this solution, QoS-Flow-ID is used as a marking value and an identifier of the A-Type or B-Type QoS profile to identify the same QoS Flow over UE and the UP.
During the PDU session establishment, one or more QoS-Flow-ID(s) is installed as NAS-filter(s) together with QoS Rule, in the UE and CN_UP. The QoS Rule includes an indicator whether Reflective QoS is applied for the QoS Flow.
A QoS-Flow-ID may have an uplink QoS profile and/or a downlink QoS profile where an uplink and downlink QoS profile might have different QoS characteristics.
A QoS profile can be standardized QoS profile (Type-A) or dynamic QoS profile (Type-B) and its QoS parameters as described in the bullet 3c, 11 and 12 of the interim agreement on QoS framework (see section 8.2 of this TR).
After the network decides to apply the reflective QoS, the network marks the downlink packet with QoS-Flow-ID. The AS layer of the UE receives the packet and sends the pair of received QoS-Flow-ID and the packet to the NAS layer. The NAS layer checks that QoS-Flow-ID was installed for the Reflective QoS. If the QoS Flow should be applied, it derives the packet filter (n-tuple) from the received packet and installs the newly derived packet filter to the table of QoS Rule.

## Slide 5: Understanding Reflective QoS (2/2)
QoS Rule
  QoS Rule consists of packet filter (n-tuple), NAS-level QoS Profile and precedence order
  NAS-level QoS Profile can be Type-A (Standardized) QoS or Type-B (Dynamic) QoS.
  NG3 marking value refers the NAS-level QoS profile.
  Note that whether Reflective QoS is applied for QoS Flow may be signaled or indicated from AS layer.
Precedence order | Packet Filter (n-tuple) | Marking value (QoS-Flow-ID) | NAS-level QoS Profile | Reflective QoS[1]
1 | (1.1.1.1,2,2,2,2,TCP, *,80) (1.1.1.1,2,2,2,2,TCP, *,443) | 2 | B-Type, QoS (A,B,C) | NO
2 | (1.1.1.1,*,*,*,*) | 3 | A-Type QoS Profile = X | NO
3 | (1.1.1.1,*,*,*,*) | 1 | A-Type QoS Profile = Y | YES
4 | (10.10.0.1,*,*,*,*) | 4 | A-Type QoS Profile = X | NO
5 | (10.10.0.1,*,*,*,*) | 5 | A-Type QoS Profile = Z | NO
[1] Note that whether Reflective QoS is applied for QoS Flow may be signaled during PDU session establishment for the QoS Flow, or it may be indicated from the AS layer per each IP flow. |  |  |  | 

## Slide 6: Proposal – Asymmetric QoS
Let’s extend the NAS-level QoS profile to have UL and DL NAS-level QoS profile to support asymmetric QoS (green row)
Support the asymmetric QoS by deriving a new packet filter as used in the same way as reflective QoS.
Only one addition is to allow the one QoS-Flow-ID value to have two different QoS characteristics for the uplink and downlink QoS flow respectively.
For the asymmetric QoS, QoS Rule(s) is provision to the UE, AN and CN_UP from CN_CP
  UE is provisioned with precedence order, n-tuple packet filter, marking value, NAS-level QoS Profile (UL)
  AN is provisioned with marking value, NAS-level QoS Profile for UL and DL
  CN_UP is provisioned with precedence order, n-tuple packet filter, marking value, NAS-level QoS Profile (DL)
Precedence order | Packet Filter (n-tuple) | Marking value (QoS-Flow-ID) | NAS-level QoS Profile (Uplink) | NAS-level QoS Profile (Downlink) | Reflective QoS
1 | (1.1.1.1,2,2,2,2,TCP, *,80) (1.1.1.1,2,2,2,2,TCP, *,443) | 2 | B-Type QoS (A,B,C) | B-Type QoS (A,B,C) | NO
2 | (1.1.1.1,*,*,*,*) | 3 | A-Type QoS Profile = X | A-Type QoS Profile = X | NO
3 | (1.1.1.1,*,*,*,*) | 1 | A-Type QoS Profile = Y2 | A-Type QoS Profile = Y1 | YES
4 | (10.10.0.1,*,*,*,*) | 4 | A-Type QoS Profile = X | A-Type QoS Profile = X | NO
5 | (10.10.0.1,*,*,*,*) | 5 | A-Type QoS Profile = Z | A-Type QoS Profile = X | NO
Notes: 본 제안에서는 asymmetric 한 uplink/downlink QOS 를 가지는 application 을 위하여 Reflective QoS 에서 동적으로 packet filter 를 생성하는 방법을 사용하여, QoS Flow-ID (marking value) 를 통하여 서로 다른 uplink 와 downlink 를 지정할 수 있는 방안을 제안한다.

## Slide 7: Example: Personal Live Broadcasting (UL Reflective QoS)
Assumptions
  Mobile Operator A have a contract on the uplink differentiation service with the OTT service provider (Personal Live Broadcasting Service).
  Since the OTT service provider uses the CDN technologies, the IP addresses of the server changes. The OTT service provider does not inform the Mobile Operator A of the exact list of the IP address to the Mobile Operator A beforehand.
  The Mobile Operator A’s UP function can detect the OTT service provider’s traffic to be differentiated.
Procedures
Step 1. During PDU session establishment, the CN-CP function install the pre-authorized QoS rule including packet filter (derived from Reflective QoS), QoS-Flow-ID and QoS Profile to the CN-UP.
Step 2. User starts the Personal Live Broadcasting (PLB) Application and generate uplink traffic for the service.
Step 3. The operator’s UP function detects the PLB application traffic.
Step 4. UP function marks the downlink traffic for the corresponding uplink traffic to be differentiated for the given QoS-Flow-ID.
Step 5. RAN binds QoS Flows onto access-specific resources based on the NG3 marking/tunnel information and the corresponding QoS characteristics provided during PDU session establishment.
Step 6. When UE receives the downlink packet marked with the QoS-Flow-ID, it installs the derived packet filter.
Step 7. When the UE’s PLB application sends the uplink packet, the UE matches the packet to the packet filter derived in Step 6 and marks the QoS-Flow-ID for the uplink traffic.
Step 8. RAN performs differential QoS treatment for the PLB application uplink traffic.
Notes: 가정
  이동통신 사업자는 OTT A (실시간 개인방송) Personal Live Broadcast 사업자와 협약을 맺는다.
  이동통신 사업자는 실시간 개인 방송 traffic 을 UP function 에서 detection 할 수 있다고 가정한다.
절차
  PDU session 생성 시에, Pre-authorized QoS rule은 다음을 포함한다. CP 는 UE 에 NAS-filter rule 로 다음을 전송한다.
    Packet filter (derived from Reflective QoS), QoS-Flow-ID, UL QoS Profile
  사용자는 PLB Application 을 실행하고 UE application 은 개인방송 서비스를 시작한다.
  사업자의 UP function 은 PLB application 을 detection 하고 DL link 로 QoS-Flow-ID 를 marking 하여 내려 준다.
  UE NAS-filter 에서 packet을 받아서, packet filter rule 을 갱신한다.
  UE application 에서 내려오는 uplink traffic 을 filter 에서 찾고, QoS-Flow-ID marking 한하여 AS 로 내보낸다.
  AS 에서 적절한 DRB mapping 하여 차별화된 QoS 를 제공한다.

## Slide 8: Example: OTT Video Streaming – DL Reflective QoS
Assumptions
  The user subscribed the premium service to the operator for use UE’s differential OTT video treatment.
  UE is configured to apply special QoS for the OTT video application.
Procedures
Step 1. During the PDU session establishment, the pre-authorized QoS rule includes high level packet filter which can derive the n-tuple packet filter, QoS-Flow-ID, QoS Profile.
Step 2. The user starts the OTT video application.
Step 3. The UE marks the uplink traffic with the QoS-Flow-ID for the OTT video application.
Step 4. RAN determines the NG3 QoS marking, selects the NG3 tunnel and forward the NG3 marked packet to the UP
Step 5. The UP applies Reflective QoS to derive the DL packet filter from the uplink packet and install the derived n-tuple packet filter for DL traffic.
Step 6. When the downlink traffic comes to the UP function, the UP function marks the QoS-Flow-ID and forward the packet to the AN marked with NG3 tunnel.
Step 7. RAN applies QoS treatment according to the QoS-Flow-ID in the downlink packet.
Notes: Assumption
  OTT video application 을 실행한다.
  Premium user is subscribed to the operator to use UE’s differentiation QoS service.
  단말에서 OTT video application 은 특정 QoS 로 설정하도록 한다.
Procedures
  PDU session 생성 시에, Pre-authorized QoS rule은 다음을 포함한다. CP 는 UE 에 NAS-filter rule 로 다음을 전송한다.
    Packet filter (derived from Reflective QoS), QoS-Flow-ID, UL QoS Profile
  단말의 OTT video application 을 실행하면, 단말에서 차별화된 DL 서비스를 원하는 uplink traffic 에 pre-authorized QOS 를 사용한다.
  QoS-Flow-ID 가 붙은 uplink traffic 은 RAN 을 거쳐 UP 에 도착한다.
  UP 에서는 Refelective QoS 를 적용한다. 즉, DL traffic filter 를 갱신 한다.
  서버로 부터 다운링크 패킷이 도착할때, QoS-Flow-ID 를 tagging 한다.
  RAN 에서 video packet 에 대하여 우선순위를 높여서 처리한다.

## Slide 9: Solution evaluation
This solution is an extension of the Reflective QoS mechanism to support asymmetric QoS. This solution does not require any additional signalling.
Notes: 본 제안에서는 asymmetric 한 uplink/downlink QOS 를 가지는 application 을 위하여 Reflective QoS 에서 동적으로 packet filter 를 생성하는 방법을 사용하여, QoS Flow-ID (marking value) 를 통하여 서로 다른 uplink 와 downlink 를 지정할 수 있는 방안을 제안한다.

## Slide 10: Proposed Interim agreement
17. An identifier for the QoS Flow (which is also used as NG3 marking value) indicates either an uplink QoS profile, downlink QoS profile or both where the uplink and the downlink QoS profile have different QoS characteristics.

## Slide 11: [FYI] Interim agreement of Reflective QoS [TS23.799]
1a. Support Reflective QoS over RAN under control of the network.
  The network decides on the QoS to apply on the DL traffic and the UE reflects the DL QoS to the associated UL traffic.
  When the UE receives a DL packet for which reflective QoS should be applied, the UE creates a new derived QoS rule.
  The packet filter in the derived QoS rule is derived from the (i.e. the header of the) DL packet.
  For traffic that is subject to Reflective QoS the UL packet gets the same QoS treatment as the reflected DL packet.
  It shall be possible to apply Reflective QoS and non-reflective QoS on the same PDU session.
1b Reflective QoS can be used for non-GBR service data flows.

## Slide 12: [FYI] Reflective QoS in Fixed Broadband Access [TS23.139 6.3.3]
Some clarifications to the function of reflective QoS in the UE (this describes only the logical function for the reflective QoS marking, the implementation might be differently):
  For each incoming downlink IP packet the UE checks if a DSCP marking rule for the n-tuple of this IP packet exists. If the rule does not exist, then a new marking rule is added. Otherwise, the DSCP value and the time stamp for this marking rule are set.
  The uplink n-tuple in each marking rule is made from the downlink n-tuple of that rule by swapping address (and port) destination and source.
  For each outgoing IP packet the UE checks if a marking rule for this IP packet exists. If the n-tuple of the packet matches the uplink n-tuple of a marking rule, then the DSCP value of the packet is set to the DSCP value of that marking rule. The time stamp for that rule is set.
  For tunnelled scenarios, the n-tuples correspond to the n-tuples of the inner header of the packet. In all scenarios, the DSCP value of the marking rule is the DSCP value of the outer header of the packet. This in both downlink and uplink direction.
  A marking rule is removed when a certain period of time has passed since the time stamp.
  The function of reflective QoS will overwrite DSCP markings set by the UE application.