## Slide 1: Interworking between NGC and EPC
NTT DOCOMO
working draft

## Slide 2: Assumptions for the slide-set
UE supports both S1 mode (EPC NAS procedures) and N1 mode (NGC NAS procedures)

## Slide 3: Purpose: Answer questions for interworking in S2-170590 (SA2-118AH). Propose principle level agreements
Does the UE need to advertise its “single registration” and ”dual registration” capabilities to the network
  Shall the UE always support “single registration” capability?
Does the network need to advertise NGx is supported or not?
  Is the advertisement PLMN-wide or only registration-area wide only?
How is the final mode of operation selected between UE and network? What are the procedures followed.

## Slide 4: “Single Registration” Mode UE
In single-registration mode, UE has only one active MM state machine and is either in N1 mode or in S1 mode (when connected to 5GC or EPC, respectively). Similarly, the network keeps only one active MM state machine that is synchronised with the MM state machine in the UE and is located in either the AMF or in the MME. UE maintains one common registration for EMM and NMM indicating whether the UE is registered for packet services or not.
5G Radio
4G Radio
EMM
ESM
NMM
NSM
1. EMM and NMM states are synchronized.
2. EMM/ESM and NMM/NSM contexts are mapped at mobility.
2. Only one of these contexts are active at any time
Only one of the radios are active at any time
Contexts and State machine
Inactive
Active
UE

## Slide 5: “Dual Registration” Mode
In dual-registration mode, UE can handle independent MM state machines: one MM state machine in N1 mode (i.e. for UE’s connection to 5GC) and one MM state machine in S1 mode (i.e. for UE’s connection to EPC). In this mode, the UE may be registered to 5GC only or EPC only or to both.
5G Radio
4G Radio
EMM
ESM
1, EMM/ESM and NMM/NSM states are un-coordinated and non-synchronized.
2, Both contexts or single context maybe active at any time
Both or single radios maybe active at any time
Contexts and State machine
NMM
NSM
Inactive
Active
UE

## Slide 6: What is required by network to support dual-registration?
Dual-registration may exist for
  Short duration, eg. UE performs “handover attach” in target CN and then moves all PDN connections to the target network.
  Long duration, eg. UE is able to keep PDN connectivity to both EPC and 5GC (eg. use of LTE/eLTE or dual-radio capability of UE.
If the network supports simultaneous-registration of MME and AMF, then it can support dual-registration.
  NOTE: In EPC simultaneous registration of S4-SGSN and MME is supported.
HSS/AuC
5G Radio
4G Radio
MME
AMF/SMF
EMM
ESM
EMM
ESM
1, EMM/ESM and NMM/NSM states are un-coordinated and non-synchronized.
2, Both contexts maybe active at any time
Both MME and AMF are registered for the UE.
Both radios maybe active at any time
Contexts and State machine
PGW/TUPF
SGW
UPF
User Plane
Context maybe active towards both CNs.
NMM
NSM
NMM
NSM
Inactive
Active
UE
Control Plane

## Slide 7: SHALL Network always provide support for dual-registration mode?
    NOTE/MOTIVATION: The support for these dual-registration feature is not necessarily required for networks supporting NGx. However, the support of such features can enable the deployment of 5G NR Standalone without NGx at > 6 GHz (non-LTE frequencies) and UE operating in dual-radio, dual-registration mode and able to simultaneously do data transfer via both 5G NR and LTE.
Proposal 2: The network SHALL provide support for “dual registration” mode:
  It shall be possible for both AMF and MME to be simultaneously registered at the HSS/UDM for the UE.
  Paging for SMS, eg via SGs, can be done in sequential order, eg first in last registered RAT and then in the previous RAT.

## Slide 8: Should network advertise non-support of NGx to UE? or
How does Single registration UE handle network w/o Nx support?

## Slide 9: UE modes and Network mode interactions: Starting Assumptions
Assumptions:
  UE does not advertise its support of dual or single-registration to network
  Network does not advertise its support of NGx to UE
(x-Network support y- UE capability) | w NGx | w/o NGx
Single Registration only | OK Connected Mode: HO or release-w-redirection Idle Mode: TAU. | (Q1) Session Deleted. Connected Mode: RRC release with optional redirection followed by UE doing idle mode behavior Idle Mode: TAU with mapped GUTI-> TAU failure (no Context found). UE goes to EMM-DEREGISTERED and deletes all SM context.
Dual Registration only | (Q3) IGNORE for now. | IGNORE for now.

## Slide 10: Problem of single-registration UE in network with no Nx support
As MME is unable to get the UE context from AMF (even if it is able to determine the UE identity from old GUTI), the network sends TAU Reject(Cause=UE Identity cannot be derived in the network). The UE will enter EMM-DEREGISTERED and deletes all context information.
UE
AMF
MME
SGW
PGW/TUPF
UE registered in 5GC.
UE goes idle, Selects EPC
TAU Request(mapped 5G-GUTI, old GUTI)
TAU Reject (no context)
Attach Request(mapped GUTI, old 4G-GUTI, HO flag)
Identity Request (IMSI)
Identity Response (IMSI)
Attach Accept()
Network does not advertise “No NGx support”
UE deletes all MM/SM Context

## Slide 11: Possible Solutions
Network at attach tells UE not to operate in “single registration” mode.
  UE operates in “dual registration” mode and performs Handover-attach.
Single-registration UE performs handover-attach and sessions are handed over like in non-3GPP to 3GPP HO.
  NOTE: Solutions 1 and 2 are the same.
EPC supports ”modified TAU” procedure for these UEs.
  Huawei proposal (approximately): MME supports a modified TAU procedure. On receiving TAU with mapped GUTI, the MME knows from mapped GUTI that UE is last registered on 5GC. The MME gets PGW address from HSS and moves over all PDN connections to EPC.
    How does the MME figure out the APNs to move over to EPC. Is the APN list also in HSS. Is it all the APNs?

## Slide 12: Solution 1 or 2
Analysis:
  Same behavior as if UE is in “dual-registration” mode w/o having registered in EPC.
    If UE already has a valid registration in EPC, the UE will perform a TAU followed by moving PDN connections over to EPC.
UE
AMF
MME
SGW
PGW/TUPF
UE registered in 5GC.
UE goes idle, Selects EPC
Attach Request(mapped GUTI, old 4G-GUTI, HO flag)
Identity Request (IMSI req)
Identity Response (IMSI)
Attach Accept()
Network advertises “No NGx support”, or
Network tells UE to operate in “Dual Registration Mode”

## Slide 13: Proposal 3
Analysis:
Solution 1 or 2 require no changes to EPC core.
Solution 3 requires MME to support a new TAU procedure just for interworking with 5GC.
Solution 2 is ”cleaner” for the UE stack => UE is operating in dual-registration mode.
PROPOSAL 3:
UE tells network in NAS during attach its support for “single registration” or “dual registration”.
If network does not support Nx, during attach to PLMN the network informs the UE in NAS to operate in “dual registration” mode.
If UE does not support dual registration mode, UE will perform TAU with mapped GUTI which will result in TAU reject. UE will enter EMM-DEREGISTERED state and delete UE all context and perform attach.

## Slide 14: With Proposal 3
Assumption:
  UE advertises its support of dual or single-registration in NAS to network at attach in either EPC or NGC.
  If network does not support Nx, during attach network tells UE to operate in “dual registration” mode.
(x-Network support y- UE capability) | w NGx | w/o NGx
Single Registration only | OK Connected Mode: HO or release-w-redirection Idle Mode: TAU. | (Q1) If UE does not support single registration mode, sessions are deleted at HO. If UE supports dual registration mode, operation as below
Dual Registration only | (Q3) IGNORE for now. | IGNORE for now.

## Slide 15: Interaction of ”Dual Registration” only UE with Network

## Slide 16: UE modes and Network mode interactions: Assumption set from Proposal 3
Assumption:
  UE advertises its support of dual or single-registration in NAS to network at attach in either EPC or NGC.
  If network does not support Nx, during attach network tells UE to operate in “dual registration” mode.
(x-Network support y- UE capability) | w NGx | w/o NGx
Single Registration only | OK Connected Mode: HO or release-w-redirection Idle Mode: TAU. | (Q1) If UE does not support dual registration mode, sessions are deleted at HO. If UE supports dual registration mode, operation as below
Dual Registration only | (Q3) See next slide | OK Connected Mode: No HO. RRC Release or release w redirection. UE follows idle mdoe. Idle Mode: Handover attach w native ID.

## Slide 17: Mismatch Quadrant 3: UE support dual-registration only, Network supports NGx
At NSM bearer setup, network does not provide mapped ESM context since network knows UE operating in “dual registration” mode.
Idle-mode mobility: OK
  If UE is already registered in EPC: UE will perform an TAU with native 4G GUTI. then do “UE requested PDN connection w handover flag” to move desired PDN connections over to EPC.
  If UE is not registered in EPC: UE performs handover attach and moves desired PDN connections to EPC.
Connected-mode: OK
  RAN will ask UE to make measurements and report. Assume DR UE supports this.
    A DR UE which does not want network to redirect may not support E-UTRAN measurement reporting in NG-RRC.
  RAN decides to RRC release-w-redirect.
    If DR UE does not support E-UTRAN measurement reporting, the network will just perform RRC release at network edge.
  No HO is performed either due to (a) CN providing ”assistance information” to RAN that UE is DR, or (b) UE does not provide support for HO in RRC UE-Radio Capability. However, since UE’s Radio capability is a static capability and UE may decide to operate in “single registration” or “dual registration” mode, it is best for the CN to provide assistance information to RAN stating that UE is operating in dual registration mode and RAN will not attempt HO for the UE.

## Slide 18: Proposal 5: Overall interworking procedures
Assumptions:
  UE advertises its support of dual or single-registration in NAS to network at attach in either EPC or NGC.
  If network does not support Nx, during attach network tells UE to operate in “dual registration” mode.
    CN provides assistance information to RAN stating that UE is operating in dual registration mode and RAN will not attempt HO for the UE.
(x-Network support y- UE capability) | w NGx | w/o NGx
Single Registration only | OK Connected Mode: HO or release-w-redirection Idle Mode: TAU. | (Q1) If UE does not support dual registration mode, sessions are deleted at HO. If UE supports dual registration mode, operation as below
Dual Registration only | (Q3) Connected Mode: None. RRC Release Idle Mode: Handover attach or TAU based on UE’s EMM/NMM Registration State | OK Connected Mode: No HO. RRC Release or release w redirection. UE follows idle mdoe. Idle Mode: Handover attach w native ID.

## Slide 19: Overall Procedure
UE when it attaches to NGC, states whether it supports “single registration” mode or ”dual registration” mode in NAS message.
  This exchange can occur in any registration (attach, TAU) and the response should be valid PLMN wide or until next update by network.
The AMF based on whether it supports Nx, selects which mode to use. If no Nx then no support of single registration. AMF specifies mode to the UE in NAS reply. The selected mode is applicable PLMN wide and valid until network changes this in subsequent update (should not occur often).
Single registration Mode
  Describe both UE and network behavior
Dual Registration Mode
  Describe both UE and network behavior.

## Slide 20: Backup
Will be removed before final submission

## Slide 21: What does support of “single registration” imply.
What does single-registration require?
  Ability to map security context between 5GC and EPC
    5G-GUTI to GUTI mapping. Security context mapping.
  Ability to map between NSM and ESM contexts
    Mapping provided by the network
  EMM-NMM registration machine coordination.
  Support for “gap based” IRAT measurements and reporting to RAN for IRAT mobility (handover or release with redirection).
  NOTE: Support for HO procedure is optional in UE
    This can be part of radio capability. If UE and network supports HO, HO is performed otherwise RAN performs RRC Release with redirection. Signaled as part of “feature group indicators” in RRC.
    UEs that support voice shall also support HO.

## Slide 22: Should support/no-support of Nx be PLMN wide (only in attach) or TA-basis (in each TAU)?
The support of Nx provided on TA-basis can only provide Nx connectivity to neigbhouring MMEs. The UE in idle-mode can go via a tunnel and appear in a totally different geographical area, i.e MME service area which does not have Nx connectivity to the source AMF. The serving MME may not have Nx with the source AMF. The UE will perform TAU, which will fail even though the source AMF provided indication that Nx is supported.
Proposal: Support/no-support of Nx should be PLMN wide.
  NOTE: We do not believe indication of support of Nx is needed to be provided to UE.
NOT NEEDED