## Slide 1: Discussion for QoS target fulfillment observability
Huawei

## Slide 2
Regarding 5G QoS target fulfillment observability
To Huawei understanding, the ongoing SID eVoLP has very a close link to 5G QoS discussion triggered by S2-170138 and therefore we propose to take VoLTE as example to see:
  how QoS target fulfillment observability is achieved in 4G
  whether 4G QoS target fulfillment observability is good enough
  If not, how to enhance QoS target fulfillment observability in 5G(also in 4G?)

## Slide 3
4G QoS target fulfillment observability for VoLTE by eNB
Operator first perform field test for VoLTE to get curves of RSRP vs MOS Score and then configure the according RSRP(per codec) in eNB as HO threshold.
One can see 4G eNB is mainly based on RSRP to observe QoS target fulfillment observability for voice due to that
  Service quality for voice is usually measured by MOS and MOS is directly mapped to RSRP via i.e. observing voice QoS target fulfillment is equal to observe a dedicated UE’s RSRP.
  Per S2-165666 , eNB is configured -110 dBm and -115dBm for AMR fitting/EVS fitting with MOS Score 3.8

## Slide 4
4G QoS target fulfillment observability for VoLTE by eNB(Cont)
For Rel-14 RobVoLTE, eNB will reject QCI=1 bearer request to force the UE to perform CSFB if the RSRP for the UE is lower than VoLTE HO threshold(which is statically configured in eNB)
However, it looks beneficial eNB notify AF/PCRF, allowing AF/PCRF to either adapt to lower QoS requirements (e.g. using EVS rather AMR with transcending) or to end the service.
Please note the notification mechanism for the ongoing voice session is very similar
b)Expected solution
a) Legacy
solution

## Slide 5
Open discussion for averaging window size - how it works
Huawei see a need for well defined QoS target definitions and are open to averaging widow size but need some further clarification how averaging window size works
Assuming averaging widow size is defined, eNB has the following parameters:
  Bit Rate
  Packet delay and Loss requirement
  averaging widow size
Please note we still take VoLTE as a example:
  Case A: If the mobile originating VoLTE user is speaking and the peer side is listening, then there are many uplink packets while a few downlink packets from the mobile originating user.
  Case B: if the subscriber mute himself/herself, there are only few silence frame and very few uplink packet:
  Question:
    how to measure Bit Rate and Packet Delay/Loss for uplink and downlink with fixed window size?
    eNB may have to measure Bit Rate and Packet Delay/Loss in short time e.g. 500ms for VoLTE, the eNB performance is FFS?

## Slide 6
Open discussion for averaging window size – how to get it
Based on field test, one can get HO threshold for VoLTE i.e. the curves for RSRP vs MOS Score has to be ONLY based on field test
HO threshold for VoLTE is dynamically changed per codec and different codec has different RSRP( e.g. EVS preforms better in weak coverage compared to AMR)
Back to averaging windows size, it seems one still has to rely on field test to get it , which is also dynamically changed per codec(similar to HO threshold for VoLTE).
However, even with averaging windows size, eNB still have to derive the HO threshold from averaging widows size together with Packet Loss and bit rate, which seems not that direct.

## Slide 7
Huawei view on 5G QoS target fulfillment observability
Huawei share the view that observability of target fulfillment is difficult and therefore see a need for well defined QoS target definitions that could used by eNB directly
Huawei prefer service coverage compared to APP coverage as APP usually have multiple services and each service has its own coverage e.g. VoLTE/ViLTE coverage.
For VoLTE, one can see we have to rely on field test to rate the user experience, which is not simply related to Bit Rate and Packet Delay/Loss and widow size. Therefore, further discussion is needed about how to enhance QoS framework.

## Slide 8
Open discussion for way forward
How to observe QoS target fulfillment is a common issue for both 4G/5G and therefore it is proposed to support this feature for both 4G and 5G. However it looks more discussion is needed to have a full view
It looks VoLTE is very good example to get a full picture and it seems beneficial to take into account the discussion outcome of eVoLP especially considering that
  objective part of eVoLP clearly indicates
    the solutions should be flexible enough to apply to any other service that has dedicated radio coverage requirement
    Depending on the investigation outcome, SA4/RAN WGs(as appropriate) needs to be consulted to ensure and evaluate the performance applicability and any solutions implications on RAN area
  The key issue about how to identify the information needed by RAN to make optimized HO decision and how to provide RAN with this information has been agreed in eVoLP
  The key issue about RAN information sending to EPC/IMS for VoLTE to allow application level to have possible optimizations is proposed by CMCC per S2-171032 this meeting.