## Slide 1: Discussion on Reflective QoS Deactivation (User Plane approach)
3GPP SA WG 2 Meeting#121
15 – 19 May, Hangzhou, China
Source: LG Electronics, SK Telecom, ETRI, InterDigital
Title: Discussion on Reflective QoS deactivation
Document for: Discussion
Agenda Item: 6.5.5 QoS concept and functionality
Work Item / Release: 5GS_Ph1 / Rel-15
S2-173386
LG Electronics, SK Telecom, ETRI, InterDigital

## Slide 2: Reflective QoS Activation
PDU
SMF
UE
UPF
data
RQI
=1
QFI
Start policing to corresponding packets
Generate Derived QoS Rule
data
RQI
=1
QFI
Reflective QoS Configuration
(User Plane)
Reflective QoS Configuration
(Control Plane)

## Slide 3: Reflective QoS Deactivation
Solution 1 – Timer based solution
Start / Reset Timer whenever indicating RQI=1
Set RQI=0 if SMF configured UPF to stop using RQ
Continuously monitors RQI and
start / reset Timer whenever receiving RQI=1
Deactivated when Timer is expired
Remove Derived QoS rule associated with the Timer
Deactivated when Timer is expired
Stop policing to corresponding UL packets
PDU
SMF
UE
UPF
data
RQI
=1
QFI
data
RQI
=1
QFI
Reflective QoS Configuration
(Deactivation)
PDU session establishment accept or pre-configured
Timer value
NOTE: Timer in the network is optional
FFS whether Timer is reset when sending corresponding UL packets

## Slide 4: Reflective QoS Deactivation
Solution 2 – RQI based solution
  Need dummy packet when there is no DL packet
PDU
SMF
UE
UPF
Reflective QoS Configuration
(Deactivation)
Set RQI=0 if SMF configured UPF to stop using RQ
Continuously monitors RQI
Deactivated when packets with RQI=0 received
Remove Derived QoS rule
Deactivated when SMF configured
Stop policing to corresponding UL packets
data
RQI
=0
QFI
data
RQI
=0
QFI

## Slide 5: Reflective QoS Deactivation
Solution 3 – Deactivate RQI (DRQI) based solution
  Need dummy packet when there is no DL packet
SMF
UE
UPF
Reflective QoS Configuration
(Deactivation)
Indicate DRQI=1 if SMF configured UPF to stop using RQ
Continuously monitors RQI / DRQI
Deactivated when packets with DRQI=1 received
Remove Derived QoS rule
Deactivated when SMF configured
Stop policing to corresponding UL packets
PDU
data
DRQI
=1
QFI
data
DRQI
=1
QFI

## Slide 6: Reflective QoS Deactivation
Solution 4 – Timer + RQI based solution
  No dummy packets to deactivate RQI
Deactivated when either
- Timer is expired
- packets with RQI=0 is received
Remove Derived QoS rule and Timer
Deactivated when either
- Timer is expired
- When SMF configured to stop using RQ
Remove Timer and stop policing to corresponding UL packets
PDU
SMF
UE
UPF
Reflective QoS Configuration
(Deactivation)
Continuously monitors RQI and
start / reset Timer whenever receiving RQI=1
NOTE: Timer in the network is optional
FFS whether Timer is reset when sending corresponding UL packets
PDU session establishment accept or pre-configured
Timer value
Start / Reset Timer whenever indicating RQI=1
Set RQI=0 if SMF configured UPF to stop using RQ
data
RQI
=0
QFI
data
RQI
=0
QFI

## Slide 7: Pros and Cons
 | Solution 1 Timer | Solution 2 RQI | Solution 3 DRQI | Solution 4 Timer + RQI
Pros | No signalling overhead (e.g. No dummy packet, No additional indication over RAN) Workable under the congestion RQI does not need to be set in every DL packet | Immediate deactivation No additional resource for deactivation | Immediate deactivation No additional resource for deactivation RQI does not need to be set in every DL packet | No signalling overhead (e.g. No dummy packet, No additional indication over RAN) Workable under the congestion Immediate deactivation when there is DL packets
Cons | Resources to maintain timer No support of immediate deactivation No tight rule synchronization between UE and network if network does not running timer | Need dummy packet when there is no DL packets UE needs to check whether Derived QoS rule exist whenever packet without RQI is received RQI should be set in every DL packet | Need dummy packet when there is no DL packets RAN impact, e.g. additional indication needs to be transferred over RAN | Resources to maintain timer No tight rule synchronization between UE and network if network does not running timer RQI should be set in every DL packet