## Slide 1: Provision of UE Usage Type to RAN to assist RAN resource prioritisation between user groups
Source: Vodafone
SA WG2 Meeting #121 15 - 19 May 2017,Hangzhou, P. R. China
Agenda item: 7.1
Tdoc S2-173516

## Slide 2: Different Usage Groups can share RAN
eMTC
eMBB
Public Safety users
VPLMN subscribers
VPLMN Operator Group roamers
Out of Operator Group roamers
But how to control the sharing of RAN capacity between these groups?
E.g. how to:
prohibit “out of operator group eMTC devices” from more than 5% of eNB capacity
Prioritise (absoultely) 25% of RAN capacity for Public Safety Users, but allow other users to use that capacity when PS users don’t need it.

## Slide 3: Problem
No current tools available to solve this.
Current QoS information is ‘abstract’ and relates primarily to that UE
RAN does know the ‘group’ of the UE
RAN does not have visibility of the IMSI
RFSP/SPID parameter is intended for control of idle mode behaviour – not connected mode - and its coding is not great for extensibility.
Proposed Solution
Send the “UE Usage Type” to the RAN at RRC Connection Establishment. Changes needed:
  store “UE Usage Type” in MME
  send in all S1 connection establishment signalling procedures
  send from source to target eNB in X2 handover.

## Slide 4: Proposal
Agree to draft TEI-15 CRs for this functionality.