## Slide 1: Provision of UE Usage Type to RAN to assist RAN resource prioritisation between user groups
Source: Vodafone
SA WG2 Meeting #121 15 - 19 May 2017,Hangzhou, P. R. China
Agenda item: 7.1
Tdoc S2-173830
Rev S2-173516

## Slide 2: Different Usage Groups can share RAN
eMTC
eMBB
Public Safety users
VPLMN subscribers
VPLMN Operator Group roamers
Out of Operator Group roamers
As indicated in the WID, RP-151827 “RAN Aspects of RAN Sharing Enhancements for LTE”, existing eNBs are able to share load between the sharing PLMNs’ customers (“Sharing is normally based on agreed quota or share ratio.“)
But how to control the sharing of RAN capacity between groups of users in non-network-sharing cases?
E.g. how to:
prohibit “out of operator group eMTC devices” from more than 5% of eNB capacity
Prioritise (absolutely) 25% of RAN capacity for Public Safety Users, but allow other users to use that capacity when PS users don’t need it.

## Slide 3: Problem
No current tools available to solve this.
Current QoS information is ‘abstract’ and relates primarily to that UE
RAN does know the ‘group’ of the UE
RAN does not have visibility of the IMSI
RFSP/SPID parameter is intended for control of idle mode behaviour – not connected mode - and its coding is not great for extensibility.
Access Class Barring only applies to idle mode and Access Classeses are randomly allocated to devices – so all ‘groups’ are likely to have an equal proportion of devices in each Access Class.
“Low Access Priority” does not help as LAPI devices should not be rejected if their group’s load is within the eNB’s quota for that group.
Proposed Solution
Choose either the “DECOR UE Usage Type” or “eDECOR DCN ID” and send it to the RAN at RRC Connection Establishment/S1 Handover. Changes needed:
  store “UE Usage Type” /DCN ID in MME (after MME policing/modification of the information received from the HSS)
  send in all S1 connection establishment signalling procedures (e.g. as a new field within CN Assistance Information)
  send from source to target eNB in X2 handover.

## Slide 4: Proposal
Agree to draft TEI-15 CRs for this functionality.