## Slide 1: Policy Framework Annex
Ericsson
S2-175434

## Slide 2: Distribution of the Policy Framework in 23.501 Annex into 23.203, 23.501 and 23.502 (1)
Criteria followed:
  Describe the Policy Framework features in only one TS
    Reason is that there may be dependencies between each feature in this release (e.g. event reporting) or in future releases that may be more complex to describe when distributed.
  Reduce the description of the Policy Framework so that normative text is not duplicated.
  Policy Framework may evolve with 5G specific functionality so that an Annex in 23.203 is not feasible.

## Slide 3: Distribution of the Policy Framework in 23.501 Annex into 23.203, 23.501 and 23.502 (2)
The full context of Annex A is moved to 23.203 new clause in the main body.
The Policy Framework Requirements moved to 23.203
The Policy Framework Architecture moved to 23.203.
The Policy Framework Features:
  Common for PCC and Policy Framework are described in 23.203.
  Policy Framework specific are described in 23.501.
PCC Rules, AMC information, UE Policies, Policy PDU session information, event triggers are described in 23.203.
5G procedures in 23.502 are updated with Policy Framework specific information.

## Slide 4: Distribution of the High level Policy requirements and Policy Reference Architecture of Annex Policy Framework into 23.203 and 23.501 (1)
Annex in 23.501N/A. | New clause 23.203 | 23.501
A.1-High level Policy requirements | X (full description) Reference to PCC for common Policy and PCC requirements. 5G Policy requirements explicitly listed | N/A.
A.2-Policy Reference architecture | X (full description) | Reference to 23.203.
A.2.2-SBA Policy interfaces and Reference points | X (Policy specifics) Reference to 23.501 for those present in 5G reference architecture. Full description of Policy specifics (e.g. Nwda or OCS interfaces) | X (not Policy specifics) N25 added

## Slide 5: Distribution of the High level Policy requirements and Policy Reference Architecture of Annex Policy Framework into 23.203 and 23.501 (2)
Annex in 23.501 | New clause 23.203 | 23.501
A.3.1.3.1-Distribution of the Policy Enforcement in SMF and UPF | X (full description) under Policy Reference Architecture. This is to show at high level the PCEF distribution in 5GS. | UPF descriptions include Policy enforcement.
A.3.1.2-Distribution of enforcement of Policy Decisions. | N/A | X (full description). This is to show policy enforcement in 5GS

## Slide 6: Distribution of the Policy Framework 5G Features described in 23.501 Annex into 23.203 and 23.501
Annex in 23.501 | New clause 23.203 | 23.501
A.3.1.6 UE Access and Mobility Management Control | X (Description of PCF to AMF info sent) AMC rule and operation | X (Complete Feature) Feature description including PCF to AMF to UE interaction to provide AMC Rules.
A.3.1.8 UE Policy | X (Description of PCF to AMF info. sent) USRP | X (Complete Feature) Feature description including PCF to AMF to UE interaction to provide URSP
A.3.1.11 Traffic Steering Control Information | X (Description of PCF to SM info. sent) PCC Rule extensions to provide traffic steering control for 5G | X (Complete Feature) Feature description for AF influence in traffic routing incudes traffic steering control information

## Slide 7: Distribution of the common Policy Framework and PCC Features in 23.501 Annex into 23.203, 23.501
Annex in 23.501 | New clause 23.203 | 23.501
A.3.1.1 Existing Policy Features, QoS, charging, Usage Monitoring, background traffic handling | X (Full description) Reference to description of PCC feature | SM, QoS, include a reference to 23.203.
A.3.1.13 Session binding | X (Full description) Reference to description of PCC feature | N/A
A.3.1.15 Event triggers | X (Full description) Reference to description of PCC feature | N/A
A.3.1.9 Policy Control Subscription information management | X (Full description) Reference to description of PCC feature | N/A

## Slide 8: Distribution of the PCC Rules, AMC control information, UE Policies in Annex Policy Framework into 23.203 and 23.501
Annex in 23.501 | New clause 23.203 | 23.501
A.3.1.3-Policy and charging control (PCC Rules + PDN session info) | X (PCC Rule/PDN info) PCC Rules and PDN session in 5G context described | X (PCC Rules used in Session Manag.) AF influence in traffic routing includes a reference to 23.203 for PCC Rule. SMF behavior when PCC Rule with traffic routing is received.
A.3.1.6 Access and Mobility control (AMC Rules) | X (AMC Rule) AMC Rules and operations described. | X (AMC Rules used in Mobility Manag.) Management of Service Restrictions include a reference to AMC rule. AMF behavior when AMC rule is received.
A.3.1.3 URSP | X (URSP) USRP Context described | X (URSP used in 5G features) AMF behavior when URSP is received.

## Slide 9: Distribution of the NFs description in Annex Policy Framework into 23.203 and 23.501
Annex in 23.501 | New clause 23.203 | 23.501
A.3.1.4-Policy and charging control enforcement | X (Included in the SMF) | X (SMF includes a reference to 23.203 for Policy and charging control enforcement)
A.3.1.5 Access and Mobility control enforcement | X (Included in the AMF) | X (AMF includes a reference to 23.203 for AMC enforcement)
A.3.1.10 NWDAF | X (full NF description) | N/A
A.3.1.8 Description of PCF NF including roaming Description of AF NF | X (full NF description) | X (Reference to 23.203)

## Slide 10: Distribution of the Policy Framework Procedures of Annex Policy Framework into 23.203 and 23.502
Annex in 23.501 | New clause 23.203 | 23.502
A.4 UE Context Procedures | Policy Framework procedures for UE Context are in 23.502 | (De-)Registration procedures include transfer of AMC Rules from PCF to AMF and then to RAN and UE. Generic UE configuration procedures include transfer of URSP Policies from PCF to AMF and then to the UE