## Slide 1
SA WG2 Meeting #S2-122-BIS
August 21 – 25, 2017, Sophia Antipolis, France
S2-175461
Source: NEC
Title: Typical use case to enable minimum time interval for Continuous Location Reporting
Document for: Information
Agenda Item: 6.11
Work Item / Release: NAPS / Rel15

## Slide 2: Usecase1: Semi-realtime car location monitor
  Application plots a lot of car locations on display screens.
  Application refreshes display screens per certain interval, e.g. 60 sec.
App server
App clients
Cars
60
sec
This use case needs the continuous location reporting to plot exact car locations, but it does not require two or more reportings for each car during a refresh interval of display screens.
PROPOSAL: To reduce unnecessary signaling for this kind of use cases, we propose to enable minimum time interval for Continuous Location Reporting. (Proposed CR: S2-175460)

## Slide 3: Usecase 2: Cargo/parcel tracking
Source: 3GPP TR 22.888 - Study on enhancements for Machine-Type Communications (MTC), Release 11
Note that this contain both checkpoint and regular reporting usecase.
Time

## Slide 4: Location Tracking MTC Feature 4.4.1 Use-Case: Checkpoint Reporting (TR 22.888)
Courier services may attach communication tags on customer's parcels/cargoes to track the current location of the items.
While on a transport, it is generally not necessary to get accurate location information of each item.
There will be pre-determined locations (i.e. checkpoints) where the tags should report their locations to the MTC Server.
This checkpoint reporting will enable the courier service company to provide real-time tracking updates to their customer on the delivery status of the cargoes/parcels.
Also, the MTC Server would like to know when the parcels/cargoes arrive in a switching centre, so that possible transfers of parcels/cargoes to achieve the most efficient/speedy delivery can be determined.
When the network operator provides the service of tracking the MTC Devices, it removes the need for communication tags to contain GPS units, making it an attractive solution to MTC Customers.

## Slide 5: Location Tracking MTC Feature:Cargo Tracking (TR 22.888)
Courier services may attach communication tags on customer's parcels/cargoes to track the current the location of the cargoes.
While transporting, many such cargos may be placed in the same container truck.
The courier service company may utilize third-party transport companies such that the cargoes on a single truck may be from different courier services.
In addition, in order to optimize transport schedule, a cargo may switch between different container trucks before reaching its final destination.
These make it necessary for each customer's cargo to be attached with a separate communication tag.
These communication tags are then MTC Devices that will be co-located throughout the duration of the transport. This use case demonstrates the scenario of MTC Devices being co-located temporarily (but may be for a long time).

## Slide 6: Required features for cargo/parcel tracking
Can be very large number of MTC (M2M/IoT tags) devices to be tracked.
It is continuous monitoring but accurate location (GPS) is not generally required (cell-level is acceptable).
Regular reporting of location is important to ensure parcels/cargo reach the destination on schedule/time and safely.
Typical life-span of cargo delivery can be hours, days or weeks.
Usually a rough route taken by the goods is enough to investigate any problem with the delivery.
If there is delivery issue of any parcel/cargo, there is ability to find the last reported location and turn on the more accurate location tracking.
IoT/M2M tags based methods conserve battery and ability configure during their service.
In these scenarios, final goal is parcels/cargo reaching their final destination on agreed timeline/schedule. Neither the log of route nor the accurate location every time is important.

## Slide 7: Location Monitoring parameters
Monitoring event
  Maximum Number of Reports - sets maximum number of reports
  Monitoring Duration – Sets the maximum duration of monitoring
  Group Reporting Guard Time – aggregates the messages (applicable at HSS and SCEF)
Location Monitoring
  Location Type – last known or current location
  Accuracy (optional) – specify the granularity of location reporting
Current specification lacks a parameter that specify reporting of events only at set duration, MME level for individual UE/devices for location reporting.
  Reduce unnecessary signalling/messages at MME and subsequently in interface S6t, T6a/T6b and T8

## Slide 8: Summary and Next steps
Identified real-life usecases that can benefit from having (event driven but) set duration location reporting – as per application requirements
  Any additional location information is not required for the success of application execution.
  Parcel/cargo tracking service can list location of parcel at set times for the benefit of the sender/receiver.
  Cell-level location accuracy with regular reporting optimises required number of reporting versus full-scale event driven location reporting.
When network operator provides the service of tracking the MTC Devices (IoT/M2M tags), it removes the need for these devices to contain GPS units, configurable and conserve battery.
Current specification lacks a parameter that specify reporting of events only at set duration, MME level for individual UE/devices for location reporting.
  Reduce unnecessary signalling/messages at MME and subsequently in interfaces S6t, T6a/T6b and T8
This points to a need for new parameter within the Location Monitoring in TS 23.682 MONTE.
CR S2-175460 implements this parameter – Minimum monitoring Interval