## Slide 1: Provision of UE Usage Type/DCN-ID to RAN to assist RAN resource prioritisation between user groups
Source: Vodafone
SA WG2 Meeting #122bis 21-25 August, Sophia Antipolis, France
Agenda item: 7.1
Tdoc S2-175948
Rev S2-173830 (updates in blue)

## Slide 2: Different Usage Groups can share RAN
eMTC
eMBB
Public Safety users
PLMN’s own subscribers
MVNO subscribers with same MNC/MCC as PLMN’s own subscribers
Inbound roamers from VPLMN’s Operator Group
Out of Operator Group inbound roamers
As indicated in the WID, RP-151827 “RAN Aspects of RAN Sharing Enhancements for LTE”, existing eNBs are able to share load between the sharing PLMNs’ customers (“Sharing is normally based on agreed quota or share ratio.“) In a non-shared PLMN, or a PLMN with few sharing partners, this eNB functionality can be re-purposed to service different Usage Groups.
But how to control the sharing of RAN capacity between groups of users in non-network-sharing cases?
E.g. how to:
prohibit “out of operator group eMTC devices” from getting more than 5% of eNB capacity
Prioritise (absolutely) 25% of RAN capacity for Public Safety Users, but allow other users to use that capacity when PS users don’t need it.
Provide MVNO subscribers with an agreed level of service for that MVNO (that may be different to the service level of the HPLMN)

## Slide 3: Problem
No current tools available to solve this.
Current QoS information is ‘abstract’ and relates primarily to that UE
RAN does know the ‘group’ of the UE
RAN does not have visibility of the IMSI
RFSP/SPID parameter is intended for control of idle mode behavior – not connected mode - and its coding is not great for extensibility.
Access Class Barring only applies to idle mode and Access Classes are randomly allocated to devices – so all ‘groups’ are likely to have an equal proportion of devices in each Access Class.
“Low Access Priority” does not help as LAPI devices should not be rejected if their group’s load is within the eNB’s quota for that group.

## Slide 4: Proposed Solution
Choose either the “DECOR UE Usage Type” or “eDECOR DCN-ID” and send it to the RAN at RRC Connection Establishment/S1 Handover.
UE Usage Type vs DCN-ID
    As “UE Usage Type” is already stored in MME but DCN-ID is not, need to store DCN ID in MME if choice is to use DCN-ID
  For inter-CN node handover, UE Usage type is already sent from source to target CN node, but DCN-ID is not sent. However, eDECOR capable target CN node has the capability to map from UE Usage Type to DCN-ID, and, different CN nodes might have different mappings.
  eDECOR enabled eNB has configuration for DCN-ID, but that would typically be for one DCN-ID to one set of MMEs. If DCN-ID is extended for this task, multiple DCN-IDs would typically point to the same set of MMEs.
  RAN re-routing functionality requires RAN to have UE Usage Type configuration
  UE Usage Type tends to be provided by the HPLMN and might be re-mapped by the VPLMN. DCN-ID is always derived in the VPLMN. The RAN is part of the VPLMN, so DCN-ID might be more consistent.
  DCN-ID is [16 bits] long while UE Usage Type is [8 bits] long.
  Existing eNB implementations likely to be able to support “6 usage groups” (as they may support 6 sharing PLMNs), so the need for > 8 bits for “RAN resource group” is low.
 very little difference between UE Usage Type and DCN-ID
Changes needed:
  send in all S1 connection establishment signalling procedures (during Attach, in Service Request, in Handover Request) e.g. as a new field within the (S1-AP and X2-AP) Expected UE Behaviour IE that is part of the CN Assistance Information
  send from source to target eNB in X2 handover.
  If DCN-ID is used, at inter-CN handover, target MME maps UE Usage Type to local DCN-ID

## Slide 5: Proposals
a) Agree to draft TEI-15 CRs for this functionality.
b) Identify any other differences between DCN-ID and UE Usage Type and decide which to use.