## Slide 1
Slicing drafting SA2#123
Tdoc S2-177888
Agenda Item: 6.5.1
Tdoc for Information

## Slide 2: UE<>NW Information Exchange for Slicing
[NW>UE] Configured NSSAI - Per PLMN with PLMN specific values S-NSSAIs (Optional)
  h-S-NSSAIs for HPLMN (Mandatory)
  v-S-NSSAIs for other PLMNs (Optional)
[NW>UE] NSSP - defined by HPLMN (Optional)
  One or more h-S-NSSAIs ( Configured NSSAI) each with {APP ID}
[UE>NW] Requested NSSAI (Conditional i.e. if Configured / Allowed NSSAI available)
  One or more h-S-NSSAIs (non-roaming); or
  One or more v-S-NSSAIs (roaming)
   Allowed NSSAI if available, or if not, Configured NSSAI. NO Rejected S-NSSAI
[NW>UE] Allowed NSSAI
  One or more h-S-NSSAIs (non-roaming) or v-S-NSSAIs (roaming),
  Per serving PLMN /and RA (set by serving PLMN and permanently stored)
  (Optional, roaming only) Mapping of v-S-NSSAIs in a PLMN to h-S-NSSAIs in HPLMN
[NW>UE] Rejected S-NSSAIs
  One or more h-S-NSSAIs (non-roaming) or v-S-NSSAIs (roaming)

## Slide 3: How does the UE obtain information it needs to operate slicing
Configuration by HPLMN (for Configured NSSAI and NSSP) and/or
Registration Accept, if the UE sends no Requested NSSAI or a Requested NSSAI that cannot be fully accepted by the AMF and/or
UE configuration update from Serving PLMN

## Slide 4: Registration accept content
If the UE included a Requested NSSAI that is fully accepted
  Allowed NSSAI and, for the roaming case, mapping to corresponding h-S-NSSAIs values.
If the UE included no Requested NSSAI (i.e. it has no configured or allowed NSSAI for serving PLMN) :
  Allowed NSSAI and for the roaming case, mapping to h-S-NSSAIs. The Allowed NSSAI is comprised only of the Default S-NSSAIs that are supported in the RA
  other S-NSSAIs that the UE can use in the PLMN. Temporarily rejected S-NSSAIs are included in the list also. This list and the Allowed NSSAI are stored in the Configured NSSAI for the UE for the PLMN
  NSSP (the UE receives NSSP from the AMF in the Registration Accept (FFS if retrieved from PCF or from UDM, see EN in 23.503, clause A.3.1.8.1) OR the HPLMN is assumed to configure
If the UE included a Requested NSSAI that is not fully accepted by AMF :
  The Allowed NSSAI and, for the roaming case, mapping to corresponding HPLMN h-S-NSSAIs.
    The Allowed NSSAI is comprised of A subset of the S-NSSAIs from requested NSSAI based on operator policy.
  other S-NSSAIs that the UE can use in the PLMN. Temporarily rejected S-NSSAIs are included in the list also. This list is updating the Configured NSSAI for the UE for the PLMN
  The Rejected S-NSSAIs from the Requested NSSAI with any rejection condition.
ONLY applicable in the UE if the UE already has a Configured NSSAI with h-S-NSSAIs

## Slide 5: UE Configuration update
At any time the AMF may provide the UE with a new list of S-NSSAIs the UE can use in the PLMN alongside their mapping to the respective S-NSSAI values in the H-PLMN. This result to changes in the Configured NSSAI for the PLMN.
If the HPLMN is performing the configuration update, this will result in changes to NSSP and Configured NSSAI in HPLMN. The HPLMN and only the HPLMN may also update Configuration for other PLMNs using the Configuration Update method.

## Slide 6: What does the UE include in SM
The DNN
The S-NSSAIs values of the applicable serving PLMN and HPLMN slice based on the mapping information.

## Slide 7: What does the UE include in Registration request
If available, a Requested NSSAI with VPLMN values, as per current spec.

## Slide 8: Which function provides the mapping of S-NSSAIs
AMF or AMF assisted by NSSF.