## Slide 1
Slicing drafting SA2#123
Tdoc S2-177888
Agenda Item: 6.5.1
Tdoc for Information

## Slide 2: UE<>NW Information Exchange for Slicing
[NW>UE] Configured NSSAI : S-NSSAIs per PLMN with values that are valid for the PLMN (Optional)
  HPLMN : S-NSSAIs which match all the subscribed S-NSSAIs (unless it is outdated – but this is error case trigger)
  OTHER PLMN: S-NSSAIs valid for other PLMNs and Mapping to S-NSSAIs in HPLMN Configured NSSAI
[NW>UE] NSSP : defined by HPLMN (Conditional – i.e. not there if Configured NSSAI is not there and also it is not needed if only one slice is configured for the UE)
  Maps APP IDs to S-NSSAIs in the Configured NSSAI for the HPLMN
[UE>NW] Requested NSSAI: (Conditional i.e. if Configured / Allowed NSSAI available)
  As defined in the TS
[NW>UE] Allowed NSSAI
  One or more S-NSSAI of the serving PLMN as described in the TS
  It may include Mapping of Allowed NSSAI S-NSSAIs to Configured NSSAI S-NSSAIs
[NW>UE] Rejected S-NSSAIs
  See paper S2-177890

## Slide 3: How does the UE obtain information it needs to operate slicing
Configuration
Registration
UE configuration update by AMF

## Slide 4: During Registration
If the UE included in Registrations Request no Requested NSSAI (i.e. it has no configured or allowed NSSAI for serving PLMN) :
  Allowed NSSAI and, for the roaming case, mapping to corresponding HPLMN S-NSSAIs.
  This may trigger the UE to be also provided if applicable with a with Configured NSSAI for the Serving PLMN and, if needed, NSSP
If the UE included in Registrations Request a Requested NSSAI that is fully accepted in a Registration Accept:
  Allowed NSSAI and, if needed, mapping to corresponding S-NSSAIs values in the Configured NSSAI of the HPLMN.
If the UE included in Registrations Request a Requested NSSAI that is not fully accepted by AMF in a Registration Accept:
  The Allowed NSSAI and, for the roaming case, mapping to corresponding HPLMN S-NSSAIs.
  This may trigger the UE to be also provided if applicable with a with Configured NSSAI for the Serving PLMN and, if needed, NSSP.
  The Rejected S-NSSAIs from the Requested NSSAI with any rejection condition (see paper S2-177890)

## Slide 5: UE Configuration update
At any time the AMF may provide the UE with a new list of S-NSSAIs the UE can use in the PLMN alongside their mapping to the respective S-NSSAI values in the H-PLMN. This results to changes in the Configured NSSAI for the PLMN.
If the HPLMN is performing the configuration update, this will result in updates to Configured NSSAI in HPLMN.
NSSP Update may be triggered at the same time if necessary.

## Slide 6: What does the UE include in SM
The DNN
The S-NSSAIs values of the applicable serving PLMN and HPLMN slice based on the mapping information in Allowed NSSAI.

## Slide 7: What does the UE include in Registration request
If available, a Requested NSSAI with serving PLMN values, as per current spec.

## Slide 8: Which function provides the mapping of S-NSSAIs
AMF or AMF as directed by the NSSF.