## Slide 1: 6.8 ATSSS
Key Issue Update on Traffic Switching (23.793 v0.1.0)

## Slide 2: There is basic support for traffic steering / switching in Rel-15
  In Rel-15:
    UE is responsible for establishing new PDU Session(s) and maintaining on-going PDU session(s)
    UE uses UE Route Selection Policy (URSP) to determine which access is used to deliver traffic over. URSP is delivered to UE by the PCF (via the AMF over N1) when UE first registers with 3GPP network (23.503 section 6.6.1.2 & 6.6.2)
    URSP rules may be overridden by user preferences (23.503 section 6.1.2.2.1)
    URSP rules may also be preconfigured in the UE. Rules delivered by the PCF take precedence

## Slide 3: URSP provides basic Steering capability
URSP provides a basic Steering capability for a new PDU Session
A URSP rule will be selected based on a match to a Traffic descriptor (23.503 section 6.6.2) which identifies the application targeted by the rule
Rules are prioritised in case traffic matches multiple rules
The access that should be used to deliver the traffic is specified by the Access Type Preference (23.503 table 6.6.2-2) and indicates the preferred access on PDU Session establishment – this a steering capability. The Access Type has coarse granularity – one of 3GPP or non-3GPP
URSP does not provide a mechanism to steer traffic at a finer access type granularity for a given access type technology, e.g. 5GNR, 4G, mmW, etc in the case of 3GPP access

## Slide 4: URSP provides basic Switching capability
URSP provides a basic Switching mechanism for an existing PDU session:
  When preferred access defined by Access Type preference becomes unavailable, application traffic may be switched to the alternative access
  Possible outcome
    UE can request the network to handover the PDU session from current (unavailable) access to other (standby) access by indicating “Existing PDU session” RequestType in PDU session establishment message
    Coupled with SSC mode 1, session continuity can be maintained across access types:
      23.501 S5.6.9.2.1: “the UPF acting as PDU Session Anchor at the establishment of the PDU Session is maintained regardless of the access technology (e.g. Access Type and cells) a UE is successively using to access the network…. SSC mode 1 may apply to any PDU Session type and to any access type.”
Besides this basic mechanism, URSP does not include further policy to UE to perform switching
Therefore there is a need to enhance this basic switching mechanism to consider
  Traffic performance and/or AN related measurements in the UE
  UE to make switching decision based on traffic switching assistance information
  An example of this would be UE is able to handover PDU session from WiFi to outdoor/indoor radio coverage in areas where WiFi coverage is bad

## Slide 5: Update of Key Issues on Switching
How does a UE (including RG/CPE) perform traffic performance and AN related measurements in the preferred access network and/or alternative access network in order to make switching decision?
What parameters can be used as traffic switching assistance information in the UE (including RG/CPE) to make switching decision? Such traffic switching assistance information can be pre-configured in the UE or provided by the network.