## Slide 1: Access and Congestion Control
Discussion
v10

## Slide 2: Access Control
TS 22.261 obsoletes TS 22.011 for Access Control - In unified access control, each access attempt is categorized into one or more of the Access Identities and one of the Access Categories.
Access Identity Number | UE Configuration
0 | Not configured
1 | Multimedia Priority Service
2 | Mission Critical Service
3-10 | Reserved for future use
11 | Access Class 11
12 | Access Class 12
13 | Access Class 13
14 | Access Class 14
15 | Access Class 15
Access Category Number | Conditions related to the UE | Type of access attempt
0 | All | MO signaling resulting from paging
1 | UE is configured for delay tolerant service | All except for Emergency
2 | All | Emergency
3 | All except Access Category 1 | MO signalling resulting from other than paging
4 | All except Access Category 1 | MMTEL voice
5 | All except Access Category 1 | MMTEL video
6 | All except Access Category 1 | SMS
7 | All except Access Category 1 | MO data that do not belong to any other Access Categories
8-31 |  | Reserved standardized Access Categories
32-63 | All | Based on operator classification

## Slide 3: Congestion Control
Reject NAS messages except:
  Response to paging
  Signaling with ‘higher priority’ than was used when the back-off timer was received
General NAS level congestion control
  Reject all NAS messages except:
    Deregistration
    High priority access (Access Identity Number 11-15)
    Emergency services
    Mobile terminated services
DNN based congestion control
  Reject NAS-SM messages to a specific DNN or empty (not provided) DNN except:
    High priority access (Access Identity Number 11-15)
    Emergency services
    PDU Release Request
S-NSSAI based congestion control
  Reject NAS messages associated with an S-NSSAI and optionally a DNN except:
    High priority access (Access Identity Number 11-15)
    Emergency services

## Slide 4: Issues and options
Signaling with ‘higher priority’ implies order which is currently missing
  Access Identity (AI 3 means higher than MPS and MCS)
  Access Category (no ordering)
  Establishment cause (no ordering)
Network permission to use higher priority (other access identity) is necessary
Non-3GPP access
Options:
  Change ‘higher priority’ to ‘high priority access’ as those access classes are already mapped to Access Identities in TS 22.261
  Introduce more granular congestion control with multiple signaling priorities possibly based on a mapping to Access Identities and Categories