## Slide 1: Key Open Issues of LADN Principles
Drafted based on the discussion during LADN Drafting Session

## Slide 2: Does LADN support roaming case?
Some companies didn’t want to make such limitation.
No decision was made.

## Slide 3: AMF assisting NAS SM message rejection
Proposal #1: Sony, NEC proposed that AMF include indication in the N11 message from AMF to SMF during PDU Session Establish procedure if it knows the UE presence in a LADN service area is OUT.
  Supporting companies: 3
  Objecting companies: 2
Proposal #2: Huawei proposed that AMF reject the NAS SM request message if it knows the UE presence in a LADN service area is OUT.
  Supporting companies: 2
  Objecting companies: 4
As a less optimum solution has been supported in 23.502, do we need to continue the discussion on optimized solution for NAS SM message rejection? This question was not asked yet, can we have a drafting show of hands and move on with majority preference?
Conclusion:

## Slide 4: How does UE know whether a DNN is LADN DNN?
Two solutions on table:
  Solution #1: AMF indicates to UE over NAS message by reusing LADN information, but this has dependency on how AMF knows this information.
  Solution #2: PCF sends indication along with each LADN DNN to UE using URSP.
Current situation: It seems each solution has its Pros and Cons, some companies asked to postpone the decision.
But whether AMF needs to know whether a DNN is LADN DNN has dependency on the chosen solution for UE.
Can we have a drafting show of hands between the above two solutions to move on with majority preference?
Conclusion:

## Slide 5: How does AMF knows whether a DNN is LADN DNN?
Option #1: Configuration in some AMFs of the PLMN
  Per online discussion, this is always needed as some AMFs has to be configured to know the LADN information.
Option #2: AMF knows that from UDM as part of User subscription
  Huawei stated this option has dependency on how UE knows whether a DNN is LADN DNN.
  But in 23.501, it says “When the UE performs a successful (Re)registration procedure, the AMF may provide to the UE, based on local configuration information (e.g. via OAM) about LADN Information, UE location, UE subscription information received from the UDM about DNNs that is subscribed as LADN, the LADN Information for the LADNs available to the UE in that RA in the Registration Accept message. ”
  From above description, it seems Option #2 has been supported.
This can be revisited and decided once agreement is made on how UE knows whether a DNN is LADN DNN.
Conclusion:

## Slide 6: How does SMF know whether a DNN is LADN DNN?
Option #1: SMF knows from UDM as part of User subscription
  This is the current work assumption for 5GS but not explicitly addressed yet, clarification in 23.501 and 23.502 is needed.
Option #2: Configuration in SMF
  Not discussed yet.
Can we move on with option #1 to clarify the missing description in 23.501 and 23.502?
Conclusion: