## Slide 1: Slicing interworking principles
Drafting session outcome

## Slide 2: Connected mode mobility from EPC to 5GC (with N26): Selection of appropriate AMF
Background: “Registration with AMF re-allocation” that 23.501 (clause 6.3.5) refers to applies to Idle mode only and may not clean up resources on initially selected AMF (see E// paper in S2-180106)
Options
  Re-select AMF after completion of handover: Introduce a new procedure to support AMF change in Connected mode
  During handover preparation: AMF to fetch S-NSSAIs from H-SMFs, re-select to appropriate AMF based on S-NSSAIs received from H-SMFs
  During handover preparation: Send handover container with S-NSSAIs (MME->AMF) to enable AMF to select appropriate target AMF (during handover preparation)
  Do nothing: AMF selected by MME assumed to support S-NSSAIs of UE’s PDU sessions
    Note: In case we go with this option, it becomes questionable why we need to ensure to select a specific AMF in the Idle mode case.
Way forward: Do nothing (AMF selected by MME assumed to support S-NSSAIs of UE’s PDU sessions)

## Slide 3: Idle mode mobility from EPC to 5GC (with N26): How to enable binding between EPS bearer contexts received via N26 and PDU session IDs?
Background
  AMF receives EPS bearer contexts from MME including PGW-C address and bearer ID (EBI)
  How to correlate EPS bearer contexts with PDU session ID (and potentially S-NSSAIs received from UE)?
Options
  AMF sends EBI to SMF to learn PDU session ID (and S-NSSAI) from SMF (ZTE paper in 637), aligns with Connected mode behavior
    Note: This option implies that AMF can only select default V-SMFs (as AMF does not know which S-NSSAI to use for which EBI)
  UE to send EBI together with PDU Session ID in Registration Request to AMF to enable AMF to bind
  Correlation of PDU session IDs via UDM (Docomo paper in 733)
Discussion results
  Some companies prefer to go with Option (2), referring to potential relation with Rel-16 studies
  Some companies prefer to go with Option (1)
   For the next meeting this issue needs to be revisited; input explaining relation to Rel-16 studies would be welcome

## Slide 4: Idle mode mobility from EPC to 5GC (with N26): Need for S-NSSAIs of PDN connections in Registration Request?
Background: S-NSSAI of PDN connections in Registration Request enables
  AMF to select V-SMFs taking S-NSSAIs into account
    Dependency on binding discussion, see previous slide: Unless we add EBIs into Registration Request, AMF cannot determine which S-NSSAI belongs to which EPS bearer context received from the MME
  AMF to select appropriate (other) AMF based on S-NSSAIs of UE’s PDN connections
    Note: Normally AMF would select a different AMF based on S-NSSAIs in Requested NSSAI,
    However, not all S-NSSAIs may be included in Requested NSSAI in roaming case (see slide on “S-NSSAIs in Requested NSSAIs”)
Options:
  Keep S-NSSAIs of PDN connections that UE had in EPC in Registration Request (current spec)
  Remove S-NSSAIs from Registration Request, AMF learns S-NSSAI from SMF (proposed by ZTE in 637)
Discussion results
  Issue has not been discussed yet

## Slide 5: Idle mode mobility from EPC to 5GC (with N26): S-NSSAIs in Requested NSSAI
Background: Potential confusion for RAN if S-NSSAIs from HPLMN (received via PCO in EPS) are included by UE in RRC in Registration Request
Options
  PLMN ID in PCO
    Key idea:
      Include PLMN ID in PCO (in addition to S-NSSAI) to inform UE which PLMN provided the S-NSSAI
      For Requested NSSAI:
        UE to only include S-NSSAIs received in PCO in Requested NSSAI that are from same PLMN as target PLMN (5GC PLMN), OR
        If UE has a Configured NSSAI for the target PLMN, apply mapping for S-NSSAIs received in PCO; UE to include mapped S-NSSAIs in Requested NSSAI
      For Registration Request: UE to include S-NSSAIs and PLMN IDs (as received in PCO) for the PDN connections that were active in EPC
(Note: Once UE receives Configured NSSAI it can locally update the S-NSSAIs for the transferred PDU sessions to reflect the correct S-NSSAI)
Way forward: Introduce PLMN ID in PCO