## Slide 1: Questions for show of hands for LADN
Drafted based on the discussion during LADN Session

## Slide 2: AMF assisting NAS SM message rejection
According to clause 5.6.5 of 23.501, when the UE is out of a LADN service area, the UE:
  - shall not request to activate UP connection of a PDU Session for this LADN DNN;
  - shall not establish/modify a PDU Session for this LADN DNN;
  - needs not release any existing PDU Session for this LADN DNN unless UE receives explicit PDU Session release request from network.
Current solution for 5GC to handle the case that 5GC receives NAS message when UE presence in a LADN DNN is OUT:
  If for some unknown reason, AMF receives the Registration Request, Service Request or PDU Session Establishment/Modification Request message concerning a LADN DNN where the UE presence in this LADN service area is OUT, the AMF still sends N11 message carrying the NAS SM message to SMF, once SMF knows the UE presence in this LADN service area is OUT, the SMF shall (clause 5.6.5 of 23.501):
    - release the PDU Session immediately; or
    - deactivate the user plane connection for the PDU Session with maintaining the PDU Session and ensure the Downlink Data Notification is disabled The SMF may release the PDU Session later.
There are two papers (S2-180377 from Sony, S2-180502 from Huawei) proposing to optimize current solution, both of them were not agreeable. The debate has been lasting for two meetings, we need to make a decision to move on.
Question #1: Can we agree to stop discussing any optimization proposal?
  Supporting companies:
  Objecting companies:
Conclusion:

## Slide 3: How does UE know whether a DNN is LADN DNN?
Three options on table:
  Option #1: During registration procedure, UDM provides the list of UE subscribed LADN DNN list to AMF, AMF indicates whether a DNN in the subscribed LADN DNN list is a LADN DNN to UE via NAS message by reusing LADN information IE as proposed in S2-180441.
  Option #2: PCF sends an LADN indication along with each LADN DNN to UE using URSP as proposed in S2-180669. With this solution, UDM only provides the list of UE subscribed DNN list to AMF, AMF only provides LADN information to UE when the LADN DNN is in the UE subscribed DNN list.
  Option #3: UE knows whether a DNN is LADN DNN per configuration.
Question #2: Can we go with solution #1?
  Supporting companies:
  Objecting companies:
Question #3: Can we go with solution #2?
  Supporting companies:
  Objecting companies:
Question #4: Can we go with solution #3?
  Supporting companies:
  Objecting companies:
Conclusion:

## Slide 4: Whether and how AMF knows whether a UE subscribed DNN is LADN DNN
If option #1 in slide #3 is chosen, UDM needs to send the UE subscribed LADN DNN list to AMF, this is currently missing from both 23.501 and 23.502, further clarification in 23.501 and 23.502 are needed.
If option #2 or #3 in slide #3 is chosen, AMF doesn’t need to know UE subscribed LADN DNN list from UDM, no further study on this aspect is needed.
In any case, AMF needs to be configured with its supported LADN information.

## Slide 5: How does SMF know whether a DNN is LADN DNN?
Option #1: SMF knows from UDM as part of User subscription
  This is the current work assumption for 5GS but not explicitly addressed yet, clarification in 23.501 and 23.502 is needed.
Option #2: Configuring LADN DNNs in SMF
  Not discussed yet.
Question #5: Can we move on with option #1 to clarify the missing description in 23.501 and 23.502?
  Supporting companies:
  Objecting companies:
Question #6: Can we move on with option #2 to clarify the missing description in 23.501 only?
  Supporting companies:
  Objecting companies:
Conclusion: