## Slide 1
Multi-user share the same IMS signaling bearer
Discussion paper
UNIGROUP SPREADTRUM & RDA
S2-18xxxx

## Slide 2: Background Description
An terminal may have multiple IMS users(e.g. multiple SIM cards). Each user needs to activate an IMS signalling bearer for IMS communication services.
Example : A terminal with two SIM cards
  Each SIM card needs a separate IMS signaling bearer for IMS communication services.
  But now many terminals are dual-card dual-standby and cannot make call at the same time.

## Slide 3: Background Description
Also, we can use two IMS signaling bearers and two RFs to implement dual-card dual-pass.
  This solution will increase the terminal's cost & power consumption and so on.
A solution: Multiple users in the same terminal share the same IMS signaling bearer for IMS communication services.
  Just one user need to active an IMS signaling bearer, and other users share it.
  Two SIM cards can make calls and other IMS communication services at the same time.

## Slide 4: Solution: Multi-user share IMS signaling bearer
One of the users activate the IMS signaling bearer , acquire the IP address and P-CSCF address.

## Slide 5: Solution: Multi-user share IMS signaling bearer
Multiple users register to network with the same IP.

## Slide 6: Solution: Multi-user share IMS signaling bearer
Each user's MO/MT Call is independent and does not affect each other.

## Slide 7: Solution: Multi-user share IMS signaling bearer
Each user uses the same IMS signalling bearer for IMS registration.
  The PCSCF address and IP address each user uses maybe identical, but the port number of the IP address must be different.
  The private user identity generated by each user is independent of each other.
  The public user identity generated by each user is independent of each other.
  Each user's registration process should be in accordance with the TS 24.229 protocol specification.
After each user registers on IMS, each user can perform IMS communication services independently and has no impact on each other.

## Slide 8: Advantages
Each user can perform IMS communication services independently and has no impact on each other.
Services based on IMS are independent from the signalling bearers and IMS network is not bounded from the IP-CAN network.

## Slide 9: Advantages
Accelerate 2G/3G network migration to 4G networks, reducing 5G terminal multi-mode complexity.

## Slide 10: Challenges
Multiple users of different operators share the same IMS signaling bearer.
  The IMS roaming architecture is required,now there are some IMS roaming architecture options such as“S8 Home Routed (S8HR)”which is studied in TR 23.749.
SRVCC scenario when using the same IMS bearer for IMS Call. E.g. If two SIM cards share sim1`s IMS signaling bearer to make call, the call of sim2 will cannot SRVCC to 2/3G.
  2/3G networks will gradually withdraw from the network, more and more countries and operators will support 4G and 5G networks.

## Slide 11: Conclusions
We propose that SA2 can clarify “Multi-user share IMS signaling bearer ”is a reasonable method.
  In the future, we can add the related descriptions in TS 23.228 through a CR.
We propose that the 3gpp IMS protocols can use the description of “users” to replace the “UE”, in order to reflect the independence of IMS communication services and radio bearers better.
  In the general RAN, SA, and CT protocols, the UE includes UICC, radio bearers and software devices such as the IMS.

## Slide 12
THANK YOU!