## Slide 1: Output of NSSAI handling in Access Stratum drafting sessions
SA2#127 April 16-20 2018, Sanya, China Tdoc S2-184219

## Slide 2: RRC INACTIVE and NSSAI (response to RAN2 LS)
Since RRC Connection Resume procedure MSG3 triggers retrieval of the context in the Anchor NG-RAN node, the UE needs not pass NSSAI to the NG-RAN node in MSG5 as the Allowed NSSAI is already in the context it obtains from the Anchor RAN node.
Proposal: agree that for RRC inactive the UE does not include NSSAI in the Resume procedure.

## Slide 3: Access stratum Connection Establishment procedure (Idle-Connected transition)
The AS may use the NSSAI in the Connection establishment procedure to trigger upfront C-Plane policies in the (R)AN before the CN provides the NG-RAN with the Allowed NSSAI. One example is the Overload control procedure. Other NSSAI-related policies may be configured in the (R)AN also.
  These RAN policies, e.g. in the case of the overload control procedure aimed at protecting the AMF, need a complete view of all the Slices the UE may use once the AS connection is established as partial indication of the S-NSSAIs in the Allowed NSSAI may lead to needless release of the RRC connection.
EXISTING TEXT in TS 23.501: For AS Connection Establishment triggered by a Registration procedure, the Requested NSSAI is formed as documented in clause 5.15.5.2.1 (which documents Registration procedures and slicing).
TO BE VERIFIED WITH RAN BY LS EXCHANGE: All other MO transitions to connected mode DO NOT trigger change the set of slices the UE is allowed to use (defined by the S-NSSAIs in the Allowed NSSAI)  the UE therefore returns in the MO AS Connection Establishment procedure for these transitions a REQUESTED NSSAI equal to the the Allowed NSSAI it stores for the Access type.