## Slide 1: Discussion on ATSSS function
SA WG2 Meeting #129BIS S2-1812115
26 - 30 November 2018, West Palm Beach, USA
Source: Huawei, HiSilicon
Title: Conclusion proposal for Key Issue #4
Document for: Approval
Agenda Item: 6.8
Work Item / Release: FS_ATSSS / Rel-16
Huawei, HiSilicon

## Slide 2: Introduction
  SA2 has agreed the following steering modes in ATSSS SID:
    Active-Standby, Smallest Delay, and Load-Balancing
  We see:
    In order to support the Load-Balancing, an additional tunnel needs to be established between the UE and the UPF to transport the sequence number.
    Except the above three modes, Redundancy transmission mode is also needed to support e.g. URLLC service.

## Slide 3: Problem statement
Steering mode : Load-balancing
Traffic type: TCP, UDP (e.g. VR/AR services)
Problem statement: disordering happen when an SDF is split per packet based on the weight factor.
Observation 1: The packets disordering issue shall be solved for the Load-balancing steering mode.
Steering mode : Redundancy transmission
Traffic type: TCP, Ethernet
Problem statement: disordering and replication packets happen when an SDF is redundancy transmission over 3GPP and non3GPP access.
Observation 2: The packets disordering and packets duplication issues shall be solved for the Redundancy transmission steering mode.
A sequence number could be transported with the packet to solve the packets disordering and duplication issues.
Steering mode : Smallest Delay or Active-Standby
Traffic type: TCP, UDP, Ethernet
Problem statement: disordering will happen when an SDF is switching between 3GPP and non3GPP access.
Observation 3: The packets disordering happened in switching procedure should be solved, especially, for the Smallest Delay mode, the switching procedure may happen frequently resulting in the bad user experience.

## Slide 4: Alternative Solution 1
A sequence number could be transported in MPTCP or/and GRE tunnel, as bellows:
GRE protocol extension for the sequence number
MPTCP protocol already supports the sequence number

## Slide 5: Alternative Solution 2
A sequence number could be transported in TFCP/GMA tunnel, as bellows:
TFCP/GMA protocol defined for the sequence number

## Slide 6: Evaluation
 | ATSSS function | 
 | Solution 1 | Solution 2
Use cases | All type of traffic (TCP, UDP, Ethernet, etc.) | All type of traffic (TCP, UDP, Ethernet, etc.)
Transport resource consumption | Heavy header, i.e. MPTCP/TCP/IP or GRE/UDP/IP header (three new layers between the UE and UPF) | Light header, i.e. TFCP/GMA header (one new layer between the UE and UPF)
Tunnel related information | Convergence method : MPTCP or GRE Tunnel IP address: UE IP and UPF IP address | Convergence method :TFCP/GMA
Implementation | OS | Chip
Solution
Criteria
On the protocol selection for tunneling, our preference is GMA/TFCP. However, we could accept to apply MPTCP and/or GRE tunnel with support of sequence number to resolve reordering and duplication issues.

## Slide 7: Conclusion
1) Add the Redundancy transmission steering mode.
2) Standardize the alternative solution 1 and alternative solution 2.