## Slide 1
SA WG2 Meeting #129 Bis
26th - 30th Nov., 2018, West Palm Beach, USA
Source: Nokia, Nokia Shanghai Bell
Title: Usage monitoring for multiple PCF deployment of the same DNN and S-NSSAI
Document for: Discussion
Agenda Item: 6.5.6
Work Item / Release: 5GS_Ph1/Rel-15
S2-1812126

## Slide 2
Problem
If multiple PCFs are deployed in a [DNN, S-NSSAI], when usage monitoring is applied, “Remaining allowed usage subscription information” stored in the UDR may be retrieved and updated by multiple PCFs, thus the sum of the usage controlled by all the PCFs in a [DNN, S-NSSAI] may be over the retrieved “Remaining allowed usage”, as there’s no PCF interaction.
Then it is assumed that only one PCF is selected for all PDU sessions for a [DNN, S-NSSAI] for the UE if usage monitoring is required for this UE.

## Slide 3
AMF
SMF
BSF
PCF ID
PCF selected by BSF Indicator
SUPI,
IP,
DNN,
S-NSSAI
Option 1 (Huawei proposal, postponed)
SMF selects the PCF by querying BSF if “PCF selected by BSF Indicator” is received from the AMF
Con:
new SMF-BSF interface
AMF has no knowledge on whether usage monitoring is required for the SUPI
AMF always needs to identify if there are multiple PDU sessions going to the same [DNN, S-NSSAI] for the SUPI.

## Slide 4
AMF
PCF
SMF
UDM
BSF
Policy Data
Subscription Data
H-UDR
SUPI, PCF ID, other subscription data
V-UDR
Option 2
SUPI,
IP,
DNN,
S-NSSAI,
PCF ID
SUPI,
IP,
DNN,
S-NSSAI
PCF ID
SUPI, DNN, S-NSSAI
SUPI, PCF ID, other subscription data
SUPI, DNN, S-NSSAI
Serving PCF ID is stored in the H-UDR by the BSF as the subscription data that can be retrieved by the SMF when the 2nd PDU session is established
Con:
For roaming case, BSF in the VPLMN updates the subscription data stored in the H-UDR

## Slide 5
AMF
PCF
SMF
UDM
Policy Data
Subscription Data
H-UDR
V-UDR
Option 3
SUPI,
IP,
DNN,
S-NSSAI,
PCF ID
SUPI, DNN, S-NSSAI
BSF
SUPI,
IP,
DNN,
S-NSSAI,
PCF ID
SUPI, DNN, S-NSSAI
SUPI, PCF ID, other subscription data
SUPI, PCF ID, other subscription data
Serving PCF ID is stored in the H-UDR by the PCF as the subscription data that can be retrieved by the SMF when the 2nd PDU session is established
Con:
For roaming case, PCF in the VPLMN updates the subscription data stored in the H-UDR

## Slide 6
AMF
PCF
SMF
UDM
BSF
Policy Data
Subscription Data
H-UDR
V-UDR
BSF Data
SUPI,
IP,
DNN,
S-NSSAI,
PCF ID
SUPI,
IP,
DNN,
S-NSSAI,
PCF ID
SUPI, DNN, S-NSSAI
SUPI, PCF ID, other subscription data
SUPI, PCF ID
SUPI, other subscription data
Option 4
Serving PCF ID is stored in the V-UDR by the BSF as the BSF data that can be retrieved by the SMF via UDM when the 2nd PDU session is established
Con: for the roaming case, UDM in the HPLMN retrieves the BSF data stored in the V-UDR

## Slide 7
AMF
PCF 2
SMF
BSF
SUPI,
IP,
DNN,
S-NSSAI,
PCF 2 ID
Option 5
When PCF registers itself to the BSF, and BSF discovered that for the same [SUPI,DNN, S-NSSAI] there is already a PCF registered, it returns a PCF ID to the PCF. If usage monitoring is required for the SUPI, the PCF provides the PCF ID to the SMF for it to reselect a PCF.
Note: PCF can identify whether usage monitoring is required from the PCC policy data retrieved from the UDR
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
PCF 1
Con: PCF redirection may be required

## Slide 8
AMF
PCF 2
SMF
BSF
SUPI,
IP,
DNN,
S-NSSAI,
PCF 2 ID
Option 6
It is SMF who registers [PCF ID, SUPI, DNN, S-NSSAI] to the BSF after a PCF is selected
SMF registers [PCF ID1, SUPI, DNN, S-NSSAI] to the BSF after PCF1 is selected for PDU session 1
When SMF registers [PCF ID2, SUPI, DNN, S-NSSAI] to the BSF, and BSF discovered that for the same [SUPI,DNN, S-NSSAI] there is already a PCF registered, it returns PCF ID1 to the SMF for it to reselect a PCF.
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
PCF 1
Con:
SMF doesn’t know if usage monitoring is required for the SUPI
New SMF-BSF interface
Too much change to the existing solution

## Slide 9
Way forward
To follow the assumption that only one PCF is selected for all PDU sessions of the same [DNN, S-NSSAI] for the UE when usage monitoring is required for this UE, option 5 has the least impact.
  The only problem introduced by Solution 5 is that PCF redirection may be required.
  Considering that for most of the cases the same PCF is selected and the redirection rarely happens, it is proposed to adopt Solution 5
Alternatively, the over resource consuming may also be avoided if the UDR can intelligently allocate the “remaining allowed usage” to multiple PCFs
  When UDR discovers that there are more than one PCF retrieving “Remaining allowed usage subscription information”, it redistributes the “remaining allowed usage” value for the multiple PCFs, e.g. it may generate another instance of “Remaining allowed usage subscription information” for the new PCF and pushes the updated value to the PCFs who had retrieved it from the UDR before.
Proposal: Either Solution 5 is adopted or UDR is enhanced to intelligently allocate the “remaining allowed usage” to multiple PCFs