## Slide 1
Source: Nokia, Nokia Shanghai Bell
Service Request with change of access

## Slide 2: Contents
1) Description of the issue
  Summary: At meeting SA2#128bis, a correction to Service Request when triggered by the network while the UE is in CM-IDLE in non-3GPP access was agreed in CR 0697R3 (S2-188923). In such scenario, the AMF may notify the SMF that the access can be changed, and the SMF is expected to retrieve the PCC rules for the new access and to send a new N1/N2 message to the AMF.
  The issue arises in home routed roaming scenario
2) Proposal
  Summary: The “access type” is added to N1N2MessageTransfer (same as for ATSSS MA-PDU session but from Rel-15 onwards)

## Slide 3: Description of the issue (1/4)
Rationale for involving PCF
  Originally, Service Request procedure was not designed to involve PCF and to be limited to the Served PLMN. But when using Service Request procedure for change of access, this cannot be true anymore
  The SMF is expected to retrieve the PCC rules for the new access, even if QoS is access agnostic. This is because PCC rules contain the Charging Rating Groups for a specific access
Non-roaming scenario
  Step 1: Network Triggered Service Request (TS 23.502 Figure 4.2.3.3-1 adapted to DL signalling data)

## Slide 4: Description of the issue (2/4)
Non-roaming scenario (cont’d)
  Step 2: Service Request received over 3GPP access
1) step 4: AMF informs SMF about possible access change (via PDU Session UpdateSMContext Request)
2) step 11: New QoS rules are received (via PDU Session UpdateSMContext Response)
3) AMF knows that the new QoS rules are related to the “other” access (non-3GPP access), because it obviously links the UpdateSMContext Response with the Request
Hence, no issue in non-roaming case

## Slide 5: Description of the issue (3/4)
Home routed scenario (refer to figure in next slide)
AMF still uses the Nsmf_PDUSession_UpdateSMContext Request to inform SMF about access change
But V-SMF and H-SMF use the Nsmf_PDUSession_Update procedure for their exchanges.
  V-SMF  H-SMF: (1e) Nsmf_PDUSession_Update Request
  H-SMF  V-SMF: related Nsmf_PDUSession_Update Response does not include the new QoS rules (anyway, they would be received too late)
  QoS rules are only included in the second Nsmf_PDUSession_Update Request (from H-SMF to V-SMF in step 3), then sent to AMF via N1N2MessageTransfer
But, at V-SMF and AMF, there is no way to link Nsmf_PDUSession_Update Request/N1N2MessageTransfer with the original AMF request to SMF: it could be a totally new exchange initiated by PCF, not related to the AMF original request  AMF does not know which access the N1N2MessageTransfer is referring to

## Slide 6: Description of the issue (4/4) Figure 4.3.3.3-1: Home routed roaming scenario

## Slide 7: Proposal
Since, in home-routed scenario, the AMF does not know which access is concerned by the N1N2MessageTransfer, it is proposed to add the “Access Type”
  Please note that the “Access Type” is also introduced in Rel-16 for ATSSS: the establishment of a MA-PDU Session (step 7 of TR 23.793 clause 6.2.2.2)
  Also note that it is only needed when N1N2MessageTransfer includes N2 SM Container (which is access dependent)
Collateral: a new parameter “indication of access type change possible” is needed in PDU Session Update Request (1e) between V-SMF and H-SMF
  The existing “Access Type” refers to the current access, and used for charging wrt OCS
  “indication of access type change possible” would be mapped to “access type” in SMF-initiated Policy Association Modification towards PCF (which remains unchanged)
A companion CR is proposed to TS 23.502

## Slide 8
Thank You!