## Slide 1
Handling of slice based overload control at NG-RAN
NEC, Interdigital, AT&T, KDDI, NICT, Convidawireless
SA WG2 Meeting #130 S2-1900433
21 – 25 January 2019, Kochi, India

## Slide 2
Rel-15 UE and Network behaviour
    An AMF invokes Slice based overload control at NG-RAN by sending Start Overload message containing a congested S-NSSAI(s).
    When a NG-RAN receives Requested NSAAI during the RRC connection establishment procedure and the requested NSSAI are indicated as congested by the AMF then the NG-RAN sends a GENERIC wait time in the RRC connection release to the UE.
    When the UE receives GENERIC wait time in the RRC connection Release message it will not send any AS and NAS signalling till the wait time expires. This procedure may block ALL services at the UE.

## Slide 3
  When the AMF requests NG-RAN to perform overload control for one service/Slice (S-NSAAI) then the NG-RAN will send generic wait time to the UE if the UE has sent only the congested S-NSSAI during the RRC Connection establishment procedure (e.g. in the RRC Connection Setup Complete message (enhanced E-UTRAN connected to 5G) or RRC Setup Complete message (NR connected to 5G)). As a result all the other services (essential services e.g. V2X) at the UE are blocked till the generic wait time expires. This will create bad user experience. The same issue happens in case of non-3GPP access also.
  For example a UE supports IoT, V2X and eMBB services. A IoT related slice is congested and the AMF requests 5G-RAN to perform overload control for IoT only. When the UE includes IoT slice only during the AS connection establishement procedure then the NG-RAN releases the AS connection with generic wait time. After receiving the generic wait time the UE is not allowed establish AS connection for any services. Therefore the user will not get V2X and eMBB services althougth eMBB and V2X slices are not congested. This has serious consequences for services like V2X.
Issue : Drawback of the Rel-15 UE and Network behaviour

## Slide 4
    Following solutions are proposed in Rel-16 to introduce a better mechanism to handle the slice based overload control at a NG-RAN and an UE. Two CRs are submitted for proposal 1 and proposal 2. It is proposed to captures Proposal 1 in the specification to solve the issue described in the discussion paper.
Proposal 1: Sending a slice specific wait time for each congested S-NSSAI.
The 5G-AN sends wait time for each congested S-NSSAI present in the requested S- NSSAI in the RRC Connection Release message. On receiving the wait time for each S- NSSAI the UE shall not initiate any NAS/AS signalling for this S-NSSAI till the wait timer is running.
Proposal 2: Sending a common wait time for all congested S-NSSAI.
The 5G-AN includes a common wait time for all congested S-NSSAI present in the requested NSSAI in the RRC Connection Release. The UE will run a single wait time for all congested S-NSSAI and shall not initiate any NAS/AS signalling related to the congested S- NSSAI till the timer expires.
Proposal