## Slide 1: Discussion about 3GPP Rel-17 eNA phase 2 China Mobile, Huawei

## Slide 2
Key Issue # | Title | Descriptions | Conclusion
1 | Analytic Information Exposure to 5GS NF | General Framework | R16
2 | Analytic Information Exposure to AF |  | R16
3 | Interactions with 5GS NFs/AFs for Data Collection |  | R16
4 | Interactions with OAM for Data Collection and Data Analytics Exposure |  | R16
5 | NWDAF-Assisted QoS Profile Provisioning | 5G QoS enhancement | R16
6 | NWDAF assisting traffic routing | UPF Selection (MEC) | R16
7 | NWDAF assisting Future Background Data Transfer | Background Data Transfer | R16
8 | Performance improvement and supervision of mIoT terminals | mIoT Terminals monitoring | R16
9 | Customizing mobility management based on NWDAF output | Mobility Management | R16
10 | NWDAF service support to select NF instances | NF instance selection | Postponed to R17
11 | NWDAF-Assisted predictable network performance |  | Postponed to R17
12 | Support of Northbound Network Status Exposure |  | R16
13 | UE driven analytics |  | Postponed to R17
14 | How to ensure that slice SLA is guaranteed | Slice SLA guarantee | Postponed to 2019 Q2 R16
Release 16 eNA Key Issues overview:

## Slide 3
Rel-17 eNA Objectives (Detailed discussion in future slides)
  Objective 1: objective is to study the potential enhancements and new scenarios for eNA, including
    Architecture enhancement to support:
      Multiple NWDAF Instances in one PLMN
      Inter PLMN Roaming and Inter Region Roaming
    R16 NWDAF features enhancement
      Recommendations produced by NWDAF
      Enabling real-time or near real-time NWDAF communication
      NWDAF-Assisted UP Optimization
    New Use Cases/key issues
      NWDAF based Smart City
      NWDAF and 3rd AI Model &Training Service
      NWDAF and Wireless network energy saving
      Parental Control for website visiting
      Etc..
    Leftover KIs from R16
      KI#10: NF instance selection
      KI#11: NWDAF-Assisted predictable network performance
      KI#13: UE driven analytics
      KI#14: Non-concluded part of Slice SLA guarantee
      Unresolved problem in KI#4: How avoid negative interaction among consumers of NWDAF analytics
    Leftover unresolved problems from R16
      Unresolved problem: How UPF report data to NWDAF
      Note: Related to S2-1902993: Study on introducing UPF service in 5GC

## Slide 4
  Objective 2: NWDAF Deployment Guideline
    Multiple NWDAF Instances Deployment Guideline
    NWDAF and 3rd AI Model &Training Service Deployment Guideline
    NWDAF and Smart City Deployment Guideline
    Etc.
Rel-17 eNA Objectives (Detailed discussion in future slides)

## Slide 5
Supporting multiple NWDAFs deployment
    How to support layered deployment architecture for multiple NWDAFs inside a PLMN, e.g., data collection/storage and data analytics provisioning to relevant NFs or AFs.
    How to support roaming case between different PLMNs, e.g., NWDAF access authentication, data collection/storage and data analytics provisioning to relevant NFs or AFs.
    Multiple NWDAF Instances Deployment
Fig : Multi-PLMN deployment in roaming scenario

## Slide 6
Recommendations produced by NWDAF
It is evaluated in KI 1 that recommendation produced by NWDAF should be further studied after Release 16.
Solution #9 (Recommendations produced by NWDAF) is a solution that has been evaluated to possibly only cover a limited number of key issues/use cases, which are a subset of what can be solved by analytics. It is not recommended for Release 16, because it requires additional study. It is desirable that this Solution be reconsidered following the results obtained on the implementations of Release 16, in order to examine its relevancy on stronger use case basis.
Context extracted from TR 23.791:

## Slide 7
NWDAF-assisted UP optimization
  NWDAF gathers info from 5GS and Application Platform (e.g., EC platform) and obtains analytics on :
    UE service behavior analytics (i.e. Application ID per region per UE group per time)
    5GS Service MOS analytics (i.e. Service MOS per application ID)
  Based on UE service behavior analytics and 5GS Service MOS analytics, 5GS and Application Platform can select optimized user plane path and application server for this application

## Slide 8
5G NF
NWDAF
AI Model and Training Service Platform
RAN
CN
NEF
AI Model Related to Energy Consumption Reduction
Other Model
Data Collection
Model Update
Operator 1
Data updating
Model updating
AI Model for Resource Utilization Improvement
AI Model Related to User Experience Enhancement
5G NF
NWDAF
RAN
CN
NEF
Data Collection
Model Update
Operator 2
Data updating
Model updating
Operator n
NEF
5G NF
NWDAF
RAN
CN
Data updating
Model updating
Some small and medium-sized operators are proposing new requirements, the cost of independently deploying AI models and training services is high, including hardware and software costs, as well as the development of numerous AI models and continuously updated R&D costs. Can third parties provide independent AI models and training services? Operators use this service directly to achieve cost reduction.
Some large operators have multiple sub-networks in multiple regions, can these sub-networks use a unified AI model and training platform? Because the unified platform enables data fusion of multiple subnets, sharing hardware and software costs and AI model development costs. In this case, the data of each subnet can directly interact with the AI model and the training platform without going through NEF.
NWDAF and 3rd AI Model &Training Service

## Slide 9
NWDAF and Smart e.g. intelligent transportation to alleviate urban traffic congestion
Urban traffic lights
5GS
Centralized NWDAF
City-level networks
UPF
SMF
AMF
Network
Data
OAM
OAM Data
UE MDT
e.g. MR Report
Timing schemes of
traffic light Control
AI Model and Training Service Platform
AI Model for Intelligent Transportation
Other Model
AI Model for Safe City
OAM Data
Edge NWDAF
Timing schemes for traffic light
Spatio-Temporal Prediction
Data Collection
Smart
City Data
Traffic Light Intelligent Control Platform
(Government owned, City level )
Urban traffic congestion
Data
Traffic light
data
Traffic surveillance camera data
Analytics
exposure
  Release 17 objective:
      The Common ICT Infrastructure is constructed based on government scenarios (public transport, resource allocation, safe city, etc.), and gradually evolves into the public infrastructure of the whole society.
      Building Common ICT Infrastructure for Future Intelligent Society Based on 5GS and NWDAF i.e. deliver smart city related data over 5GS and leverage NWDAF to perform data analytics to complement Smart city.
      Taking intelligent transportation as an example, NWDAF collects data from third-party servers (such as urban traffic congestion data, urban traffic light configuration data, etc.), camera data (detecting the number of cars in front of traffic lights, etc.), combined with real-time user location provided by the network. The data provides a more reasonable timing schemes of traffic light to alleviate urban traffic congestion.
Data updating & Model updating
Data updating & Model updating
State level network
Network Data
Camera Data
Notes: 1、；

## Slide 10
NWDAF generates energy-saving related data analytics (e.g. traffic activity prediction) for a given cell by analyzing
  third-party data
  UE related network data
    UE moving Trajectory
    UE service invoking e.g. when and where and which UE invokes which application.
    UE priority e.g. golden\silver\bronze
    UE activity information e.g. TAU/Service Request/Internet surfing
NWDAF only provides energy-saving related data analytics to OAM and OAM makes the decision to perform energy-saving related action .e.g. turn-off load threshold, turn-off time window, etc.
After OAM performed energy-saving action, NWDAF monitor the service experience of the impacted cell and provide further data analytics to OAM.
3rd Data Service（Optional）
Weather data
Map POI
Sports meeting
Holiday data
5G NF
Data Collection
CN
NEF
UE MDT Data
CN Data
RAN Data
Data Analysis
NWDAF
OAM
Energy-saving Decision
RAN
Performance monitoring
Data analytics
1
2
3
4
UE related network data
NWDAF and Wireless network energy saving

## Slide 11
Thanks!