## Slide 1: ATSSS and EPS IWK
Telstra, Deutsche Telekom, BT, Orange, Ericsson, Nokia, Nokia Shanghai Bell
S2-1903135
SA WG2 Meeting #132
8 – 12 April, 2019, Xi’an, China

## Slide 2: Background
So far EPC IWK has not been addressed for ATSSS:
  The study concluded that it would be handled in normative phase
  During normative phase the topic has so far been not handled / postponed
Solution discussed so far assume that MA PDU Session becomes a ”single access” PDN Connection when in EPS and may be turned back into a MA PDU Session when moved to 5GS
  This however focuses on ”turning off” ATSSS as soon as EPS is involved

## Slide 3: Motivation and use cases
EPS IWK will be a key component in many operator’s networks for several years to come
  ATSSS should accomodate also such scenarios
  The targeted scenario is when UE/RG is connected over LTE in EPS and non-3GPP/wireline access in 5GS
  Such connectivity is supported already in rel-15, but only with single-access PDU Sessions => For ATSSS, investigate how it can be handled for MA PDU Sessions
Two major use cases:
  Mobile handset/tablet supporting 5GC+ATSSS
    The issue: With original NR coverage typically on mid & high bands with low in-building penetration, and WiFi coverage typically in-building, the 3GPP and N3G access to 5GC will not frequently co-incide. Most operators have better LTE coverage at low frequencies - but with option1, i.e. EPC IW required. A UE supporting NR SA (Option2) may also use EN-DC (Option3) during its mobility, so this option shall be supported as well.
  Hybrid access 5G-RG (with ATSSS capability)
    The issue: The 5G-RG is in-building, it connects to 5GC via W-5GAN but NR coverage (with mid/high-band) will only progressively reach the suburbs and may require special antenna solution for the RG. Similarly to UE case, most of the 5G-RG’s do have LTE coverage already

## Slide 4: Possible solution
Build on ATSSS and allow a MA PDU Session to have a leg in LTE/EPC
ATSSS control signalling (ATSSS rules) via 5G leg, i.e. via 5G SM NAS
Impacts UE/RG and PGW-C/SMF
ATSSS features in PCF/N7 and UPF/N4 are re-used
Transparent to MME and SGW
N4
HSS+ UDM
PCF
AMF
AGF / TNGF / N3IWF
eNB
MME
SGW
UPF+ PGW-U
SMF+ PGW-C
UE / 5G-RG
Non-3GPP / wireline
S11
S6a
S1-MME
S1-U
S5-U
S5-C
N10
N15
N11
N3
N2
N7
DN

## Slide 5: Further aspects (1)
ATSSS control plane:
  ATSSS control plane supported using ATSSS rules carried via 5GC (i.e. 5G SM NAS)
  Loss of 5GC connectivity need to be handled to allow recovery (e.g. using Access Unavailability report as agreed in Tenerife)
PDN Connection establishment in EPS:
  PCO can be used to negotiate ATSSS when activating a PDN Connection in EPC
  Assume homogenous ATSSS support in PGW-C/SMF for a APN, to ensure that MME selects a ATSSS capable PGW-C/SMF
UE policies
  URSP is only applicable to 5GS, so it is unclear how the UE can know that it shall populate the PCO in EPC with ATSSS-related information. An option is that the UE supporting ATSSS with EPS IWK always includes the ”multi-access” indication in the PCO, and the network then decides whether to apply ATSSS or not.
  However this is not a special issue for ATSSS. URSP is in general not applicable to EPS so the situation is not better or worse than general EPS IWK.
Procedures for adding a leg:
  If a PDU Session is active in Non-3GPP/5GC: A ”child” PDN Connection in LTE/EPC can be added using PDN Connection Establishment with ”HO flag” and including a PCO with "MA PDU Request" indication.
  If a PDN Connection is active LTE/EPC: A ”child” PDU Session in Non-3GPP/5GC can be added using current ATSSS procedure for adding a leg (i.e. PDU Session Establishment with "MA PDU Request" indication).

## Slide 6: Further aspects (2)
Single-registration mode and/or dual-registration mode for 3GPP access
  UE can be in either mode. The registration mode used for 3GPP access (single- or dual-) does not impact the usage of non-3GPP access
  It is however assumed that for ATSSS with EPC IWK to work, the UE can be simultaneosly registered in EPC (in 3GPP access) and in 5GS (in non-3GPP access)
  If UE can only be registered in EPS or 5GC (independent of access), also non-3GPP access need to be removed in case UE makes inter-system change to EPS
Policy control works as defined for ATSSS
  PCF provides PCC rules over N5 including Multi-access related parameters. Not impacted by EPC IWK.
  PGW-C/SMF can select PCF based on same principles as for 5GS (or a homogenous deployment is used for an APN/DNN)
Measurements
  Handled between UE and PMF/UPF and should work as defined even if UP connection is on LTE/EPC.
Slicing
  The selection of PGW-C+SMF in the correct slice requires the same mapping between EPC and 5GC slices as required for single-access PDU sessions
Applicability
  Our proposal is to describe the EPS IWK solution for UEs and RGs, but it can be discussed whether the solution shall be limited to RGs

## Slide 7: Further aspects (3): QoS
Current approach for EPC IWK is described in 23.501/23.502:
  PGW-C+SMF will receive 5G QoS information from PCF.
  PGW-C+SMF will map to EPS QoS parameters.
    This can be a 1:1 mapping between QoS flow and bearer, or a mapping of multiple QoS flows to one bearer.
  This mapping is based on operator config in PGW-S+SMF, i.e. not standardized in detail (see informative Annex C in 23.502)
AMBR in UPF: APN-AMBR / Session AMBR
  Current rel-15 specification allows UPF to enforce Session-AMBR also when UE is in EPS. This can be applies also in case of ATSSS, i.e. single Session AMBR enforcement for both legs.
AMBR in UE:
  Currently UE shall enforce UL Session-AMBR (in 5GS) and optionally UL APN-AMBR (in EPS)
  With multi-access conncetivity with a PDU/PDN Session in EPS and 5GS the UE may enforce a single AMBR in up-link
SDF level QoS
  SDF-level QoS is enforced in UPF.
  Not impacted by EPC IWK, since SDF-level QoS enforcement is access independent
GBR QoS flows
  GBR QoS flows will only be carried on a single access at a time (according to existing agreements in ATSSS).
  There should thus be no impact due to EPC IWK. PGW-C+SMF will provide the GBR QoS info either via EPS or via 5GS (AS + NAS).
Non-GBR QoS flows
  Non-GBR traffic may be split/switched between the accesses.
  SMF will provide the respective QoS information to both accesses (EPS QoS parameters via EPC, 5G QOS parameters via 5GC)
  UE should apply the respective access-specific rules (TFTs etc for EPC and QoS rules for 5GC) for UL traffic, depending on UL traffic steering in UE.
  UPF will perform DL traffic mapping to bearers based on rules (PDRs, FARs) from SMF. SMF can provide separate FARs for 4G and 5G and thus the appropriate GTP-U header will be generated based on FAR.
  There is thus no specific impact doe to ATSSS for EPC IWK
How would the QoS enforcement in UE and UPF be impacted by ATSSS with EPC IWK?

## Slide 8: Proposal
Limited impact to support ATSSS also with EPC IWK (UE/RG and PGW-C/SMF)
23.501 CR available in S2-1903136
A corresponding proposal for 5WWC is available in S2-1903137