## Slide 1: Source: Ericsson Title: Unsynchronized EPS Bearer status when UE moves from EPS to 5GS (Unsynchronized QoS Flow status in 5GS) Document for: Agreement Agenda Item: 6.5.9 Work Item / Release: 5GS_Ph1/ Release 15
SA WG2 Meeting #132 08-12 April 2019, Xi’An, China
Tdoc S2-1903146

## Slide 2: Background
In SA2#131, the issue at EPS to 5GS IDLE mobility due to unsynchronized EPS bearer status between UE and network was discussed:
  The proposal addressing the unsynchronized EPS bearer status due to UE local deletion was agreed in S2-1902648 (by means of UE sending EPS bearer status in Register Request);
  The proposal (S2-1901862) aiming to address the unsynchronized EPS bearer status due to network local deletion is still open

## Slide 3: Recap of Scenarios of unsynchronized EPS bearer status at EPS to 5GS IDLE mobility and Possible Issue (1)
Scenarios
  When UE in EPS, default bearer or dedicated bearer is locally deleted in the UE and/or in the network
    Scenario-0 (when in EPS) UE or network locally deleted the default bearer
    Scenario-1 (when in EPS) UE locally delete a dedicated bearer
    Scenario-2 Network deleted a dedicated bearer (e.g. MME delete GBR bearer at S1 Release due to radio link failure) but UE is not aware
  UE stays in IDLE state;
  Then UE moves to 5GS.
Scenario-0 (when in EPS) UE or network locally deleted the default bearer
  Default bearer corresponds to the QoS Flow of the default QoS rule (i.e. PDU Session),
  PDU Session status synchronization in 5GC will ensure the synchronization => NO ISSUE

## Slide 4: Recap of Scenarios of unsynchronized EPS bearer status at EPS to 5GS IDLE mobility and Possible Issue (2)
Scenario-1 (when in EPS) UE locally delete a dedicated bearer
  PDU Session is maintained, but the NW still has the dedicated bearer thus its associated QoS Flow(s), then
      DL packet will be able to be sent to the UE on the un-synched QoS Flow
      UL packet will probably be sent via the QoS Flow associated with the default QoS rule
  [Observation-1] The possible issue is that differentiation of UL packet forwarding treatment cannot be achieved (assume the UE does not drop the DL packet received from the network on the unsynchronized QoS Flow)
Scenario-2 Network locally deleted a dedicated bearer (e.g. MME delete GBR bearer at S1 Release due to radio link failure) but UE is not aware
  UE still has the dedicated bearer thus its associated QoS Flow
    DL packet will be transferred using the QoS Flow associated with the default QoS rule
    UL packets may be transferred using that QoS Flow and it may get dropped by NG-RAN or UPF because the QFI is not known.
  [Observation-2] The possible issue is that UL packets may get dropped leading to service interruption

## Slide 5: New Scenario - Unsynchronized QoS Flow status in 5GS due to UE local deletion
Scenario-3: UE in 5GS, UE locally deleted a QoS Flow (which is not associated with the default QoS rule), but the NW is not aware
  DL packet will be able to be sent to the UE on the un-synched QoS Flow
  UL packet will probably be sent via the QoS Flow associated with the default QoS rule
  [Observation-3] The same issue as in [Observation-1] also applies.
For discussion only, no CR proposed for SA2#132

## Slide 6: Discussion on UE locally deleted a dedicated bearer and a QoS Flow (i.e. Scenario-1 &-3)
Scenario-1 (i.e. UE local deletion of dedicated bearer) is addressed in S2-1902648 (23.502 CR1067: EPS bearer synchronization when move from EPC to 5GC(UE deletes the bearer locally)
Scenario-3 (i.e. UE local deletion of QoS Flow) is not yet addressed, and the following is proposed
  [Proposal-1] If a UE has locally deleted a QoS Flow which is not associated with the default QoS rule, at the next time that the UE contacts the network, the UE sends explicit NAS message to delete the QoS Flow to achieve the synchronization (same approach as network initiated synchronization with the UE in S2-1813029, agreed in SA2#129bis).
As [Proposal-1] could also be used to address Scenario-1, there could be two options on how to handle the update in S2-1902648:
  Option-1: Keep the update in S2-1902648, i.e.
    For UE local deletion of dedicated bearer, at EPS to 5GS mobility, UE do as in S2-1902648
    For UE local deletion of QoS Flow, UE do as in [Proposal-1]
  Option-2: Revert the update in S2-1902648, i.e. same logic applies to both Scenario-1 and Scenario-3:
    If a UE has locally deleted a QoS Flow (including the one mapped from EPS bearer) which is not associated with the default QoS rule, at the next time the UE contacts the network, the UE sends explicit NAS message to delete the QoS Flow to achieve the synchronization.
For discussion only, no CR proposed for SA2#132

## Slide 7: Discussion on Network locally deleted a dedicated bearer (i.e. Scenario-2 )
[Observation-6] The AMF gets EBI list from SMFs.
[Proposal-2] At EPS to 5GS Idle mobility, it’s proposed that the AMF include in Register Accept a new EPS Bearer Status IE based on the EBI list currently provided by the SMF(s).
AMF
PGW-C+SMF
PGW-C+SMF
2. Register Request (EPS to 5GS)
MME
UE moves from EPS to 5GS)
4. Nsmf_PDUSession_CreateSMContext Request/Response
V-SMF
5 Nsmf_PDUSession_Create Request/Response
5 Nsmf_PDUSession_Create Request/Response
1. MME or PGW initiate deletion of dedicated bearer, but UE is not informed
3. Context Response (UE EPS PDN Connection)
(EBIs list)
Register Accept (EPS Bearer Status (new))
[Observation-4] In EPS, the dedicated bearer deletion can be initiated by MME (e.g. at S1 release due to radio link failure per TS or by PGW per 23.401.
[Observation-5] For MME initiated dedicated bearer deletion, PGW is not aware if the UE is reached or not.
(EBI list)
(EBIs list)

## Slide 8: Proposals
For Scenario-3:
  [Proposal-1] If a UE has locally deleted a QoS Flow (including the one mapped from EPS bearer) which is not associated with the default QoS rule, at the next time the UE contacts the network, the UE sends explicit NAS message to delete the QoS Flow to achieve the synchronization.
For Scenario-1, two options:
  Option-1: Keep the update in S2-1902648, i.e.
    For UE local deletion of dedicated bearer, at EPS to 5GS mobility, UE do as in S2-1902648
    For UE local deletion of QoS Flow, UE do as in [Proposal-1]
  Option-2: Revert the update in S2-1902648, i.e. same logic applies to both Scenario-1 and Scenario-3:
    If a UE has locally deleted a QoS Flow (including the one mapped from EPS bearer) which is not associated with the default QoS rule, at the next time the UE contacts the network, the UE sends explicit NAS message to delete the QoS Flow to achieve the synchronization.
For Scenario-2,
  [Proposal-2] At EPS to 5GS Idle mobility, it’s proposed that the AMF include Register Accept a new EPS Bearer Status IE based on the EBI list currently provided by the SMF(s).
        See 23.502 CR1146 (S2-1903147)

## Slide 9
THANK YOU !