## Slide 1
User Plane CIoT optimisation options for 5GS
Sony, Ericsson, Nokia
SA WG2 Meeting #132 S2-1903232
8 – 12 April 2019, Xi’an, China

## Slide 2
  In SA WG2 Meeting #129 in West Palm Beach, which was the last meeting before the 5G_CIoT study should be completed, the group left the conclusion on “frequent small data” open:
    Some companies wanted to implement EPS functionality Suspend-Resume also known as “UP CIoT EPS optimisation”
    Other companies argued that 5GC already support RRC-Inactive which also allow to Suspend and resume the radio bearers
  One power save working assumption related to RRC-Inactive was agreed during the study. This was to allow eDRX in RRC_Inactive, but with the limitation on NAS Retransmission timer value (TBD by CT1, approx. 10-20s).
    In EPS Connected Mode eDRX is up to 10.24s due to NAS retransmission timers
    Also described in S2-1900246, the use of eDRX in RRC_Inactive with values of 10,24s does not offer sufficient power save modes for IoT devices. And especially not comparable with UP solutions in EPS.
Background

## Slide 3
Options
    1) Enhance the 5GC Rel-15 RRC_Inactive functionality to allow long eDRX,
    2) Implement the UP CIoT EPS optimization in the 5G system

## Slide 4
  The main motivation to introduce RRC-Inactive in Rel-15 was
    Less RAN-CN signalling since the N2/N3 remains after UE transition to RRC-Inactive
    RAN paging is more efficient than CN paging, due to the smaller RAN notification area.
    Introduce a new more efficient “Idle mode” for 5G UEs
    RRC Inactive is natively supported in Rel-15, so it should not be removed in Rel-16, rather further enhanced in Rel-16.
  For Frequent small data transmission, the first motivation fits very well.
    For small data, it is important to keep the signalling overhead low, else the signalling might be larger than the actual user data.
    Frequent transmission – then it makes sense to keep N2/N3
  RAN based paging results in shorter PTW than CN based PTW, less power consumption for UE when monitoring POs
  The RNA size can impact the UE signalling if the RNA size is smaller than the UE mobility, due to RNA-U when the UE moves to another RNA.
    RNA can be as large as a TA – this minimizes the extra signalling of RNA-U due to mobility.
Why RRC-Inactive in Rel-15

## Slide 5
  Long eDRX is needed for IoT devices, even if the UE have frequent transmissions. The typical data transmission frequency compared to normal DRX values is still long. Several minutes compared vs a few seconds. Furthermore these types of devices’ data is UL dominated and tolerant to delay – long eDRX is needed.
  What is needed
  RAN to be able to perform extended buffering, since the N3 is still active the user data will be forwarded to RAN
  RAN to be able to handle NAS messages, since the N2 is still active
  To handle the two above, RAN needs the capability to notify the CN that the UE is currently not reachable.
    The notification message could include e.g. estimated buffering time, whether the data was discarded.
    The notification message need in this case not trigger the release of the UE
    RAN must have a possibility to opt out of extended buffering
  The RAN might also need to provide a second notification that the UE soon will be reachable
  For NB-IoT the UE needs to support RNA and RNA-U
What is needed to enhance RRC-Inactive with long eDRX

## Slide 6
  Suspend-Resume CM-Idle as in User Plane CIot EPS Optimisations
    E-UTRAN and NB-IoT support already support suspended mode.
    NR needs to update
      RRCRelease msg needs a new cause value (rrc-suspend, if same as LTE is used)
  RRC-Inactive
    E-UTRAN and NR support already support RRC-Inactive
    NB-IoT needs to update two RRC-messages (same additions as for E-UTRAN in rel-15)
      RRCConnectionRelease-NB need to include rrc-inactiveConfig IE
      RRCConnectionResume-NB needs to include new cause value for RNA-U
  In both cases either TS 36.331 or TS 38.331 behaviour text needs to be updated
RRC impact

## Slide 7
  Suspend-Resume CM-Idle as in User Plane CIot EPS Optimisations
    New N2 messages to support Suspend/Resume
    Suspend the N3 tunnel
      AMF needs keep the UE is CM-Idle (suspend) state
      AMF needs to forward the suspend top the SMF
      SMF send a new N4 message to suspend the N3 tunnel at the UPF
  RRC-Inactive
    New or updated N2 message to support RAN notifications towards AMF
RAN3 impact

## Slide 8
  Suspend-Resume CM-Idle as in User Plane CIot EPS Optimisations
    AMF needs to store new UE state in context (CM-idle/suspend mode).
    AMF needs to forward the suspend/resume message to the SMF
    SMF needs to suspend/resume the user plane, new N4 messaging to suspend and resume N3.
    New functionality between AMF and SMF
  RRC-Inactive
    AMF support receiving extended notification from RAN and re-use the non-reachability API towards the SMF to trigger data delivery status reporting
    RAN opt out of extended buffering either
      re-use Rel-15 RAN paging failure procedure, or
      RAN notifies the AMF that can send a notification message to the AF informing the AF that the UE is not reachable
    Re-use 4.8.3 procedure to support on-time availability notification event reporting requested by AF.
CN impact

## Slide 9
  Suspend-Resume CM-Idle as in User Plane CIot EPS Optimisations
    CN based paging using PTW for reliable paging
  RRC-Inactive
    RAN based paging
    Smaller area and no CN-RAN synchronisation issues results in shorter PTW than CN based paging
  UE will consume less power due to the shorter PTW in RRC-Inactive, since the UE needs to monitor less paging occasions than in CM-Idle with longer PTW.
Paging aspects of using eDRX

## Slide 10
  Both solutions require updates and changes to RAN/CN
  RRC-Inactive offer
    Less RAN - CN signalling and no additional NF - NF signalling if the Data Delivery Status service is not requested by the AF.
    Lower power consumption when monitoring paging occasions (shorter PTW)
    Potential higher power consumption in case of high mobility UE (mobility across several RNA=TA)
    Continuation of the core 5G-system feature - RRC-Inactive
  Suspend-Resume offer
    Potential lower power consumption in case of high mobility UE (mobility across several TA)
    Higher power consumption when monitoring paging occasions (longer PTW)
    higher RAN - CN signalling and NF - NF signalling (several network functions involved)
    Continuation of LTE RAN feature User Plane CIoT Optimisation
Summary

## Slide 11
    Alt1: Select RRC-Inactive as the new UP optimisation in 5GS
    Alt2: Implement both solutions to offer high mobility UE lowest possible power consumption
Proposal