## Slide 1: Comparison & Evaluation of Soln 11 Option 2 and 3 Ericsson, Huawei, ZTE
S2-1903371
3GPP SA2#132, April 8 – 12, 2019
Xi’an, P.R. China

## Slide 2: Time synchronization – Analysis
solution 11 option 2:
    UPFs and gNBs directly connected to external clocks,
    and all clocks sent OTA to UEs
    RAN provides its own reference 5G clock and tracks up to 32 more
    gNBs and UPFs are synced to multiple (external) clocks via transport network, (gNB maintains also an internal 5G clock)
solution 11 option 3:
    gNBs provide only sync for UEs for 5G-clock (sent OTA)
    RAN agnostic to external time domains
    UPFs time-synced to the gNB/RAN clock
    External clocks synced via u-plane path with time-stamping in TSN translators (@ UPF and UE)
    All 3GPP u-plane nodes are synced to one common clock (3GPP clock)
Option B
TSN
GM2
End
station
UE
solution 11 option 2
End
Station
UPF
gNB
5G GM
TSN
End
Station
TSN
uu
M
S
TT
5G time
domain
UE
TT
TT
TSi
TSi
UE
TSe
TSe
TSe
TSe
solution 11 option 3

## Slide 3: Time-aware system according to IEEE 802.1 AS
802.1 AS compliance means:
preciseOriginTimestamp not touched
Update correctionField by link delays and residence times
External clocks synced via u-plane path
Time-Aware System
ResidenceTime
Link Delay
GM
Time-Aware System
Time-Aware System
Internal synch
Residence
time
stamp
stamp
Last slave
preciseOrigin Timestamp
Updated correctionField
Follow_Up(preciseOriginTimestamp,
correctionField)
Sync(originTimestamp, correctionField)
Time-aware system i-1
master port
Time-aware system i
Slave port master port
Time-aware system i+1
Slave port
Follow_Up(preciseOriginTimestamp,
correctionField)
Sync(originTimestamp, correctionField)

## Slide 4: Option#3 Transport of Time Information
802.1 AS compliance means:
preciseOriginTimestamp not touched
Update correctionField by link delays and residence times
External clocks synced via u-plane path
Time-Aware System
ResidenceTime
Link Delay
GM
Time-Aware System
Time-Aware System
Internal synch
Last slave
preciseOrigin Timestamp
Updated correctionField
Follow_Up(preciseOriginTimestamp,
correctionField)
Sync(originTimestamp, correctionField)
Time-aware system i-1
master port
Time-aware system i
Slave port master port
Time-aware system i+1
Slave port
Follow_Up(preciseOriginTimestamp,
correctionField)
Sync(originTimestamp, correctionField)
5G System
802.1 AS gPTP transmitted over 5G u-plane
Residence
time
stamp
stamp

## Slide 5: IEEE 802.1AS compliance requirement
11.2.14.3 State diagram
The MDSyncReceiveSM state machine shall implement the function specified by the state diagram in Figure 11-6, the local variables specified in 11.2.14.1, the functions specified in 11.2.14.2, the structure specified in 11.2.10 and 10.2.2.1, the messages specified in 11.4, and the relevant global variables and functions specified in 10.2.4 through 10.2.6. The state machine receives Sync and, if the received information is two-step, Follow_Up messages, places the time-synchronization information in an MDSyncReceive structure, and sends the structure to the PortSyncSyncReceive state machine of the PortSync entity of this port.
11.2.15.3 State diagram
The MDSyncSendSM state machine shall implement the function specified by the state diagram in Figure 11-7; the local variables specified in 11.2.15.1; the functions specified in 11.2.15.2; the structures specified in 11.2.9, 11.2.11 and 10.2.2.1; the messages specified in 11.4; the MD entity global variables specified in 11.2.13; and the relevant global variables and functions specified in 10.2.4 through 10.2.6. The state machine receives an MDSyncSend structure from the PortSyncSyncSend state machine of the PortSync entity of this port and transmits a Sync and corresponding Follow_Up message.
Based on the state diagrams ,the preciseOriginTimestamp shall contain the timestamp from the GM. As 802.1AS time aware is a BC compliant clock, that must not update the precise origin timestmap. IEEE1588 actually does not require the preciseOriginTimestamp or originTimestamp to reflect the local PTP clock, but only the sum of the respective one of these and the respective correction fields. In 9.5.9.4 of the latest draft of 1588-Rev, it says:
The originTimestamp field of the Sync message shall be an estimate no worse than ±1 s of the <syncEventEgressTimestamp> excluding any fractional nanoseconds.
The originTimestamp field of the Sync message should be the <syncEventEgressTimestamp> excluding any fractional nanoseconds. The sum of the Sync message correctionField and originTimestamp field shall be the value of the <syncEventEgressTimestamp> including any fractional nanoseconds

## Slide 6: Comparison of the main approaches (1)
 | Solution#11 Option 2 | Solution#11 Option 3 & Solution#28 | Solution#11 Option 4
5GS must be IEEE 802.1AS compliant | No (preciseOriginTimestamp is not preserved) | Yes | Yes
TSN Impact on RAN | Yes, Add complexity (in order to support gPTP in addition to PTP) | No. Only 5GS clock at gNB, Uu scheduler only deal with 5GS clock. | No
gNB clock handling 5GS clock | 5G clock: the gNB needs to track the 5GS clock for radio functions Is the 5G clock distributed over Uu? | gNB needs to maintain 5GS clock for radio functions 5G clock is distributed over Uu | gNB needs to maintain 5GS clock for radio 5G clock is distributed over Uu
gNB clock handling TSN clock | Yes, gNB needs to track the TSN clock The TSN clock is distributed over Uu (SIB:160ms interval  impact on TSN clock drift) | No. | No
Impact on UPF / TSN translator (TT) | Yes TSN clock is connected to gNBs via PTP compatible underlying transport network between UPF/TT and gNBs. UPF is entry point for external gPTP messages. Note* External TSN clock does not really have a direct cable to each gNB, TSN GM directly connected to gNB is a special (unrealistic) case. | Yes, UPF/TT is synchronized with 5G GM, Requires timestamping for gPTP messages (based on the 5G clock) | Yes, UPF is synchronized with 5G GM
Impact on UE/TT | Yes needs to support gPTP, needs timestamping with TSN clock on the egress port. | Yes needs to support gPTP, timestamping with 5G clock on the egress port | Yes needs to support gPTP timestamping with 5G clock
Synchronization directions | Dowlink: Yes Uplink: No | Dowlink: Yes Uplink: Yes | Dowlink: Yes Uplink: Yes

## Slide 7: Comparison of the main approaches (2)
 |  | Solution#11 Option 2 | Solution#11 Option 3 & Solution#28 | Solution#11 Option 4
gNB Complexity in the support of Multiple TSN working clock domains |  | Yes, Complexity to manage/track multiple clocks in the gNB. | No | No
UPF/TT Complexity in the support of Multiple TSN working clock domains |  | Yes, Complexity to manage/track multiple TSN clock domains at UPF / underlying transport network “UPF implementations may need to be synchronized with TSN master clock”—option2 description | Yes, Complexity to manage/track multiple TSN clock domains at UPF / underlying transport network Manage/track 5GS clock domain Timestamping of gPTP messages for every domain with the 5GS clock | No. only 5GS clock at UPF (limitation to sync all OT working clocks to 5G) (*)
Complexity in deployment |  | High Every gNB has to deal with multiple clock domains | Medium One UPF may be connected to several gNBs, only the UPF deals with multiple clock domains. | Low only 5GS clock at UPF (limitation to sync all OT working clocks to 5G) (*)
Multiple TSN working domain (see TS 22.104, annex D2) | “separate” use case | Unknown | Yes | N/A
 | “merge” use case | Can use option4 for multi-domain support | Yes | Yes
(*)May require changes to industrial controllers (unrealistic)

## Slide 8: Comparison of the main approaches – another angle
Use Cases | GM internal to the 5GS | GM external to the 5GS | IEEE802.1AS Rev Compliance
Single working time domain | Opt 2 and 4 fundamentally identical. Solution could be described using Option 4 with a sub-option that the GM could be an 802.1AS GM instead of a G.8275.1 GM * | Option 2 : requires all nodes in the 5GS (including gNB) to support 802.1AS . 5GS requires ptp timescale, and is typically locked to GNSS using the G.8275.1 telecom profile. Running also 802.1AS in the gNB requires implementation of 2 different PTP instances Option 3: no impact on gNB. | Option 3 fully aligned with 802.1AS Rev. For Option 2 to be compliant, would need to relay the TSN GM preciseOriginTimestamp across the 5GS
Multiple TSN working time domains | N/A Option 2 would mean multiple TSN GMs running with arbitrary timescales connected to the gNB. | Option 2 : requires all nodes in the 5GS including gNB to support x instances of the 802.1AS. Increased complexity as number of domains increases. 5GS requires ptp timescale, and typically locked via GNSS using the G.8275.1 telecom profile. Running 802.1AS in the gNB requires implementation of n +1 different PTP instances Option 3: no impact on gNB. Scalable if number of time domains increases | 

## Slide 9: Compare Complexity in RAN and UPF
Solution 11 Option 2
Solution 11 Option 3 & Solution 28
TSN
Up to 32 working clock domains
GM
GM
GM
GM
…
UPF is tracking multiple TSN time domains
UPF is tracking the 5G clock
gNB
gNB
gNB
UPF
TT
Every gNB is tracking the 5G clock
5G time domain
GM 5G
TSi
TSi
TSi
TSi
TSN
5G time domain
Up to 32 working clock domains
GM
GM
GM
GM
…
gNB
gNB
gNB
UPF
TT
GM 5G
Every gNB is tracking multiple TSN time domains
Every gNB is tracking the 5G clock
UPF is tracking multiple TSN time domains

## Slide 10: Time-sync for device based Grand Master time distribution
Solution#11 Option 3 & Solution#28
The 5GS (UE, gNB, UPF) is time synchronized in 5G Clock
TSN time domain is synchronized on the user-plane, independent from uplink or downlink via timestamping, and determination of residence time
 Time synchronization is also feasible in uplink
Solution#11 Option 2
No uplink time distribution is described
 Does not work for Time Grand Masters at UE side
TSN
gNB
UPF
Translator
/ Adaptor
Device (talker)
UE/TT
GM
e.g. PLC
controller
E.g. industrial robots
There can be use cases when the Time Grand Master (GM) is located at the UE (e.g. a PLC controller with a GM)
Device (listener)
Device (listener)

## Slide 11: TSN traffic characteristics for RAN optimization

## Slide 12: 5G RAN optimization for Qbv
CNC – 5GS traffic profile info
The message from CNC could provide the following info.
  Packet size, Packet periodicity
  Message arrival time at 5G ingress (TT)
    RAN need ”arrival time at gNB”
    Time at the ingress of 5GS, not at the gNB
      T depends on UPF processing and transport delay, and introduce an error in ”Message arrival time”
       this error needs to be corrected, and may need to be updated e.g. after handover
    PTP compatible transport network can provide transport delay correction, but it is NOT a U-plane path  cannot be used for T
A
uu
AF/ Transl.
CNC Central Network Config
CUC Central User Config
SMF
AMF
NEF
PCF
TSN Node (A)
Virtual 5G TSN Bridge (B)
TSN Node (C)
UPF
Transl.
gNB
Transl.
UE
TSN traffic pattern A
TSN traffic pattern A
TSN traffic pattern A
TSN traffic pattern A
Downlink
A
T

## Slide 13: Time scales between CNC and u-plane
Message (A) is sent whenever the TSN traffic profile is changed by the CNC
  Typically rarely, e.g. once per week
  No “start time” of packets but only of a message profile
TSN u-plane traffic (B) is sent frequently, e.g. every ms
B
Msg.
size
periodicity
e.g. 1 ms
CNC update
e.g. 1 week
B
A
Many data packets, e.g. 108
The gNB can estimate arrivals of packets from the periodicity and the arrival time of earlier packets
CNC cannot provide the start time of individual packets

## Slide 14: Time scales between CNC and u-plane (2)
Message (A) is sent whenever the TSN traffic profile is changed by the CNC
Message (A) can contain
  Packet size
  Periodicity
  Arrival time
 Packet size and periodicity valid for the entire time the traffic profile is used
 Arrival time only applicable for instances when the traffic profile changes.
B
Msg.
size
periodicity
e.g. 1 ms
CNC update
e.g. 1 week
A
Many data packets, e.g. 108

## Slide 15: Non-public networks impact on time-sychronization

## Slide 16: Time-sync in NPN
3GPP SA2 defines non-public networks (NPN) for Industrial IoT in two variants
  Standalone NPN
  Public network integrated NPN
Related analysis for NPN has been published by 5G-ACIA
  5G-ACIA, ”5G Non-Public Networks for Industrial Scenarios,” March 2019, 5G-ACIA https://www.5g-acia.org/index.php?id=6958
Standalone NPN
Public network integrated NPN (multiple variants)

## Slide 17: Time-sync in NPN
A relevant scenario for 5G in industrial use cases for TSN is a shared RAN for multiple NPNs (e.g. at an industry park)
Each NPN can have multiple time domains, e.g.
  one shopfloor time domain
  one time domain per production domain (i.e. one controller with a number of actuators / sensors)
GM – Grand master clock

## Slide 18: Time-sync in NPN comparison Time domain distribution GM  5GC  5G RAN (Step 1/2)
Solution#11 Option 3 & Solution#28
5G Time is distributed to UPFs
 Simple time distribution
 Can scale to arbitrary number of time domains
Solution#11 Option 2
All time domains from all NPNs need to be provided to all RAN gNBs
 Complex time distribution
 Scalability problem for X*32 time domains for X NPNs
GM – Grand master clock

## Slide 19: Time-sync in NPN comparison Time domain distribution 5G RAN to UE (Step 2/2)
Solution#11 Option 3 & Solution#28
5G Time only is distributed from all gNBs to all UEs
  RAN broadcast or RAN unicast control (RRC)
Working clock domain times are transmitted over user-plane UPFUE
   U-plane load (manageable according to RAN LS)
 Simple time distribution
 Security model of u-plane applies for time distribution (separation of different NPNs)
Solution#11 Option 2
All time domains from all NPNs are distributed from all gNBs to all UEs (up to X*32 time domains)
  RAN broadcast or RAN unicast (RRC)
 Concerns
   Scalability of RAN control plane
   Security concern to distribute time sync information from one NPN publicly to other NPN UEs?
GM – Grand master clock