## Slide 1: Data Analytics based 5G Slice SLA Guarantee China Mobile

## Slide 2: Slice provisioning stage (Agreed in 3GPP)
RAN
NSSF/PCF
CN
OAM (Slice Creation + Slice Resource Configuration)
NWDAF
AMF
New Slice
Existing Slice
PCF
PCF
CN Resource Configuration
3rd Party
Tenant SLA Requirement (Serviceprofile)
Slice Resource Configuration
Radio Resource Configuration
(rRMPolicyRatio2 =Initially 15%~70%)
  Traditionally OAM IS responsible for network/slice configuration and DOES NOT feedback Slice SLA fulfillment to 5GS
Slice level resource configuration:
- Existing Slice A(SLA agreement ) :
> Guaranteed: 10%
> Maximum: 50%
- New Slice B on trail
> Guaranteed: 15%
> Maximum: 70%
MDAS
  Very flexible per slice radio resource boundary in RAN is configured by OAM

## Slide 3: Slice Run-Time stage – Trial phase for the new slice (Agreed in 3GPP except Slice QoE Evaluation)
  Open Question: How RAN schedule the proper radio resource to accurately meet Slice QoE with such flexible per slice radio resource boundary configured by OAM?
Slice level resource configuration:
- Existing Slice A(SLA agreement ) :
> Guaranteed: 10%
> Maximum: 50%
- New Slice B on trail
> Guaranteed: 15%
> Maximum: 70%
RAN
NSSF/PCF
(Slice QoE Evaluation)
CN
OAM (Slice SLA Evaluation + Cause Domain Determining)
3rd AF
⑤ new slice QoE(Service MOS)
NWDAF
(Service MOS Measurement)
① new slice Service MOS Query (Network Area by Tenant)
AMF
New Slice
Existing Slice
PCF
PCF
Service MOS
Slice QoE Requirement in 6.32, TR 23.791
- Network Area
- Average Service MOS per A
- Percentage UEs’ Service MOS satisfied
Time | Slice B Service MOS per Application | Percentage UEs’ Service MOS satisfied | Slice B QoE Fulfilment
8:00AM-8:10AM | 2.5 | 90% | Underfitting
8:10AM-8:20AM | 4.0 | 98% | Overfitting
… | … | … | 
- 8:00AM-8:10AM
> Slice B : Scheduling 20% Radio Resource
- 8:10AM-8:20AM
> Slice B : Scheduling 50% Radio Resource
……
MDAS
RAN RRM(vendor implementation): Run-Time per slice Radio resource scheduling

## Slide 4: Slice QoE monitoring/QoE evaluation VS. Slice SLA KPI monitoring/SLA Evaluation
Slice QoE measured by CP | Source
Average Service MOS | Clause 6.4, TS 23.288-020
Number of Subscribers | Clause 6.32, TR 23.791
Percentage UEs’ experience satisfied | Clause 6.32, TR 23.791
5G NF
Mobile Pay
Autopilot
Vertical (URLLC)
NWDAF
Service MOS Measurement
Video
Data Collection
UE /QoS Flow Data
RAN
CN
Service MOS
NEF
Service MOS Requirement
e.g. More than 3.0
PCF
(QoS Adjustment)
OAM
OAM Data
UE MDT Data
CN Data
RAN Data
Trained Service MOS Model
Average Service MOS
Control Plane is responsible for Slice QoE monitoring/QoE evaluation
Service MOS measurement is already defined in Clause 6.4, TS 23288-020
Network Slice KPI measured by OAM | Source
Virtualised resource usage measurement | Clause 6.2, TS 28.552
Registered Subscribers of Network and Network Slice Instance through AMF | Clause 6.2.1, TS 28.554
Registered Subscribers of Network and Network Slice Instance through UDM | Clause 6.2.2, TS 28.554
Registration success rate of one single network slice instance | Clause 6.2.3, TS 28.554
End-to-end Latency of 5G Network | Clause 6.3.1, TS 28.554
Upstream Throughput for Network and Network Slice Instance | Clause 6.3.2, TS 28.554
Downstream Throughput for Single Network Slice Instance | Clause 6.3.3, TS 28.554
Upstream Throughput at N3 interface | Clause 6.3.4, TS 28.554
Downstream Throughput at N3 interface | Clause 6.3.5, TS 28.554
RAN UE Throughput | Clause 6.3.6, TS 28.554
Mean number of PDU sessions of network and network Slice Instance | Clause 6.4.1, TS 28.554
Virtualised Resource Utilization of Network Slice Instance | Clause 6.4.1, TS 28.554
OAM is responsible for Network Slice KPIs monitoring and Slice SLA evaluation

## Slide 5: Slice Run-Time stage – Slice QoE Fulfillment feedback to RAN (Open Discussion)
RAN
NSSF/PCF
(Slice QoE Evaluation)
CN
OAM (Slice SLA Evaluation + Cause Domain Determining)
3rd AF
⑤ New slice QoE
NWDAF
(Service MOS Measurement)
③ Query a Cell with poor Slice QoE
- Average Service MOS < 3
- Percentage UEs’ experience satisfied < 80%
② Cause Domain is RAN for the new slice
AMF
New Slice
Existing Slice
PCF
PCF
Service MOS
④ Slice QoE Fulfillment for a dedicated cell
Slice level resource configuration :
- Existing Slice A (high priority with SLA agreement ):
> Guaranteed: 10%
> Maximum: 50%
- New Slice B on trail (low priority)
> Guaranteed: 15%
> Maximum: 70%
- 8:00AM-8:10AM
> Slice B : Scheduling 20% Radio Resource
Slice QoE Fulfilment: Underfitting
- 8:10AM-8:20AM 2nd
> Slice B : Scheduling 22% Radio Resource
Slice QoE Fulfilment: Underfitting
…
- 8:10AM-8:20AM
> Slice B : Scheduling 50% Radio Resource
Slice QoE Fulfilment: Overfitting
- 8:10AM-8:20AM 2nd
> Slice B : Scheduling 45% Radio Resource
Slice QoE Fulfilment: Overfitting
…
……
  RAN schedule radio resource for the existing slice A in priority(with SLA agreement) compared to the new slice B on trial phase
MDAS
Slice QoE Requirement in 6.32, TR 23.791
- Network Area
- Average Service MOS per A
- Percentage UEs’ Service MOS satisfied
Time | Slice B Service MOS | Percentage UEs’ Service MOS satisfied | Slice B QoE Fulfilment
8:00AM-8:10AM | 2.5 | 90% | Underfitting
8:10AM-8:20AM | 4.0 | 98% | Overfitting
… | … | … | 
① new slice Service MOS Query (Network Area by Tenant)
RAN RRM(vendor implementation): Run-Time per slice Radio resource scheduling(for example)

## Slide 6: Slice Run-Time stage – Trail phase for the new slice (To be agreed in 3GPP)
Slice level resource configuration update
- Existing Slice A(high priority with SLA agreement):
> Guaranteed: 10%
> Maximum: 50%
- New Slice B on trail (low priority)
> Guaranteed: 15% ->20%
> Maximum: 70% ->80%
RAN
NSSF/PCF
CN
OAM (Slice Creation + Slice Resource Configuration)
NWDAF
AMF
New Slice
Existing Slice
PCF
PCF
CN Resource Configuration Update
3rd AF
Slice Resource Configuration Update
Radio Resource Configuration Update
(rRMPolicyRatio2=20%~80%)
  Only OAM can decide whether to update the slice resource configuration
⑤ New slice QoE (Service MOS)
MDAS

## Slide 7: Way Forward：
  Alternative A：
    Control Plane is responsible for Slice QoE evaluation while Management Plane is responsible for Slice SLA evaluation and cause domain determining
    NWDAF provides a service for slice QoE analytics that can be consumed by OAM and 5GC NFs and how these 5GC NFs can use such slice QoE analytics needs further study and will not be specified in Rel-16
    Whether RAN needs Slice QoE fulfillment analytics to perform more efficiently radio resource scheduling and how to do the adjustment will be discussed in R17.
  Alternative B:
    On top of Alternative A, it is further agreed:
      RAN needs Slice QoE fulfillment analytics to perform more efficiently radio resource scheduling
      The QoE analytics could be sent either from slice Control plane or Management plane, which will be studied/resolved in 3GPP SA2 and SA5 and will not be specified in R16
  Alternative C:
    On top of Alternative A, it is further agreed:
      Whether RAN needs Slice QoE fulfillment analytics to perform more efficiently radio resource scheduling is a valid question, which will be discussed in R17
  It is proposed to adopt Alternative A

## Slide 8
Thanks!

## Slide 9: Slice SLA related TDocs and Common Understandings
Slice SLA related TDocs
Common understandings
  The slice radio resource configuration parameters i.e. “Guaranteed/maximum slice radio resource” have already been defined by SA5, i.e. RRMPolicyRatio2 (including rRMPolicyMaxRatio, rRMPolicyMarginMaxRatio, rRMPolicyMinRatio, rRMPolicyMarginMinRatio) in clause 4.4.1, TS 28.541 v15.1.0.
  The slice QoE provided by NWDAF will benefit for slice radio resource configuration/adjustment by OAM.
 | China Mobile/Huawei | Samsung | Ericsson | Nokia
RAN3 |  |  |  | 
SA2 |  |  |  | 
SA5 |  |  |  |