## Slide 1: Discussion on Further Criteria for NWDAF Discovery and Selection Huawei, HiSilicon, Orange

## Slide 2
Background & Problem
Extracted from TS 23.288 (V0.3.0):
Extracted from CR 0987 for TS 23.501 revision3 - S2-1902556:
The need for further criteria for NWAF selection is motivated by factors included in TS 23.288:
Possibility of different NWDAF deployment alternatives (Clause 4.1)
NWDAF needing to generate analytics for Areas of Interest requested by consumer of analytics (Clause 6.6)
Problem
Assuming a scenario of multiple NWDAFs with some NWDAFs with the same analytics ID:
How can a consumer of Network Performance Analytics ID discovery the NWDAF that can provide analytics for the “are of Interest” required by the consumer of such analytics?

## Slide 3
Details of Problem
B
A
CR 0987 for TS 23.501 (S2-1902556) defines only S-NSSAI and Analytics ID as information for selection.
  Information is not enough to allow consumer to identify the criteria to select a NWDAF that can serve the analytics information
In case of multiple NWDAFs supporting the same analytics ID, consumers can rely on criteria related to generic description of NFs, such as load of NF
  In this case, this criteria will not help, because even if NWDAF#1 and #2 provide the same analytics ID, they do not support the same area of interest
  This will lead to increase in rejection signalling.

## Slide 4
Need for Further Criteria for NWDAF Discovery and Selection
Consumers of NWDAF analytics should be able to select NWDAF also based on the Analytics Serving Area
Analytics Serving Area defines the area of interest (or a set of area of interest) that can be covered by analytics generated by a NWDAF
  Analytics Serving Area information is identified by:
    List of TAIs : Aligned with interpretation of area of interest defined in TS 23.501 Clause 5.3.4.4 (“The Area Of Interest is represented by a list of Tracking Areas, list of cells or list of (R)AN node identifiers”)
City B
City A

## Slide 5
Thanks!