## Slide 1: Discussion of SA Only Network Support Roaming Users from NSA Network
China Mobile

## Slide 2: Scenario to be Addressed: NSA&SA dual mode UE
5G NR
LTE
EPC+
Interworking
Function
5GC
5G NR
HPLMN
VPLMN
SA (option 2) only network support NSA&SA dual mode UE, with NSA (option 3) as HPLMN
The requirement cam from GSMA (S2-180019/S2-178937)
  GSMA NG SIGNAL would like to ask clarification on how the roaming interworking is envisaged between 5G networks with NGC and 5G networks with EPC.

## Slide 3: Discussion
Similar problem has been done by CT4 in R8
  TS 29.305 “InterWorking Function (IWF) between MAP based and Diameter based interfaces”
  It is not deployed in real network
Motivation: the Option 3 to 2 roaming is important in view of
  Both Option 3 and Option 2 are considered as “5G”. Roaming support rely on 4G may limit the user experience
  Option 2 only operator (either deployed in the initial phase or migrated, e.g., from Option 3) may want to support inbound 5G roaming users from NSA, which may exist for some period in some market

## Slide 4: Roaming Requirement has been Discussed but not Addressed Yet
SA2 has discussed such scenario and replies GSMA (S2-180810)
  Recognises that the different nature of 5GC and EPC, and the expected difference from protocol perspective, may demand an interworking function to be deployed when roaming agreements are expected between networks with different stand-alone core network deployments.
  Strongly recommend GSMA analysing the different architectures of the Core Networks, i.e. SBA in 5GC versus point-to-point interfaces in EPC, when addressing any potential interworking function as well as comparing the 5GS and EPS roaming interfaces to identify what mapping may be possible and what additional functionality and information a potential interworking function may need to provide.
  Draw GSMA attention to the Security Edge Protection Proxy (SEPP), that introduces functionality for topology hiding, message filtering and policing of inter-PLMN control plane interfaces.
It is therefore, however, the solution still missing
Our understanding is that such work shall mainly be done by CT4

## Slide 5: Proposals
Address the problem in R16: investigate the solutions, applicability, and defines interworking functions
The solution shall avoid impact to UE, RAN, existing 5G NF and EPC
The main work be done by CT4 and SA3. SA2 shall be informed if any alignment on the architecture is required
SA2 send LS to CT4 and SA3 as above