## Slide 1: Making S6b Optional for ePDG connected to 5GS
Cisco Systems

## Slide 2: Proposal
Rel-15 Architecture
Rel-16 Proposal
S6b may not be used in all deployments
When S6b is not used, registration of PGW-C occurs via N10

## Slide 3
AAA
AAR(IMSI,APN,PGW-FQDN)
(i.Authorize PDN and ii.Transfer
PGW add to HSS)
SAA(APN Configuration Data)
Create Session Request
ePDG
SMF+
PGW-C
AAA
UDM+
HSS
SAR(IMSI,APN,PGW-FQDN)
Is user Authorized
For the APN?
Create Session Response
Nudm_SDM_Get Request
(i.Fetch SM Subscription Data)
Create Session Request
ePDG
AAA
Create Session Response
Nudm_SDM_Get Response
(SessionManagementSubscriptionData)
Nudm_UECM_Registration Response
Create Session with S6b
Create Session with N10
A new IE ‘Indication about ePDG access’ is proposed in Nudm_UECM_Registration Request.
Presence of this IE would enable UDM+HSS to suppress notification of updated APN and PDN GW identity information to the AAA Server.
Nudm_UECM_Registration Request
(ii.PGW FQDN, P-CSCF Rest. Notif. URI,
Indication about ePDG access)
SMF+
PGW-C
UDM+
HSS
Flow-1: Registration of PGW-C in HSS+UDM
Is user Authorized
For the DNN/APN?

## Slide 4
STR
Delete Session Request
ePDG
AAA
Delete Session Response
STA
STR
STA
SAR
SAA
Nudm_UECM_DeRegistration Request
Delete Session Request
ePDG
AAA
Delete Session Response
Nudm_UECM_DeRegistration Response
STR
STA
SAR
SAA
Delete Session with S6b
Delete Session with N10
Only if last PDN
Only if last PDN
SMF+
PGW-C
SMF+
PGW-C
UDM+
HSS
UDM+
HSS
Flow-2: De-Registration of PGW-C in HSS+UDM
PDN Disconnection with UE
PDN Disconnection with UE
Notes: 29.273 is for the ePD to also inform the AAA:
The SWm reference point allows the ePDG to inform the 3GPP AAA Server/Proxy about the termination of an IKE_SA between UE and ePDG, and that therefore the mobility session established on the ePDG for all associated PDN connections are to be removed.
The SWm Session Termination Request procedure shall be initiated by the ePDG to the 3GPP AAA Server which shall remove associated non-3GPP Access information.
Between ePDG and AAA: One diameter session per PDN Connection of the UE (IKEv2 session).
Between AAA and HSS: Not session based, but transaction based. AAA contacts HSS+UDM on UE’s first PDN connection and gets all subscription data. It then only updates info at HSS (eg. PGW address).
Finally after all Diameter sessions on Swx, S6a are removed, the AAA de-registers with the HSS.

## Slide 5: Some other details (no impact to standards)

## Slide 6: P-CSCF Restoration
HSS + UDM
MME
ePDG
SMF+PGW-C
AMF
3GPP
Non- 3GPP
SGW
AAA
N10
S6a
SWx
5G
4G
S6b
S-CSCF
1. Cx: P-CSCF Restoration Indication
IMS PDN connection
2. HSS+UDM determines if the IMS PDN connection is via N10 or SWx or S6a
3. P-CSCF Restoration Indication
HSS + UDM
MME
ePDG
SMF+PGW-C
AMF
3GPP
Non- 3GPP
SGW
AAA
N10
S6a
SWx
5G
4G
S-CSCF
1. Cx: P-CSCF Restoration Indication
IMS PDN connection
2. HSS+UDM determines if the IMS PDN connection is via N10 or SWx or S6a
4. P-CSCF Restoration Indication
Same Logic as in Rel-15
REL-15
Proposed REL-16

## Slide 7
ePDG
AAA
Delete Bearer Request
PPR(P-CSCF Rest. Ind.)
Nudm_UEContextManagement_P-CSCF-RestorationNotification
Delete Bearer Request
ePDG
AAA
P-CSCF Restoration with S6b
P-CSCF Restoration with N10
SMF+
PGW-C
SMF+
PGW-C
UDM+
HSS
UDM+
HSS
RAR(P-CSCF Rest. Ind.)
UDM+HSS is aware that PDN connection
is over N10. This is existing HSS+UDM functionality
Existing REL-15 Procedures
23.380, Clause 5.8.4.2 Trigger P-CSCF Restoration Procedure via SMF
NOTE: After receiving the Cx SAR message, the HSS forwards the P-CSCF restoration indication to the UDM internally. The deployment variation of HSS and UDM is out of scope, and the interaction between HSS and UDM is implementation specific.