## Slide 1: RACS-PLMN-assigned capability ID deletion
3GPP TSG-SA WG2 Meeting #133 S2-1905141
May 13 - 17, 2019, Reno, USA

## Slide 2
It has already agreed that “The UE shall delete the PLMN-assigned UE Radio Capability ID(s) for the related PLMN upon receiving an indication from this PLMN”.
In the last SA2 meeting, S2-1903803 additionally proposed the condition: under the condition that the UE also has a manufacturer-assigned ID for the same set of UE radio access capabilities.
  This condition allows only the UE belonging to a specific manufacturer deletes the PLMN-assigned UE Radio Capability ID and revert to the manufacturer-assigned ID. But it bring some complexity for UE behavior.
  The purpose of deleting the PLMN-assigned capability ID is left to UCMF implementation, does not need to be specified.
Proposal 1: Stick to the agreement: The UE shall delete the PLMN-assigned UE Radio Capability ID(s) for the related PLMN upon receiving an indication from this PLMN.

## Slide 3
In the last SA2 meeting, S2-1903217 the procedure for indicating UE deleting the PLMN-assigned capability ID as following:
  - The AMF notifies the UE via NAS message
    The AMF does not need to notifies the UEs immediately.
    The AMF can notify the UE using e.g. UCU, next Registration procedure.
  UEs are not required to go back to IDLE mode or deregistration when deleting the ID(s).
Proposal 2: AMF notifies the UE via NAS message, e.g. UCU, next Registration. UE does not required to go back to IDLE mode or deregistration when deleting the ID(s).