## Slide 1: 3GPP TSG-SA WG2 Meeting #134 S2- 1907040 Sapporo, Japan, 24 - 28 June, 2019 Source: Ericsson Title: Nudr_DM evolution Document for: Discussion Agenda Item: 6.5.11 Work Item / Release: TEI16, 5GS_Ph1
Abstract of the contribution: This document proposes to identify whether there is any constraint or limitation for the Nudr_DM evolution, and if so, indicate what will be the most reasonable way forward to include new data that do not belong to the existing Data Sets.
Ericsson
2019-06-12

## Slide 2: Partitioning based on Group Ids Rel-16 status (I)
Following NFs are considered to support partitioning: UDR, UDM and AUSF.
In last SA2 meeting (SA2#133) (eIMS related), SBI interface is added for HSS and it may be partitioned.
  New definition of HSS-IMS Group Id and extension of existing mechanism (for other NFs that support partitioning)
23.501 v16.0.2 clause 6.2.6 (definition of NF profile in NRF), includes the following text:
  NOTE 5: It is also expected that the NRF stores a mapping between UDM Group ID and SUPI(s), UDR Group ID and SUPI(s), AUSF Group ID and SUPI(s), to enable discovery of UDM, UDR, AUSF using SUPI, SUPI ranges as specified in clause 6.3.
How individual subscriber identities mapping to Group Id is provided?
  At NF (UDM, UDR, AUSF, HSS) registration
  Provisioned in NRF directly

## Slide 3: Partitioning based on Group Ids Rel-16 status (II)
NRF proprietary access to mapping from individual subscriber identities (SUPI/GPSI/IMPI/IMPU) to Group Id
Proposed solution:
  Define the individual subscriber identities mapping to GroupId as new standard data.
This data is defined as a new Data Set in UDR:
  It fits logically UDR, as long as this DB is meant to be extensible to incorporate new data (U: Unified)
  UDR already includes different types of data, even not subscription data (i.e. Application Data).
  As long as it is defined in a new DataSet it can be deployed independently of any other data in UDR.
  There are no reasons to question that Nudr as defined will not be valid, i.e. using HTTP/REST is accepted.
  For a functional perspective, there is no reason to consider any other entities in the network to hold this data.

## Slide 4: Partitioning based on Group Ids Rel-16 status (III)
A new Nudr Service is defined: Nudr_GroupIdmap, however there is no reason from stage2 perspective to do so.
  What does it imply? Every new data to be standardized will need a new service definition?
  This is against SBI, that are expected to be extensible, when same functionality is offered.
Existing Nudr_DM service provides all that is required:
  It already supports access to data in multiple Data Sets.
  It already supports all operations required to access any data (CRUD operations).
  It is defined to support extensibility of new data (in existing Data Sets), but as well new Data Sets.
  It is the natural way of adding new standard data, except it is not expected that UDR

## Slide 5: Partitioning based on Group Ids Rel-16 status (IV)
Stage 3 Nudr_DM extensibility:
  Versioning
    Per service
    Version will be incremented whenever there is a (non)backward compatible change in any of the functionality related to any of the data sets.
    Well documented in stage 3 TS 29.501. Nothing special here (just that the data sets are documented separately in different TSs and that the versioning of the API is included in the generic TS, but this is a documentation task).
  Feature control:
    Per resource within a specific data set, as the features are negotiated when the related resource is created.
    The feature names are documented in the same TS 29.504

## Slide 6: Partitioning based on Group Ids Proposed way forward
In our view, Nudr_DM is extensible and supports what is required by the GroupId mapping. At stage 2 there is not any identified limitation, then, if there is any, it should be identified at stage 3.
Proposal
  Send an LS OUT (S2-1907039) to CT4 and CT3, requesting the following:
    Evaluate Nudr_DM extensibility limitations/constraint and make a decisión on whether a new service for the GroupId mapping data is required, or on the contrary, Nudr_DM may be extended.
    Evaluate if any existing limitation/constraint determines Nudr_DM Service will not further evolve to include data for new Data Sets, just data for existing Data Sets.
  Update TS accordingly, see proposed CR 1481 and CR 1490 where service Nudr_GroupIdmap is removed.