## Slide 1: 5WWC IPTV solutions
S2-19xxxx Rapporteour

## Slide 2: S2-1906892 discussion/ S2-1906891 CR (Juniper Networks)
Principles
separate IGMP/PIM module, and to apply the multicast access control inside the IGMP/PIM module.
the SMF could directly pass the access control rules to the UPF, to be applied inside the IGMP module instead of in the forwarding path.
PDR for IGMP and PIM
When UPF detects UL the IGMP/PIM join messages via the PDU Session message sends the messages to a local module responsible for the IGMP/PIM protocol
The local module determines if the IGMP join request is allowed or not according to the multicast access control list it received from SMF
The proposal is to make it generic for Multicast.
The DL “PDR/FAR” for multicast packets to the destination are generated internally by UPF fr implementation and NOT by SMF
UPF acting as a IP Multicast Router
Preview of TV is managed by internal module

## Slide 3: S2-1906892 discussion/ S2-1906891 CR (Juniper Networks)
5G-RG1
5G-RG2
FAR
PDR
“multicast interface”
SMF
interface
N6
FAR
PDR
N4 session 6
IGMP Join/PIM
multicast Access
control list
PDU session
FAR
PDR
UL
“FAR”
“PDR multicast address”
DL
PD/ FAR for sending IGMP
to internal module
It is assumed that
traffic goes
to the “multicast Interface”
Per internal definition
FAR
PDR

## Slide 4: S2-1907379 CR (Nokia)
The SMF sent to the UPF acting as PSA N4 rules, PDR, FAR,.. related with the allowed IPTV services
IGMP to UPF.
UL PDR for detecting IGMP
FAR associated to the UL PDR is used to accept the IGMP
Local table is create by UPF to manage the replication N4 of the needed traffic, in order to associated the DL FAR and it is left for implementation.
All DL FAR/PDR are creates by SMF based on Access List for all possible multicast traffic that UE can received.
Replication matching based on IGMP is done internal process left to implementation
UPF acting as a IP Multicast Router
PCRT (Policy Control Request Trigger) to report if a UE join/leave a IP multicast group
Preview is managed by PCRT notification message toward SMF for authorization
Manage only 1 group per IGMP message

## Slide 5: S2-1907379 CR (Nokia)
5G-RG1
5G-RG2
FAR
PDR
SMF
FAR
PDR
N6
FAR
PDR
IGMP Join/PIM
PDR/FAR multicast control list
PDU session
FAR
PDR
UL
FAR
PDR
DL
FAR
PDR
FAR
PDR
FAR
PDR
FAR
PDR
FAR
PDR
FAR
PDR

## Slide 6: S2-1907123 discussion, S2-1907124 CR (Huawei)
The IPTV multicast solution use comment part with 6G LAN multicast/broadcast
Used internal module for packet replication
IGMP is managed by SMF which generates the FAR/PDR

## Slide 7: S2-1907123 discussion, S2-1907124 CR (Huawei)
5G-RG1
5G-RG2
PDU session
N4 session 1
FAR
PDR
FAR
PDR
Internal interface
SMF
Internal interface
FAR
PDR
N6
FAR
PDR
FAR
PDR
N4 session 6
IGMP Join
PDR/FAR
FAR
PDR
UL
FAR
PDR
DL