## Slide 1
Vertical_LAN
TSC drafting session
TSC drafting session
Devaki Chandramouli
14-10-2019

## Slide 2
Bridge Management / LLDP Agent Support related papers
S2-1909068 | DISCUSSION | Agreement | Completing Ethernet port management | Qualcomm Incorporated
S2-1909069 | CR | Approval | 23.501 CR1747 (Rel-16, 'F'): Addressing open issues for Ethernet port management | Qualcomm Incorporated
S2-1909070 | CR | Approval | 23.502 CR1729 (Rel-16, 'F'): Addressing open issues for Ethernet port management | Qualcomm Incorporated
S2-1909731 | CR | Approval | 23.501 CR1885 (Rel-16, 'F'): 5GS Bridge Management | Nokia, Nokia Shanghai Bell
S2-1909506 | CR | Approval | 23.501 CR1832 (Rel-16, 'F'): Address editor's notes on DS-TT topology discovery | Huawei, HiSilicon
S2-1909427 | CR | Approval | 23.501 CR1814 (Rel-16, 'F'): Resolving the EN on the TT port neighbour discovery configuration | ZTE
S2-1909428 | CR | Approval | 23.502 CR1805 (Rel-16, 'F'): clarification on the DS-TT port neighbour discovery | ZTE
S2-1909396 | DISCUSSION | Agreement | General port model of the 5G bridge | Ericsson
S2-1909397 | CR | Approval | 23.501 CR1803 (Rel-16, 'F'): Port model of the 5G bridge | Ericsson
S2-1909398 | CR | Approval | 23.502 CR1802 (Rel-16, 'F'): Updates for port modeling of the 5G bridge | Ericsson
S2-1909204 | CR | Approval | 23.501 CR1779 (Rel-16, 'B'): Clarification on Port management information exchange in 5GS | Samsung Electronics Polska

## Slide 3
Bridge Management, LLDP Agent support
Open Issue #1 – Should LLDP agent be supported in the DS-TT, NW-TT or both?
Editor's note: Whether both DS-TT and NW-TT or only NW-TT support Link layer connectivity discovery and reporting is FFS.
Option #1: Standards allows LLDP agent support in NW-TT only (S2-1909068-70 - QCOM) –
Supportive: E///, QCOM, Mediatek, Vivo
Objection: Huawei?
Option #2: Standards allows LLDP agent support in either DS-TT or NW-TT (S2-1909506 - HUA, S2-1909731 – Nokia, S2-1909204 - Samsung, S2-1909427-28 – ZTE)
LLDP agent is Mandatory in NW-TT and DS-TT
Supportive: ZTE, HUA, Tencent, CATT
Objection: QCOM, Ericsson, Mediatek,
Option #3: Mandatory in NW-TT for both sides and optionally in DS-TT.
Supportive: Samsung
Objection: None
Way forward:
- Current working assumption – Option 3/mandatory to support LLDP agent in NW-TT, Optional to support LLDP agent discovery in DS-TT.

## Slide 4
Ability of TSN AF to write DS-TT and NW-TT port neighbor discovery config
Open issue #2:
Clause 5.28.3.1:
Editor's note: Whether TSN AF can write DS-TT and NW-TT port neighbour discovery configuration is FFS.
Editor's note: Whether TSN AF needs to be able to read port management information and needs to be able to get port management capabilities is FFS. […]
Option #1: The ability of TSN AF to write DS-TT and NW-TT port neighbour discovery configuration is essential to enable 5GS TSN bridge operators to provide the LLDP agent in DS-TT/NW-TT with their preferred local LLDP configuration. (S2-1909068-70 - Qualcomm, S2-1909204 - Samsung, S2-1909731 - Nokia)
Option #2: ??
Way forward: Option #1

## Slide 5
Bridge Model and uplink PDU Session identification related papers
S2-1908939 | CR | Approval | 23.502 CR1699 (Rel-16, 'F'): Support for multiple ports on one DS-TT within one PDU Session | Huawei, Hisilicon
S2-1909399 | DISCUSSION | Agreement | Two 5GS bridge model interpretations | Ericsson
S2-1909400 | CR | Approval | 23.501 CR1804 (Rel-16, 'F'): 5GS bridge model interpretation | Ericsson
S2-1909737 | CR | Approval | 23.501 CR1891 (Rel-16, 'F'): Addressing unique identification of PDU Session in the uplink | Nokia, Nokia Shanghai Bell
S2-1909429 | DISCUSSION | Discussion | Discussion on configuration and scheduling on the 5G virtual bridge | ZTE
S2-1909430 | CR | Approval | 23.501 CR1815 (Rel-16, 'F'): clarification on the Qos parameters mapping and TSCAI creation | ZTE
S2-1909431 | CR | Approval | 23.502 CR1806 (Rel-16, 'F'): clarification on the Qos mapping, TSCAI creation and 5GS Bridge configuration | ZTE
S2-1909403 | DISCUSSION | Agreement | Solving EN on UL configuration issue | Ericsson
S2-1909404 | CR | Approval | 23.501 CR1807 (Rel-16, 'F'): CR for UL configuration issue (missing) | Ericsson
S2-1909401 | CR | Approval | 23.501 CR1805 (Rel-16, 'F'): Addressing EN on Traffic Forwarding | Ericsson
S2-1909202 | CR | Approval | 23.501 CR1777 (Rel-16, 'B'): Clarification on QoS parameters mapping for 5GS Bridge configuration | Samsung Electronics Polska

## Slide 6
Bridge Model and uplink PDU Session identification
Open issue #3:
Number of PDU Sessions supported per DS-TT port
Option #1: Many ports per DS-TT per UPF (S2-1908939 - HUA)
Option #2: Unique PDU Session per port per DS-TT. (S2-1909400 – E///, S2-1909737 - Nokia)
Way forward:
- One PDU Session support per DS-TT port.