## Slide 1: 5G Virtual Networks
Jeffrey Zhang
Juniper Networks

## Slide 2: 5G-VN
From 3GPP 23.501 (5G System Architecture):
  5G LAN-Type Service: A service over the 5G system offering private communication using IP and/or non-IP type communications.
  5G LAN-Virtual Network: A virtual network over the 5G system capable of supporting 5G LAN-type service.
A 5G-VN can be based on IP, Ethernet, or unstructured PDU
  23.501 Clause 5.6.10.1: Support of IP PDU Session type
  23.501 Clause 5.6.10.2: Support of Ethernet PDU Session type
  23.501 Clause 5.6.10.3: Support of Unstructured PDU Session type
At service level, 5G-VN for IP/Ethernet is no different from IP/Ethernet-VPN in fixed networks

## Slide 3: IP/Ethernet-VPN in Fixed Networks
PEs (Provider Edges) and P-Tunnels (Provider Tunnels)
CEs (Customer Edges) and PE-CE Interfaces or ACs (Attachment Circuits) in case of E-VPN
RFC2547/4364 for IP-VPN
  BGP for IP route exchange
  PE-CE interfaces bound to VRFs (routing instances)
  MPLS P-Tunnel
    VPN label stacked on top of Tunnel label
RFC4761/4762 for VPLS
RFC7432/8365 for E-VPN
  BGP for mac route exchange
  ACs bound to BDs (Bridge Domains)
  MPLS/VXLAN P-tunnel
  BD-identifying label/VNI
RFC7348 for VXLAN
  E-VPN w/o BGP
  Data plane mac learning on P-tunnels as well as on ACs
  VXLAN P-tunnel
PE1
CE4
CE3
CE1
CE2
PE3
PE4
PE2

## Slide 4: 5G-VN IP/Ethernet
Service is just like IP/Ethernet-VPN
  PE <--> UPF
  CE <--> UE
  Wired PE-CE interface <--> 5G PDU Session
  P-Tunnel <--> GTP-U
  VPN label/VNI <--> GTP TEID
Multiple UPFs may be used so that UEs nearby can communicate more efficiently w/o traffic tromboning
Implementation is SDN-like approach
  SMF (Session Management Function) acts like an SDN controller, programs forwarding state on UPFs
    PDR <--> Route Key; FAR <--> Forwarding Nexthop
    This is very much like OVSDB VXLAN (see later slides)
UPF1
UE4
UE3
UE1
UPF3
UPF4
UPF2
UE2
SMF

## Slide 5: Ethernet-VPN for Fixed Networks
Besides/before RFC7432 BGP EVPN there are three other options
  VPLS (RFC4761/4762)
  VXLAN with OVSDB
    Limited scale for DC vSwitches
    Similar to current 5G-VN approach – mac routes programmed from controllers
  RFC7348: VXLAN with mac learning on both ACs and P-tunnels
    Same has been proposed for 5G-VN Ethernet (S2-1905197/S2-1905681)
BGP-signaled EVPN (RFC7432) is designed for better scale and convergence
  All-Active and Active-Standby multi-homing
  Proactive mac routes advertisement and fast convergence mechanisms
  Mac mobility
  Wide range of P-tunnel types
  Lots of optional enhancements/extensions for various scenarios

## Slide 6: 5G-VN Enhancement Study Item S2-1906725
Enhancement of 5G VN group management:
  Whether there is a need to support and how to support 1: N mapping between DNN and 5GLAN group, where a UE can belong to multiple 5GLAN groups at the same time under the same DNN.
  Support fast configuration of a 5G VN group and potential improvements related with 3rd party configuration of a VN group.
  More efficient support of a large 5G VN group involving multiple N19 tunnels
  Whether and how to improve reliability of 5G VN group sessions by removing the restriction of at most a single SMF Set per 5G VN.
Enhancement of 5G VN group communication:
  Whether and how to support additional user plane efficiency for 5G VN group communication (e.g. due to UE mobility, I-SMF existence )
  Study potential improvements on packet routing and forwarding to support broadcast and multicast communications

## Slide 7: Integration of IP/E-VPN into 5G?
IP/E-VPN technologies are mature and widely deployed by SPs
  Most providers have both fixed and wireless network
    Would be good to use the same technology for the same service
IP/E-VPN for fixed network can be seamless integrated into 5G-VN
  3GPP protocols and procedures establish IP/Ethernet PDU sessions from UEs to appropriate VRFs/BDs on UPFs
  The rest is taken care of by existing IP/E-VPN protocols and procedures
    This can be augmented by the existing SMFUPF centralized control based on PDR/FAR
  This also enables the same service across both wireless and fixed network seamlessly
With the integration, many enhancements in the study item are pretty much already covered
  All features and future enhancements of IP/E-VPN are also available to 5G
    E.g. E-Tree (RFC8317), multi-homing, multicast/broadcast, etc.
  IEEE-compatible Ethernet Service as discussed in S2-1905040 is also achieved (proposal 7)

## Slide 8: The Multicast/Broadcast Example
Discussions on multicast/broadcast support in 5G-VN are just started
  But well understood and supported/specified in IP/E-VPN – applicable to 5G-VN as is
Optimizations/features at overlay/service level
  Sending traffic only to interested local CEs/UEs
  Sending traffic only to PEs/UPFs with interested local CEs/UEs
  Sending traffic via helper PEs/UPFs (Assisted Replication)
  Extranet (one member belonging to multiple VPNs/VNs), Hub & Spoke, etc.
  In EVPN case, Optimized Inter-Subnet Multicast (OISM)
Optimizations in the underlay
  Efficient replication via intermediate P routers
    Using PIM/P2MP tunnels, which require per-tunnel state on P routers
  Ingress Replication to all/certain PEs/UPFs
    No per-tunnel state on P routers, but replication is not efficient
  BIER - a new multicast technology that enables efficient replication w/o per-tunnel state
All these overlay/underlay optimizations for IP/E-VPN can be applied to 5G-VN as is

## Slide 9: Example 1: A VN across Wireless/Fixed Networks
An existing BGP-EVPN with members initially only on fixed side
New members are added on wireless side
  There could even be multi-homed CE/UE
CE/UE/VN management can be completely independent on wireless and fixed side
  3GPP procedures do not care about fixed side CEs/PEs
  As long as BDs are provisioned with common Route Targets on UPFs and PEs
The UPFs and PEs exchange BGP EVPN routes to automatically discover each other and set up forwarding state
  Because of the common Route Targets
  Assuming 5G CN and fixed side provider network can talk to each other
Note – this does not even involve 5WWC procedures
PE1
UE3
CE4
CE1
CE2
PE4
PE3
PE2
UPF1
UE4
UE1
UPF3
UPF4
UPF2
UE2
SMF
Provider Network
on Fixed Side
5G CN
LAG

## Slide 10: Example 2: VNs for A Large Enterprise Customer
Consider the following:
  Each department has its own Ethernet Bridge Domain and corresponding IP subnet
    Each could span multiple sites
  Intra-dept communication is intra-subnet IP routing
  Inter-dept communication is inter-subnet IP routing subject to firewall control
This is already supported on fixed networks via IP/E-VPN
  With various unicast/multicast features/optimizations
Now add wireless network into the picture
  A group member could be a 3GPP UE or fixed network CE
    3GPP only responsible for PDU sessions
    UPFs act as IP/E-VPN PEs, interacting with others (UPFs and fixed network PEs)
  One L2 DNN for each BD (that has 3GPP UEs)
  One IP DNN for the customer

## Slide 11: Summary
Service: 5G-VN service is no different from existing IP/E-VPN service
Technology
  Existing IP/E-VPN technologies are applicable to 5G-VN
  Same implementation from a vendor can be used for both
    IP/E-VPN are supported by all major vendors (Juniper, Cisco, Nokia, Ericsson, Huawei)
Deployment
  Same technology and implementation can be deployed for both
    MNOs already deploy IP/E-VPN for backhaul
  Same 5G-VN group can be seamlessly deployed across wireless and fixed network
Future development
  Any advancement/enhancement in IP/E-VPN will be available to 5G-VN

## Slide 12: Backup Slides for Details
S2-1903312 (Nokia) - 5G LAN group communication with UPF autonomous traffic forwarding
S2-1905681 (Huawei) - Discussion on 5G VN group communication
How existing fixed network IP/E-VPN solutions relate to the above two documents
An example virtual network with members on wireless and fixed network side

## Slide 13: S2-1903312: Current PFCP Model
Figure 1 – Current PFCP model for 5G LAN Group Communication
UE Session UL PDR: send all traffic to local switch
UE Session DL PDRs: send traffic from local switch to UE if dst MAC address matches
Group Session DL PDR: send all traffic to local switch
Group Session UL PDRs: send traffic from local switch to remote UPF if dst MAC address matches
These PDRs need to list MAC addresses associated with a UE or a remote UPF
A UPF first reports MAC addresses to SMF
  E.g. (mac1, UE1) & (mac2, UE2)
SMF programs UPFs with PDRs/FARs
  (mac1, UE1) & (mac2, UE2) PDRs/FARs back to UPF1
  (mac1, UPF1) & (mac2, UPF1) PDRs/FARs to UPF2
  The PDR/FAR programming may be:
    Proactive: as soon as SMF learns the MAC addresses
    Reactive: until UPF reports that it receives a packet with an unknown dst MAC address
  Large number of SMF-UPF interaction leads to scaling & convergence concerns

## Slide 14: S2-1903312 Proposal
Self programming of PDR/FAR w/o SMF interaction
  When a MAC address is learned from a UE/UPF, automatically program corresponding PDR/FAR to forwarding corresponding traffic
    MAC learning is based on the source MAC of received traffic
Flooding traffic whose destination MAC is unknown to other UPFs
  Unless it is already from another UPF
    As indicated by an GTP-U Extension Header
  A PDR/FAR is programmed by the SMF to flood traffic with unknown MAC
    A “default” mac address to match all unknown MAC addresses
    An FAR that lists all other UPFs as target
This is very much like how VXLAN works, except:
  VXLAN tunnel vs. GTP-U
    No need for an indication that traffic is from another VTEP (UPF) – it is implicit knowledge
    VXLAN tunnel could be multicast
  Flooding could also be locally controlled w/o “SMF”
    Other VTEPs auto-discovered by a multicast tunnel, or per local provisioning
  Traffic with unknow mac is also flooded CEs (UEs)

## Slide 15: Comments about S2-1903312 Proposal
Existing technology/implementation can be used as is for 5G-VN
  As long as 3GPP procedures establish the UE-UPF PDU session and anchor it to a “local switch”
  Either GTP-U tunnels or non-3GPP tunnels could be used
  Notice that BGP does not have to be used here
Say mac2 is associated with UE2 attached to UPF2. Before a packet with source mac2 is received from UPF2, mac2 is unknown on local UPF1 and a packet with destination mac2 will have to be flooded to all UPFs (even though mac2 is already known to UPF2)
  Huawei’s S2-1905681 discusses a solution for this (proposal #3 in S2-1905681)

## Slide 16: S2-1905681
Three proposals:
Same local switch concept as in Nokia’s S2-1903312
  w/o mac learning – rely on PDF/FAR from SMF
Procedures to handle mobility
  E.g. UE3 moves to the UPF on the right
Mac learning w/o SMF interaction
  Including proactively propagating to other UPFs, which is not covered in Nokia’s doc
  However Huawei does not endorse this proposal
Proactive propagation of MAC addresses among UPFs
When a UPF first learns a mac address from its UE, it constructs a broadcast packet and floods to all UPFs
  Source mac is the newly learned
  With an “self learning” indication
When another UPF receives this “self learning” packet, it learns the mac address and discard the packets

## Slide 17: Comments about S2-1905681’s Proposal 3
The proposal addresses the following problem in Nokia’s VXLAN-like solution
  Say mac2 is associated with UE2 attached to UPF2. Before a packet with source mac2 is received from UPF2, mac2 is unknown on local UPF1 and a packet with destination mac2 will have to be flooded to all UPFs (even though mac2 is already known to UPF2)
The problem is a valid problem
  Not clear why Huawei does not endorse the proposal
    Or is it just that Huawei does not endorse the particular way of proactive propagation?
It has been addressed in RFC7432 EVPN in a better way
  BGP signaling proactively advertises locally learned MAC addresses to PEs/UPFs

## Slide 18: Observations
Are we repeating the concepts/solutions existent for fixed network IP/E-VPN?
  Local-switch, MAC learning, proactive MAC propagation among UPFs
Would more repetition come?
  Multicast/broadcast handling/optimization
  Features like multi-homing, E-Tree, Hub & Spoke, Extranet, etc..
Integrating existing fixed network IP/E-VPN solution into 3GPP saves effort on every front
  Standardization
  Vendors’ implementation
  Operators’ deployment & operation

## Slide 19: Some Details for Reusing IP/E-VPN Solutions
3GPP procedures
  N1/N2/N3/N4: Establish UE-UPF PDU sessions
  N4: Anchor UE-UPF PDU sessions to corresponding VRFs/BDs
    Implementation-wise, these PDU session show up as PE-CE interfaces in VRFs/BDs
Existing IP/E-VPN procedures
  Data forwarding to/from UEs/UPFs based on IP/MAC routes in VRFs/BDs
  Without BGP: data-driven mac learning (similar to Nokia’s proposal)
  With BGP: IP/MAC routes propagation among UPFs
  All existing/future IP/E-VPN features/optimizations will apply to 5G-VN
Additional SMF-driven centralized control can still be applied
  Via PDR/FAR mechanisms