## Slide 1
S2-1911229
Introduction of the Inter PLMN UP functionality in the architecture / UPF Dedicated to IPUPS

## Slide 2
UPF Dedicated to IPUPS acting as GTP-u switch or as GTP-u pass-through?
If IPUPS is GTP-u switch (top figure), the UPF sends traffic targeting (F-TEID) to one IPUPS that is controlled to modify the target F-TEID to target the remote UPF
  All traffic of the PDU Session go via the same IPUPS which can have stateful FW capabilities
Otherwise (bottom figure)
  The UPF sends traffic targeting (F-TEID) the remote UPF
  All IPUPS need to be configured when a new PDU Session is created / released (modified)
  If stateful IPUPS FW capabilities are needed, IP routing capabilities (on both side of the IPUPS(s)) need to ensure that the same IPUPS handles the traffic of a PDU Session
SMF
UPF
IPUPS 3
Remote UPF
IPUPS 1
IPUPS 2
N4
IP
IP
N4
Local PLMN
SMF
UPF
IPUPS 3
Remote UPF
IPUPS 1
IPUPS 2
N4
IP
IP
N4
Local PLMN

## Slide 3
IPUPS Inter PLMN UP Security functionality
3GPP introducing (S2-1910799) the IPUPS Inter PLMN UP Security functionality as a UPF functionality. This is meant to be a GTP-u FW at inter PLMN border. It is controlled by N4
Could be deployed
Integrated with other UPF functionalities (PSA in H-UPF, within V-UPF)
As UPF(s) dedicated to the IPUPS functionality (shown below)