## Slide 1: 5QI values for efficient handling of congestion control marked IP packets
Ericsson, Sprint, Google, Nokia Networks, AT&T, Vodafone
Agenda 9.1
S2-1911250

## Slide 2: Outline
Introduction/abstract L4S (Low Latency Low Loss and Scalable throughput)
L4S: An Active Queue Management technique to ensure low latency
L4S adoption in the industry
L4S and 5GS?
Summary
References
Appendix: 5G_AIS objectives

## Slide 3: Introduction/abstract
Advanced Interactive Services, e.g. Cloud Gaming services and Unmanned Aerial Systems, includes requirement of low latency and high throughput
5GS Enhancements for Advanced Interactive Services is part of Rel-17 WI 5G_AIS
To efficiently meet low latency requirements, support for Active Queue Management (AQM) techniques in 5GS is necessary
An AQM mechanism, L4S, is being standardized and adopted in the industry for low latency and high throughput
RAN2 has discussed the support of L4S (R2-1913888.zip), however this support requires traffic classification in the UPF, e.g. new standardized 5QI values, to indicate the L4S enabled flows to RAN
Assuming that applications addressed by 5G_AIS will use L4S, we propose to consider the support of L4S capable Service Data Flows as TEI17 technical enhancement or as part of WI 5G_AIS

## Slide 4: L4S: An Active Queue Management to ensure low latency
L4S = Low Latency Low Loss and Scalable throughput is a combination of
  ECN marking already when queues are small, and
  A new (scalable) congestion control in end hosts
Standardized in IETF [1]
Studied in the EU project RITE [2,3]
Used already today in data centers [4]
Supported in DOCSIS standard [5]
Congestion control for L4S:
  DCTCP , Data Center TCP [4]
  BBRv2 [6]
  SCReAM (RFC8298) [7]
  TCP-Prague [8]

## Slide 5: L4S interest and possible adoption in the industry
Remote controlled vehicles (cars, trucks, drones)
  UL heavy traffic
  5G RC-Car (Ericsson Tech Demonstrator) :
    Media rates up to 45Mbps
    SCReAM congestion control (L4S capable)
Google Stadia (Cloud Gaming),
YouTube (Streaming video):
  BBR, transitioning to BBRv2 (potential L4S support)
AR/VR/XR
  What ever ’R’ that requires low (queue) delay and potentially high throughput
  L4S capablility with TCP BBRv2 or RTP/UDP + SCReAM (RFC8298)
L4S targets applications in focus for 5G_AIS WI

## Slide 6: Simulation illustrating how L4S minimize delay
L4S minimizes latency and retain throughput
Scenario 2: L4S
Scenario 1: TCP (Legacy)
Notes: Simulation conditions:
NR 40MHz, 0.125ms TTI 1 basestation, 3 cells
2ms RTT over transport network
”Pre-scheduling” of UL ACKs
User 1 starts at T= 0.0s
User 2 starts at T= 2.1s
Scenario 1: TCP (legacy)
  Cubic
  Packet pacing AQM minDropTh = 30ms
Scenario 2: L4S
  DCTCP
  Packet pacing L4S marking on PDCP (no queue on RLC)
  Mark probability computed every 10ms
  minMarkTh = 1ms
  maxMarkTh = 3ms

## Slide 7: L4S and 5GS?
A Service Data Flow from an application supporting L4S is bound to a QoS Flow that indicates L4S support to NG-RAN, e.g. implicitly via a (new) 5QI value or explicitly via a flag
Buffering of packets of a L4S QoS Flow is monitored in e.g. UPF, RAN and UE. Based on the measured queue delay, the ECN field in IP header of UP packets are toggled to indicate congestion
Transport Protocol (UE and Server side) handles rate adaptation

## Slide 8: Conclusion
Advanced Interactive Services will require low latency
In order to meet low latency requirement, active queue management needs to be enabled for L4S capable Service Data Flows
We propose that 3GPP considers to include the support of L4S either:
as a TEI17 technical enhancement; or
as part of the Rel-17 WI for 5G_AIS.

## Slide 9: Summary
Given the requirements for supporting low latency and the interest from the industry in Active Queue Management based on L4S, we propose to endorse the support of L4S capable Service Data Flows work in SA2 either:
as a TEI17 technical enhancement; or
as part of the WI for 5G_AIS

## Slide 10: References
Low Latency, Low Loss, Scalable Throughput (L4S) Internet Service: Architecture, Briscoe et al, Internet-draft, IETF, July 2019, https://datatracker.ietf.org/doc/draft-ietf-tsvwg-l4s-arch/
Deployment of RITE mechanisms in use-case trial testbeds report, Ing-Jyh Tsang, EU project RITE, January 2016, https://riteproject.files.wordpress.com/2015/12/rite-deliverable-3-3-public1.pdf
Data Center to the Home, EU project RITE, https://riteproject.eu/dctth/
Data Center TCP (DCTCP): TCP Congestion Control for Data Centers, Bensley et al, Internet-draft, IETF, October 2017, https://tools.ietf.org/html/rfc8257
Low Latency DOCSIS: Technology Overview, CableLabs, 2019, https://cablela.bs/low-latency-docsis-technology-overview-february-2019
BBR v2: A Model-based Congestion Control – IETF 105 Update, Google, IETF 105, Montreal, July, 2019, https://datatracker.ietf.org/meeting/105/materials/slides-105-iccrg-bbr-v2-a-model-based-congestion-control-00
Self-Clocked Rate Adaptation for Multimedia, Johansson and Sarker, RFC 8298, IETF, December 2017, https://tools.ietf.org/html/rfc8298
“Linux Kernel tree containing patches for TCP Prague and the dualpi2 qdisc”, https://github.com/L4STeam/linux/

## Slide 11: Appendix: 5G_AIS Objectives
This Work Item is to define potential QoS parameters e.g. new standardized 5QI(s) corresponding to QoS requirements from SA1 NCIS work item in TS 22.261 including the following aspects
• Required latency for uplink transmission from UE to UPF plus downlink transmission from UPF to UE.
• Required reliability for uplink sensor/pose data and downlink pre-rendered/rendered audio/visual data
• Required high data rate in downlink direction related to SA1 agreed KPIs including FPS (frame-per-second) and resolution etc.
NOTE 1: The KPI values including FPS and resolution were agreed by SA1 and some corresponding KPI i.e. data rate is being evaluated in SA4 . The exact values should be reviewed based on SA1/SA4 outcome i.e. after SA1 NCIS work item completion to further align stage-1 requirements and additional requirements for QoS enhancement may come from SA4’s ongoing work on 5G XR.
NOTE 2: QoS implications for RAN will be coordinated with RAN WGs.
NOTE 3: Edge computing related aspects are not in scope of this work item.