## Slide 1: Way Forward proposals for Alternative QoS Profile (AQP)
Dario S. Tonesi
Huawei

## Slide 2: Table of contents
QoS parameters signaled from CN to RAN for each Alternative QoS Profile (AQP)
  RAN3 LS in on Stage 3 for AQP
  Proposed Ways Forward for QoS parameters signaled b/w CN – RAN
Differentiation between lack of support of AQP feature and lack of support of least preferred AQP
  Issues with lack of differentiation
  Proposed Way Forward

## Slide 3: 1. Incoming RAN3 LS on Stage 3 for AQP (R3-202856)
RAN3 took the following Working Assumption
  For each AQP, CN signals to RAN
    GFBR
    PDB
    PER
This is not aligned with the current Stage 2 design which defines the AQP as having the same format as the QoS profile, which allows CN to signal to RAN, for each AQP, the full set of QoS parameters (including 5QI, MFBR, AV, MDBV, etc.)

## Slide 4: 1. Proposed Way Forward: AQP parameters signaled from CN to RAN
Way Forward Alternative 1: stick to Stage 2 design (full set of QoS profile parameters)
  Keep 5QI centric design of AQP
  For each AQP, SMF can signal to RAN
  some or all QoS profile parameters
  Liaise RAN3 accordingly
5QI ARP GFBR (UL, DL) MFBR (UL, DL) | Mandatory information
Notification control | Optional information
To overwrite the value of the 5QI: Priority Level Averaging window MDBV (for Delay-critical GBR resource type only) | 
In case of signalled 5G QoS characteristics all of: Resource Type (GBR, Delay critical GBR) Priority Level PDB (including CN PDB) PER Averaging window MDBV (for Delay-critical GBR resource type only) | 

## Slide 5: 1. Proposed Way Forward: AQP parameters signaled from CN to RAN
Way Forward Alternative 2: limited set of QoS profile parameters signaled from CN to RAN
  Keep 5QI centric design of AQP
  For each AQP, SMF can signal to RAN
  a limited set of QoS profile parameters
  Liaise RAN3 accordingly
ARP GFBR (UL, DL) MFBR (UL, DL) | 
If standardized or pre-configured 5QI exists: | If no standardized or pre-configured 5QI exists:
5QI | PDB (including CN PDB) PER Averaging window MDBV (for Delay-critical GBR resource type only)
To overwrite the value of the 5QI: Averaging window MDBV (for Delay-critical GBR resource type only) | 

## Slide 6: 2. Differentiation between not supporting AQP feature and not fulfilling any/least preferred AQP
Currently it is not possible to differentiate between a gNB that does not support the AQP feature and a gNB that does support the feature but cannot fulfill even the least preferred AQP
This impacts AF/PCF behaviour:
  with an gNB supporting AQP feature, the AF/PCF can just wait for the RAN to upgrade ASAP;
  with a Rel-15 gNB, AF needs to successively send PDU mod. requests (setting Requested QoS Profile to next best AQP) until the gNB accepts one (or none) of them
RAN 3 seemed to believe that per cell configuration data in CN could solve this. However, that approach requires SMF/PCF in HPLMN to be configured with data on all the gNBs in every VPLMN and that is unrealistic.

## Slide 7: 2. Proposed Way Forward
Way Forward Proposal: NG-RAN N2AP PDU SESSION RESOURCE NOTIFY message should enable the SMF to differentiate between
  gNB that supports Alt QoS Profiles and has downgraded the UE’s Flow’s QoS to below the least preferred Alt QoS Profile, and
  gNB that does not support Alt QoS Profiles.
Explicit indication that none of the AQPs can be fulfilled. Stage 3 details to be decided by RAN3
Liaise RAN3 accordingly

## Slide 8: Thank You!