## Slide 1: FS_ATSSS_Ph2 WG2 Status Report
Tricci So
ZTETX Inc.
3GPP TSG SA WG2 Meeting #140E
Elbonia, 19 Aug. – 1 Sep. 2020
S2-2005871

## Slide 2: FS_ATSSS_Ph2 after SA2#140E

## Slide 3: FS_ATSSS_Ph2 Rel-17 Study/Work
Progress since SA#88E:
  Latest TR will be found on server https://www.3gpp.org/ftp/Specs/archive/23_series/23.700-93
  3 KIs have been defined.
  6 new solutions have been proposed on top of existing 8 solutions to address various KIs.
  Strong dependency on IETF progress on QUIC/MP-QUIC development for to support KI#2. An LSout was sent to IETF QUIC working group to ask for clarifications QUIC/MP-QUIC IETF drafts’ availability and also the optionality to support data encryption.
RAN impacts or dependencies:
    None identified.
Next steps:
  Solution Clean-up, prepare and moderate the discussions on the evaluation and conclusion(s) for each Key Issue.
  Target Completion: There is risk that study item will not conclude by Dec, 20 due to IETF dependency.
WI Code | Work Item Title | WP | Target Date | WID#
FS_ATSSS_Ph2 | Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture Phase 2 | 35% -> 70% | Sep., 20 -> Dec., 20 | SP-200095

## Slide 4: FS_ATSSS_Ph2 status after SA2#140E (1/6)
Solutions | Title | Key Issue(s)
#1 | QUIC-LL Steering Functionality | 2
#2 | New steering mode – Autonomous steering mode | 1
#3 | New steering mode – Autonomous steering mode with advanced PMF | 1
#4 | New steering mode – Redundant steering mode | 1
#5 | Replacing 3GPP access leg of MA-PDU Session with PDN connection in EPC | 3
#6 | MPQUIC-LL Steering Functionality | 2
#7 | Proposed solution based on MP-QUIC | 2
#8 | Proposed solution based on QUIC | 2

## Slide 5: FS_ATSSS_Ph2 status after SA2#140E (2/6)
Solutions | Title | Key Issue(s)
#9 | Supporting a PDN connection in EPC as a 3GPP access leg of MA-PDU Session | 3
#10 | Extension of 5G RG solution to support Ethernet PDU Session types | 3
#11 | New steering mode – RTT difference based steering mode | 1
#12 | New steering mode – UE assisted traffic steering mode | 1
#13 | Proxy based solution using QUIC | 2
#14 | Proxy based solution using MP-QUIC | 2

## Slide 6: FS_ATSSS_Ph2 status after SA2#140E (3/6)
  RAN and/or IETF impacts and dependencies:
  None for RAN
  Strong dependency on IETF progress on QUIC/MP-QUIC development for some proposed solutions. These solutions require tighter collaboration between 3GPP and IETF to address SA2 requirements in a timely manner. An LSout was sent to IETF QUIC working group to ask for clarifications QUIC/MP-QUIC IETF drafts’ availability and also the optionality to support data encryption.
Contentious Issue:
  None
Focus for the Next Meeting (SA2#140E):
  Solution Clean-up, prepare and moderate the discussions on the evaluation and conclusion(s) for each Key Issue.
  Target Completion: There is risk that study item will not conclude by Dec, 20 due to IETF dependency.
Overall Plan:
  After SA2#140E (Sept.2020): Organize 2 CCs and offline discussions to work on merging solutions, and to moderate the evaluation and conclusion for each KI .
    NOTE-1: KI#1 may have none or more than one solution dependent for which proposed steering mode(s) are to support
  SA2#141E (Oct.2020): Solution clean up to finalize existing solutions. Start the evaluation and work towards conclusion.
  SA2#142E (Nov.2020): Complete evaluation and conclusions. Submit TR 23.700-93 to SA#90E plenary for approval.

## Slide 7: FS_ATSSS_Ph2 status after SA2#140E (4/6)
Key Issue | Key Issue Descriptions & Status | Associated Solutions
#1 | Additional Steering Methods | #2, #3, #4, #11, #12
 | 1 solution proposes a new steering mode, called Autonomous steering mode, provides to both the UE and the UPF flexibility on the traffic splitting control when two accesses are applicable for this traffic. 1 solution proposes to enhance the PMF as defined in Rel-16 needs to support the measurement according to the target QoS requirements of the traffic. 1 solution proposes new steering mode to allow the traffic transmitted via 3GPP and non-3GPP accesses in a redundant way to achieve the lowest latency and lower the loss rate. 1 solution proposes not only considers RTT of each access but also considers the RTT difference between two accesses. As a result, SDFs will be transmitted via two accesses only when the RTT difference for two accesses is acceptable so that not only the network resources of both accesses can be utilized, but also asynchronous problem can be alleviated as much as possible. 1 solution proposes UE to provide information about the state of the UE w.r.t. the 3GPP and non-3GPP access conditions that can be exploited to take more informed traffic distribution decisions to steer traffic, which can result in better system performance. Status: Average of solutions’ completeness is ~85% External Dependency (e.g. RAN, IETF): None Contentious Issue: None Next Steps: Complete solutions and start the evaluation and conclusion Target Completion: Study is aimed to be completed by Dec. 20, | 

## Slide 8: FS_ATSSS_Ph2 status after SA2#140E (5/6)
#2 | Additional Steering Functionalities | #1, #6, #7, #8, #13, #14
 | 1 solution proposes a new ATSSS steering functionality referred as QUIC-Low Layer (QUIC-LL) because it operates below the IP layer (such as ATSSS-LL) by leveraging one or more QUIC connections per access for the transport between UE and its serving UPF. 1 solution proposes a new ATSSS steering functionality referred as MPQUIC-Low Layer (MPQUIC-LL) because it operates below the IP layer (such as ATSSS-LL) by leveraging one or more QUIC connections per access for the transport between UE and its serving UPF. 1 solution proposes a new ATSSS steering functionality, MPQUIC, with the similar principle as MPTCP, but for enabling traffic splitting support for UDP traffic which was not explicitly supported by ATSSS-LL in Rel-16 1 solution proposes a new ATSSS steering functionality, QUIC, to be combined with ATSSS-LL transport to enable traffic splitting support for UDP traffic which was not explicitly supported by ATSSS-LL in Rel-16 1 solution proposes a new ATSSS steering functionality for QUIC with an hybrid approach by leveraging the QUIC transport approach from ATSSS-LL solution and the encapsulation approach from QUIC Proxy solution based on the MASQUE draft from IETF 1 solution proposes a new ATSSS steering functionality for MPQUIC QUIC with an hybrid approach by leveraging the QUIC transport approach from ATSSS-LL solution and the encapsulation approach from QUIC Proxy solution based on MASQUE draft from IETF Status: Average of solutions’ completeness is ~70% External Dependency (e.g. RAN, IETF): Strong dependency on IETF progress on QUIC/MP-QUIC development for some proposed solutions. These solutions require tighter collaboration between 3GPP and IETF to address SA2 requirements in a timely manner. An LSout was sent to IETF QUIC working group to ask for clarifications QUIC/MP-QUIC IETF drafts’ availability and also the optionality to support data encryption. Contentious Issue: TBD – if all solutions are determined as the viable new steering functionalities, then show hands may be needed for final conclusion. Next Steps: Solution cleanup, start the evaluation and conclusion Target Completion: Study is aimed be completed by Dec. 20. However, there is possibility of delay due to dependency on IETF. | 

## Slide 9: FS_ATSSS_Ph2 status after SA2#140E (6/6)
#3 | Supporting MA PDU with 3GPP access leg over EPC and Non-3GPP access leg over 5GC | #6, #9, #10
 | 1 solution proposes to enable a capable UE and network to replace the 3GPP access leg of a normal MA PDU Session with a PDU connection in EPC, while keeping the non-3GPP access leg in 5GC 1 solution is re-using the solution in TS 23.316 clause 4.12.3 from Rel-16 but supports other devices than 5G RG. 1 solution proposes to extend the R16 ATSSS interworking for 5G-RG to also support Ethernet PDU Session type and for any kind of UE Status: Average of solutions’ completeness is ~90% External Dependency (e.g. RAN, IETF): None Contentious Issue: None Next Steps: Complete solution and to align the similar existing solution that supports 5G-RG, start the evaluation and conclusion Target Completion: Study is aimed to be completed by Dec. 20. |