## Slide 1: SA2#144E N1 mode Enabling AI 4.1
Huawei, HiSilicon
2021.04.06

## Slide 2: Alternatives on the table
Alt#1: No service continuity
Alt#2: When N1 is enabled, the UE releases the old PDN connection and requests a new PDN connection.
Alt#3: Always send PDU session ID regardless of N1 mode status
Alt#4: When N1 is enabled, the UE initiates the PDN modification to send the PDU session id and get the 5G parameters.

## Slide 3
Whether support service continuity or not?
Alt#1 and Alt#2 have NO standard impact.
However, both Alt#1 and Alt#2 will causes service interruption or even termination:
Alt#1: during interworking，i.e., when the UE moves from EPC to 5GC;
Alt#2 the moment N1 is enabled;
The UE can be actively communicating, when the UE performs interworking or when the N1 mode is enabled, e.g., voice service and online gaming.
Observation 1: both Alt#1 and Alt#2 will causes service interruption or even termination

## Slide 4: Service Continuity Needs To Be Supported
Proposal 1: Support service continuity when the N1 is enabled.
Alt#1: No service continuity
Alt#2: When N1 is enabled, the UE release the old PDN connection and request new PDN connection.
Alt#3: Always send PDU session ID regardless N1 mode status
Alt#4: When N1 is enabled, the UE initiates the PDN modification to send the PDU session id and get the 5G parameters.
This leaves Alt#3 and Alt#4 as possible alternatives to choose between.

## Slide 5
Impact analysis of Alt#3
2. The source eNodeB sends Handover Required (Direct Forwarding Path Availability, Source to Target transparent container, target eNodeB Identity, CSG ID, CSG access mode, target TAI, S1AP Cause) to the source MME…
7. The SMF+PGW-C (default V-SMF in the case of home-routed roaming scenario only) sends a Nsmf_PDUSession_CreateSMContext Response (PDU Session ID, S-NSSAI, N2 SM Information (PDU Session ID, S-NSSAI, QFI(s), QoS Profile(s), EPS Bearer Setup List, Mapping between EBI(s) and QFI(s), CN Tunnel-Info, cause code)) to the initial AMF.
The target AMF sends a Handover Request (Source to Target Transparent Container, Allowed NSSAI, N2 SM Information (PDU Session ID, S-NSSAI, QFI(s), QoS Profile(s), EPS Bearer Setup List, V-CN Tunnel Info, Mapping between EBI(s) and QFI(s)), Mobility Restriction List, UE Radio Capability ID) message to the NG-RAN.
Observation 2: The PDN connections that does not support IWK may be handed over.

## Slide 6
Impact analysis of Alt#3
Observation 3: The SMF/PGW-C always considers the N1 capability is enabled. Misalignment between MM layer and SM layer if N1 mode is disabled.
Observation 4: CHF is always selected instead of OCS/OFCS. Charging is not supported for certain features , e.g., CP CIoT and CSG.
NOTE: The SMF+PGW-C knows that the UE does not support 5GS NAS if the UE does not provide PDU Session ID in PCO (see TS 23.501 [2] clause 5.15.7).
UE
MME
S-GW
SMF+P-GW
PDN connection Establishment Req(PCO(PDU Session ID))
PCF
Npcf_SMPolicyControl _Create request
(SmPolicyContextData (PDU Session ID))
The UE always provides PDU ID in establishment
UDR
CHF
Existing procedures
Consider the UE
supports IWK
Npcf_SMPolicyControl _Create response()
PDN Connection Modification Req(PCO(mapped 5G QoS paras))
Store the 5G QoS paras
Initiate the charging session
OCS/OFCS

## Slide 7: Impact analysis of Alt#4
Initiate the charging session
Observation 5: Impact on UE and SMF+P-GW.
Observation 6: Impact of PCF, but interaction with PCF is not required .
UE
MME
SGW
SMF+PGW-C
Request Bearer Resource Modification(PCO(PDU Session ID))
PCF
Npcf_SMPolicyControl _Update request( SmPolicyUpdateContextData(PDU Session ID(op)))
Trigger modification when N1 is enabled
UDR
CHF
Existing procedures
Changes PDU Session ID
Npcf_SMPolicyControl _Update response()
Session management Request(PCO(mapped 5G QoS paras))
Session management Response ()
OCS/OFCS
Terminates the charging session

## Slide 8
Impact analysis of Alt#4
4.2.4 Npcf_SMPolicyControl_Update Service
4.2.4.2 Requesting the update of the Session Management related policies
When the SMF detects that one or more policy control request triggers are met, the SMF shall send a POST request to the PCF to update an Individual SM Policy resource. The {smPolicyId} in the URI identifies the Individual SM Policy resource to be updated.
5.3.1 Resource Structure
Name | Data type | Definition
apiRoot | string | See subclause 5.1
smPolicyId | string | Unique identifier of the individual SM Policy resource.
Table 5.3.3.2-1: Resource URI variables for this resource
Observation 7 : The PDU Session ID is not required to be provided to the PCF for updates/modifications as the SMF uses the existing smPolicyID.
TS 29.512

## Slide 9
Conclusion
Proposal 2: Alt#4 is selected as way forward.
Alt#1: No service continuity
Alt#2: When N1 is enabled, the UE release the old PDN connection and request new PDN connection.
Alt#3: Always send PDU session ID regardless N1 mode status
Alt#4: When N1 is enabled, the UE initiates the PDN modification to send the PDU session id and get the 5G parameters.

## Slide 10: Thank you