## Slide 1: Open Discussion about eNA work in R18
vivo(Xiaobo Wu), China Mobile(Aihua Li)

## Slide 2: Candidate Objective(s) in R18 eNA
Rel-17 feature enhancements
Rel-17 Leftover
    KI#2. Multiple NWDAF instances on Federated ML
    Status: discussed in R17 and more study needed
    KI#3. Mapping of NWDAF use cases to NFs and identify actions that could be taken based on NWDAF analytics and predictions
    Status: deprioritized from R17
    KI#5. New types of outputs provided by NWDAF
    Status: deprioritized from R17
    KI#6. Study possible mechanisms for improved correctness of NWDAF analytics
    Status: deprioritized from R17
    KI#14. NWDAF-assisted application detection
    Status: discussed in R17 and more study needed
    KI#20. NWDAF assisting in detecting anomaly events for the user plane
    Status: deprioritized from R17
    KI#21. NWDAF assisting in user plane performance
    Status: discussed(ATSSS related in R17 and more study needed
    NWDAF Deployment options
    Status: deprioritized from R17
    Other leftover from R17 due to limited time before June
    KI#11: further enhancement data collection efficiency
    KI#12: enhanced NWDAF-assisted RFSP policy (Details in slide3）
    KI#19: ML Model between Multi-vendor (ML Model restricted in single vendor in R17)
    KI#xx : UPF data report to NWDAF?
New architecture/Use Case(s)
    Distributed AI Training and Inference architecture
    Vertical Federated Learning (UE/CN/AF collaboration)
    Online Learning (discussed in R17 and more study needed )
    Reinforcement Learning
    Roaming data/analytics exchange (including network sharing)
    Interaction between NWDAF and RAN (RAN3 started to study RAN AI and driven by use case or RAN requirement)
    NWDAF interworking with IMS
    Policy recommendation based on virtual data and simulation in NWDAF
    New use case(s)?

## Slide 3: Vertical Federated Learning mitigate Data exchange difficulty in 5G
NWDAF
(MTLR, ML Model Training)
NWDAF
(AnLF, inference )
5GC NF
CN
Data
UE/RAN
AF
AF Data
ML Model
UE/RAN Data
  Issues and requirement:
  Data analytics in 5G network usually needs data collection from different domains, but each domains (e.g. UE/RAN/CN/AF) may be isolated;
  Each domain have many private implementations and is not willing to report their data related to the private implementations.
  Potential enhancement in R18:
  Network architecture enhancement to support vertical federated learning, allowing different domains to exchange necessary intermediate information to assist E2E data analysis without exposing RAW data;

## Slide 4: Vertical Federated ML, FYI (Model training without raw data exchange)
Client A
Client B
No data is exchanged.
Encrypted entity alignment
Encryption model training
Model A
Model B
Client A
Client B
Federal system C
Federated model
1. Send the public key.
2. Interaction intermediate result
3. Calculation of gradients and losses
4. Model update
4.
4.
1.
1.
2.
2.
3.
3.
Reference: Federate Learning: Concept and Application. Qiang Yang et al. 2019.
    Data set：,
    model：，objective：：
    Encryption entity alignment is to find the intersection of the users of the A and B, and extract the common part of the two data as the training dataset.
    If the Client A is RAN and the Client B is a CN, the RAN and CN belong to the same operator. Therefore, encryption could be omitted.
    The CN has label data (e.g. Service MOS). The RAN does not need to transmit the radio data () to CN, and only needs to transfer the to CN

## Slide 5: Enhanced NWDAF-assisted RFSP policy
R17 Status：
    5G/4G RFSP index selection assisted by NWDAF：
  NWDAF provides analytics to PCF: 1) User service behavior; 2) Service experience per RAT/Frequency.
  Based on User service behavior analytics, the PCF determines the service in use for a UE, and then adjust RFSP based on the relationship between service experience and RAT/frequency.
    Leftover Issues:
  Currently, NWDAF can perform data collection and analysis only in 5G, so only support inter-frequency selection of 5G for UE. NWDAF cannot collect data collection from 4G and/or WiFi, and consequently do not support smart network selection among 5G, 4G and WiFi.
  UE also has Radio/Frequency selection policy esp. in idle mode and harmonized policy between UE and network is needed.
    Potential enhancements in R18:
  Data collection from 4G network and WiFi to support intelligent network selection among 5G, 4G and WiFi;
  study policy harmonization between UE and network.
Fig. NWDAF-assisted RFSP policy (still under discussion)
AF
Network data
OAM
Data from OAM
Cell energy saving states
5GC
AMF
EPC
UPF
SMF
MME
PGW
SGW
① service in use analytics
② Service experience analytics per RAT/Frequency
NWDAF
PCF
Service data
from AF
gNB
eNB
RFSP index

## Slide 6: UPF data reporting to NWDAF
R16/17 Status：
    Lengthy discussion occurred in R16 and R17 as UPF data is key to NWDAF for data analytics
    However, so far it is not defined how UPF report data to NWDAF, which means UPF data reporting is still vender implementation.
    Clause 6.4.2 TS 23.288 Input Data
    NOTE 1: How NWDAF collects QoS flow Bit Rate, QoS flow Packet Delay, Packet transmission and Packet retransmission information from UPF is not defined in this Release of the specification.
    Potential study in R18 :
  Seemly It is time to study how UPF report data to NWDAF

## Slide 7: backup

## Slide 8: eNA_ph2 status after SA2#143E (2/5)
  Key Issue #4: Remaining aspects on how to ensure that slice SLA is guaranteed
  3 CRs agreed for 23.288, 1 CR agreed for 23.501, 1 CR agreed for 23.502.
  Next steps: Continue the normative work.
  Key Issue #5: New types of outputs provided by NWDAF (NOT to be progressed in R17)
  Key Issue #6: Study possible mechanisms for improved correctness of NWDAF analytics (NOT to be progressed in R17)
  Key Issue #7: Adding Application attributes and KPIs as the Input data in some services described in TS 23.288 [5]
  1 CR agreed for 23.288.
  Next steps: Continue the normative work.
  Key Issue #8: UE data as an input for analytics generation
  4 CRs agreed for 23.288, 1 CR agreed for 23.502, 1 LS Reply agreed.
  Next steps: Continue the normative work.
  Key Issue #9: Dispersion analytic output provided by NWDAF
  1 CR agreed for 23.288, 2 CRs agreed for 23.502, 1 CR agreed for 23.503, 1 LS Reply agreed, 1 LS postponed to SA2#144E.
  Next steps: Continue the normative work.
  Key Issue #10: NWDAF Assisted UP Optimization
  2 CRs agreed for 23.288, 1 CR agreed for 23.501, 2 CRs agreed for 23.502.
  Next steps: Continue the normative work.

## Slide 9: eNA_ph2 status after SA2#143E (3/5)
  Key Issue #11: Increasing efficiency of data collection
  13 CRs agreed for 23.288, 4 CRs agreed for 23.501, 7 CRs agreed for 23.502.
  Next steps: Continue the normative work.
  Key issue #12: NWDAF-assisted RFSP policy
  1 CR agreed for 23.288, 1 CR agreed for 23.503.
  Next steps: Continue the normative work.
  Key Issue #13: Triggering conditions for analytics
  1 CR agreed for 23.288, 1 CR agreed for 23.501, 1 CR agreed for 23.502.
  Next steps: Continue the normative work.
  Key Issue #14: NWDAF-assisted application detection
  None.
  Key Issue #15: User consent for UE data collection/analysis
  LS Response from SA3 received
  Next steps: Start the normative work per received SA3 LS response.
  Key Issue #16: UP optimization for edge computing
  5 CRs agreed for 23.288, 2 CRs agreed for 23.501, 3 CRs agreed for 23.502.
  Next steps: Continue the normative work.
  Key Issue #17: Definition of accuracy levels
  1 CR agreed for 23.288.
  Next steps: Continue the normative work.

## Slide 10: eNA_ph2 status after SA2#143E (4/5)
  Key Issue #18: Enhancement for real-time communication with NWDAF
  1 CR agreed for 23.501, 1 CR agreed for 23.502.
  Next steps: Continue the normative work.
  Key Issue #19: Trained data model sharing between multiple NWDAF instances
  3 CRs agreed for 23.288, 2 CRs agreed for 23.501, 2 CRs agreed for 23.502.
  Next steps: Continue the normative work.
  Key Issue #20: NWDAF assisting in detecting anomaly events for the user plane
  None.
  Key Issue #21: NWDAF assisting in user plane performance
  None.