## Slide 1
Source: Ericsson Title: Signaling efficiency for Shared Delivery and others Document for: Discussion
Agenda Item: 8.9 Work Item / Release: 5MBS/ Release 17
S2-2102290

## Slide 2
Discussion (1)
General
MBS Session Management (i.e. for shared delivery) is currently based on per UE/PDU Session signaling,
  Resulting in inefficient signalling handling if no improvement is made.
Improvement were attempted during SA2#143E in S2-2101017 and S2-2100343r01 but no agreement was reached:
    S2-2101017 intends to improve signalling efficiency for MBS Session (re-)activation by SMF sending “Active List of UEs” to AMF. For MBS Session deactivation (or stop/release), MB-SMF sends requests to NG-RAN via AMF.
    S2-2100343r01 attempts to involve AMF in the MBS Session handling for shared delivery, so that the MBS Session management is handled on MBS Session level.
[Proposal-0] For shared delivery, continue to work on improving signaling efficiency.

## Slide 3
Discussion (2)
For MBS session deactivation, assume the improvement follows S2-2101017 and S2-2100343r01:
[Observation-1.1] S2-2101017 proposes that MB-SMF maintain NG-RAN node list (i.e. NG-RAN “registers” itself in MB-SMF for shared delivery, regardless of unicast transport or multicast transport over MB-N3), and then MB-SMF sends deactivation requests to the list of NG-RANs.
[Observation-1.2] S2-2100343r01 propose that AMF be informed of UE join state and get involved in MBS Session handling.
Currently SMF is only aware of UP tunnel entity of NG-RAN but has no knowledge about the global ID of NG-RAN serving the UE. In our view, the same principle should be applied to MB-SMF in 5MBS.
Besides, if multicast transport over MB-N3 interface, NG-RAN does not need to contact MB-SMF.
[Proposal-1] Involve AMF in MBS Session deactivation for shared delivery. Maintain the same principle as for unicast delivery, i.e. MB-SMF handles only NG-RAN’s tunnel entity (when applicable) without being aware of the global IDs of NG-RAN.
With the above proposal, NG-RAN does not need to “register” itself into MB-SMF when multicast transport over MB-N3 is used.

## Slide 4
Discussion (3)
For MBS Session activation, assume the improvement follows S2-2101017 and S2-2100343r01:
[Observation-2.1] S2-2101017 proposes that SMF send “Activate List of UEs” to AMF for group paging. It’s not clear whether the list include both IDLE and CONNECTED joined UEs, or only IDLE joined UEs.
  If the former, implication to handle inactive MBS Session in NG-RAN is to be investigated.
  If the latter, SMF needs to be aware of UE state by subscribing to the UE connectivity state change in the AMF which may increase CN signaling drastically. (Note that SMF does not have the exact information of UE connectivity state)
[Observation-2.2] S2-2100343r01 propose to make use of connection management (CM-IDLE and CONNECTED) which is a functionality inherent in AMF.
[Proposal-2] Involve AMF in MBS Session management for shared delivery, so that the functions inherent in AMF (e.g. managing UE’s state and awareness of NG-RAN nodes) can be utilized for MBS Session activation.
[Conclusion-1] AMF is aware of the connected RAN nodes and is responsible for connection management. If there is requirement based on knowledge of NG-RAN node list and/or UE IDLE/CONNECTED state, any solution bypassing AMF would require workaround to solve issues due to not being aware of RAN nodes and not being aware of UE state.

## Slide 5
Discussion (4)
For MBS Session Update:
  [Observation-3] MBS Session update for multicast MBS Session is not yet addressed.
  [Proposal-3] It’s proposed to address MB Session Update.
  Note that an MBS Session update may result in modification of existing MBS QoS Flow, addition of new MBS QoS Flow and/or deletion of MBS QoS Flow. This is not addressed yet.
For UE joins an MBS Session before service requirement for the MBS Session is provided by the AS/AF
  [Observation-4] If UE joining an MBS Session is rejected due to service requirement for the MBS Session not provided by the AF, end user’s experience will be affected negatively.
  [Implication-1] To mitigate the issue in [Observation-5], there was proposal during SA2#143E (in 23.757 v1.3.0) that AF establish MBS Session in inactive state, which has implication to GC AS, see slide “Discussion - aspects related to GC AS” later.

## Slide 6
Discussion (5) – taking input from pre-meeting CC
For MBS Session activation, S2-210xxxxdiscussion MBS session activation and deactivation.docx includes the following text:
  Comparison between Option 2 in S2-2101017 and S2-2100343
  Radio signalling efficiency is comparable
  S2-2100343 requires that AMF has knowledge of UEs in multicast session (AMF centric approach). This leads to extra complexity
    Procedures during join, leave, MBS session de-configuration, handover (in all variants) need to ensure that AMF has sufficient knowledge.
    Different UEs within an MBS session in the same radio are may be served by different AMFs (e.g. within one set). Which of these AMFs will handle the multicast session and how can this AMF obtain information about all UEs in the multicast session?
  S2-2101017 involves SMFs
    This leads to slightly more core network signaling (separate messages per SMF that include UE IDs), but compared to subsequent service requests per UE this can be neglected.
    Informing SMFs about activation is likely required anyway for activation of UEs with individual delivery
    SMF will be aware for IDLE UEs that PDU session is deactivated and can use this as criterion to request only paging of IDLE UEs. Alternatively, SMF can request paging of all UEs.
To S2-2100343 “S2-2100343 requires that AMF has knowledge of UEs in multicast session (AMF centric approach). This leads to extra complexity”, from our comparison to the SMF-centric approach, AMF involvement of MBS Session management has a logic that is less complicated, more consistent procedures, easier to understand, and more future proof. If there is a homogeneous support, the AMF solution is very straightforward.
To S2-2100343 “Different UEs within an MBS session in the same radio are may be served by different AMFs (e.g. within one set). Which of these AMFs will handle the multicast session and how can this AMF obtain information about all UEs in the multicast session?” , this seems to be a misunderstanding that joined UEs have to be in the same AMF. UEs joining the same MBS Sessions can be handled by different AMFs (if needed). When the 2nd or 3rd AMF tries to set up MBS Session context in NG-RAN with already established MB-N3 tunnel, the NG-RAN simply responds with success.
To S2-2101017 “Informing SMFs about activation is likely required anyway for activation of UEs with individual delivery”, this is not always the case. Individual delivery may only be needed when there is no homogeneous support of 5MBS in NG-RANs (i.e. Individual delivery is not needed with homogenous 5MBS support).
To S2-2101017 “SMF will be aware for IDLE UEs that PDU session is deactivated and can use this as criterion to request only paging of IDLE UEs. Alternatively, SMF can request paging of all UEs”,
  The first statement “SMF will be aware for IDLE … only paging of IDLE UEs” is not correct because UP deactivation of the PDU Session (associated with MBS Session) does not necessarily mean UE is IDLE. A UE may be in CONNECTED due to other PDU Session (not associated with MBS Session), as a result, group paging may not be performed by the AMF if all the joined UEs are in CONNECTED. If all the joined UEs entered CONNECTED due to PDU Sessions not associated with MBS Session, the NG-RAN will not be triggered to set up MB-N3, therefore “Alternatively, SMF can request paging of all UEs” may not work all the time.

## Slide 7
Discussion (6) - aspects related to GC AS
Aspects related to GC AS
In TR 23.757 v1.3.0 (2.0.0), the following states are proposed in 5GC:
  8.2.2.2 Multicast session
  ….
  The following states are proposed:
  - Configured multicast session: No multicast data are transmitted. Some information about the multicast session is configured, but no resources are reserved. For instance, TMGIs can be allocated but no complete session information be provided UEs may be allowed to join (subject to authorization check and configuration), but the first accepted UE join request will trigger the multicast session establishment.
  - Inactive multicast session: Established multicast session in inactive state. No multicast data are transmitted. UEs that joined the multicast session may be in CM CONNECTED or CM IDLE state. UEs are allowed to join the multicast session (subject to authorization check).
[Observation-5] AF is expected to establish multicast session in inactive state.
Implication-2: AF triggering establishment of multicast session in inactive state and activating the multicast session later impose new requirement to legacy Public Safety application.
Implication-3: If the AF establishes an inactive MBS Session and activates it later, the (preliminary) service requirement provided during establishment may be updated during activation, which may be modification of existing MBS QoS Flow as well as adding new MBS QoS Flow. This is not addressed yet.
  Q1: How is the (preliminary) service requirement determined by the AF?
  Q2: Correspondingly, if AF requested MBS Session deactivation, does it also imply some existing MBS QoS Flow may be removed ?
[Proposal-4] Keep the legacy GC AS behavior (i.e. allocate TMGI, start MBS Session which is active) to avoid new logic in the legacy AS.

## Slide 8
Proposed way forward
[Proposal-0] For shared delivery, continue to work on improving signaling efficiency.
[Proposal-1] Involve AMF in MBS Session deactivation for shared delivery. Maintain the same principle as for unicast delivery, i.e. MB-SMF handles only NG-RAN’s tunnel entity (when applicable) without being aware of the global IDs of NG-RAN.
[Proposal-2] Involve AMF in MBS Session management for shared delivery, so that the functions inherent in AMF (e.g. managing UE’s state and awareness of NG-RAN nodes) can be utilized for MBS Session activation.
[Proposal-3] It’s proposed to address MB Session Update.
[Proposal-4] Keep the legacy GC AS behavior (i.e. allocate TMGI, start MBS Session which is active) to avoid new logic in the legacy AS.
[Conclusion-1] AMF is aware of the connected RAN nodes and is responsible for connection management. If there is requirement based on knowledge of NG-RAN node list and/or UE IDLE/CONNECTED state, any solution bypassing AMF would require workaround to solve issues due to not being aware of RAN nodes and not being aware of UE state.
[Conclusion-2] Without AMF involvement, the SMF may not be able to know that the target NG-RAN support 5MBS in Xn HO thus not possible to switch Individual Delivery to Shared Delivery.
Based on the above, to have consistent handling for different procedures (e.g. MBS Session Start/Stop, Activate/Deactivation and MBS Session Update), to avoid situation that the attempt to resolve one issue will create more issues, and to have a framework that is future proof (e.g., to support network deployment with multiple SMF Service Areas), the following is proposed (as in S2-2100343r01) as way forward:
  [Proposal-5] Enhance the solution and involve AMF in MBS Session management for shared delivery, but UE join is still received in the SMF and informs AMF, and AMF interacts with MB-SMF so that the MBS Session management for shared delivery is on per MBS
  Session level. See 23.247 pCR S2-2102291 for the joining procedure.

## Slide 9
Thank You!

## Slide 10: Statement machines in 5GC from 23.757 v1.3.0
Configured multicast session: No multicast data are transmitted. Some information about the multicast session is configured, but no resources are reserved. For instance, TMGIs can be allocated but no complete session information be provided. UEs may be allowed to join (subject to authorization check and configuration), but the first accepted UE join request will trigger the multicast session establishment.
Active multicast session: Established multicast session in active state. Multicast data are transmitted to UEs that joined the multicast session. 5GC resources for the multicast session are reserved. Corresponding Radio resources are reserved depending on participating UE locations. UEs that joined the multicast session are in CM CONNECTED state. UEs are allowed to join the multicast session (subject to authorization check)
Inactive multicast session: Established multicast session in inactive state. No multicast data are transmitted. UEs that joined the multicast session may be in CM CONNECTED or CM IDLE state. UEs are allowed to join the multicast session (subject to authorization check).

## Slide 11
Info from S2-2101017
Option 2
AMF
UE
SMF
MB-SMF
MBS activate
NG-RAN
MBS data delivery
Group Paging (all RAs)
N_smf-update (PDU session activate)
Activate list of UEs
Service Request
PDU session Setup Req (MBS session ID)
MBS Activate (MBS session ID + mcast qos info)
Timer Expiry
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)

## Slide 12
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)
Info from S2-2100343r01