## Slide 1
Source: Ericsson Title: Signaling efficiency for Shared Delivery and others Document for: Discussion
Agenda Item: 8.9 Work Item / Release: 5MBS/ Release 17
S2-2103542 was S2-2102290r01

## Slide 2
Discussion (1)
General
MBS Session Management (i.e. for shared delivery) is currently based on per UE/PDU Session signaling,
  Resulting in inefficient signalling handling if no improvement is made.
Improvement were attempted during SA2#143E in S2-2101017 and S2-2100343r01 but no agreement was reached:
    S2-2101017 intends to improve signalling efficiency for MBS Session (re-)activation by SMF sending “Active List of UEs” to AMF. For MBS Session deactivation (or stop/release), MB-SMF sends requests to NG-RAN via AMF.
    S2-2100343r01 attempts to involve AMF in the MBS Session handling for shared delivery, so that the MBS Session management is handled on MBS Session level.
[Proposal-0] For shared delivery, continue to work on improving signaling efficiency.

## Slide 3
Discussion (2)
For MBS session deactivation, assume the improvement follows S2-2101017 and S2-2100343r01:
[Observation-1.1] S2-2101017 proposes that MB-SMF maintain NG-RAN node list (i.e. NG-RAN “registers” itself in MB-SMF for shared delivery, regardless of unicast transport or multicast transport over MB-N3), and then MB-SMF sends deactivation requests to the list of NG-RANs.
[Observation-1.2] S2-2100343r01 propose that AMF be informed of UE join state and get involved in MBS Session handling.
Currently SMF is only aware of UP tunnel entity of NG-RAN but has no knowledge about the global ID of NG-RAN serving the UE. In our view, the same principle should be applied to MB-SMF in 5MBS.
Besides, if multicast transport over MB-N3 interface, NG-RAN does not need to contact MB-SMF.
[Proposal-1] Involve AMF in MBS Session deactivation for shared delivery. Maintain the same principle as for unicast delivery, i.e. MB-SMF handles only NG-RAN’s tunnel entity (when applicable) without being aware of the global IDs of NG-RAN.
With the above proposal, NG-RAN does not need to “register” itself into MB-SMF when multicast transport over MB-N3 is used.

## Slide 4
Discussion (3)
For MBS Session activation, assume the improvement follows S2-2101017 and S2-2100343r01:
[Observation-2.1] S2-2101017 proposes that SMF send “Activate List of UEs” to AMF for group paging. It’s not clear whether the list include both IDLE and CONNECTED joined UEs, or only IDLE joined UEs.
  If the former, implication to handle inactive MBS Session in NG-RAN is to be investigated.
  If the latter, SMF needs to be aware of UE state by subscribing to the UE connectivity state change in the AMF which may increase CN signaling drastically. (Note that SMF does not have the exact information of UE connectivity state)
[Observation-2.2] S2-2100343r01 propose to make use of connection management (CM-IDLE and CONNECTED) which is a functionality inherent in AMF.
[Proposal-2] Involve AMF in MBS Session management for shared delivery, so that the functions inherent in AMF (e.g. managing UE’s state and awareness of NG-RAN nodes) can be utilized for MBS Session activation.
[Conclusion-1] AMF is aware of the connected RAN nodes and is responsible for connection management. If there is requirement based on knowledge of NG-RAN node list and/or UE IDLE/CONNECTED state, any solution bypassing AMF would require workaround to solve issues due to not being aware of RAN nodes and not being aware of UE state.

## Slide 5
Discussion (4)
For MBS Session Update:
  [Observation-3] MBS Session update for multicast MBS Session is not yet addressed.
  [Proposal-3] It’s proposed to address MB Session Update.
  Note that an MBS Session update may result in modification of existing MBS QoS Flow, addition of new MBS QoS Flow and/or deletion of MBS QoS Flow. This is not addressed yet.
For UE joins an MBS Session before service requirement for the MBS Session is provided by the AS/AF
  [Observation-4] If UE joining an MBS Session is rejected due to service requirement for the MBS Session not provided by the AF, end user’s experience will be affected negatively.
  [Implication-1] To mitigate the issue in [Observation-5], there was proposal during SA2#143E (in 23.757 v1.3.0) that AF establish MBS Session in inactive state, which has implication to GC AS, see slide “Discussion - aspects related to GC AS” later.

## Slide 6
Discussion (5) – taking input from pre-meeting CC
For MBS Session activation, S2-210xxxxdiscussion MBS session activation and deactivation.docx includes the following text:
  Comparison between Option 2 in S2-2101017 and S2-2100343
  Radio signalling efficiency is comparable
  S2-2100343 requires that AMF has knowledge of UEs in multicast session (AMF centric approach). This leads to extra complexity
    Procedures during join, leave, MBS session de-configuration, handover (in all variants) need to ensure that AMF has sufficient knowledge.
    Different UEs within an MBS session in the same radio are may be served by different AMFs (e.g. within one set). Which of these AMFs will handle the multicast session and how can this AMF obtain information about all UEs in the multicast session?
  S2-2101017 involves SMFs
    This leads to slightly more core network signaling (separate messages per SMF that include UE IDs), but compared to subsequent service requests per UE this can be neglected.
    Informing SMFs about activation is likely required anyway for activation of UEs with individual delivery
    SMF will be aware for IDLE UEs that PDU session is deactivated and can use this as criterion to request only paging of IDLE UEs. Alternatively, SMF can request paging of all UEs.
To S2-2100343 “S2-2100343 requires that AMF has knowledge of UEs in multicast session (AMF centric approach). This leads to extra complexity”, from our comparison to the SMF-centric approach, AMF involvement of MBS Session management has a logic that is less complicated, more consistent procedures, easier to understand, and more future proof. If there is a homogeneous support, the AMF solution is very straightforward.
To S2-2100343 “Different UEs within an MBS session in the same radio are may be served by different AMFs (e.g. within one set). Which of these AMFs will handle the multicast session and how can this AMF obtain information about all UEs in the multicast session?” , this seems to be a misunderstanding that joined UEs have to be in the same AMF. UEs joining the same MBS Sessions can be handled by different AMFs (if needed). When the 2nd or 3rd AMF tries to set up MBS Session context in NG-RAN with already established MB-N3 tunnel, the NG-RAN simply responds with success.
To S2-2101017 “Informing SMFs about activation is likely required anyway for activation of UEs with individual delivery”, this is not always the case. Individual delivery may only be needed when there is no homogeneous support of 5MBS in NG-RANs (i.e. Individual delivery is not needed with homogenous 5MBS support).
To S2-2101017 “SMF will be aware for IDLE UEs that PDU session is deactivated and can use this as criterion to request only paging of IDLE UEs. Alternatively, SMF can request paging of all UEs”,
  The first statement “SMF will be aware for IDLE … only paging of IDLE UEs” is not correct because UP deactivation of the PDU Session (associated with MBS Session) does not necessarily mean UE is IDLE. A UE may be in CONNECTED due to other PDU Session (not associated with MBS Session), as a result, group paging may not be performed by the AMF if all the joined UEs are in CONNECTED. If all the joined UEs entered CONNECTED due to PDU Sessions not associated with MBS Session, the NG-RAN will not be triggered to set up MB-N3, therefore “Alternatively, SMF can request paging of all UEs” may not work all the time.

## Slide 7
Discussion (6) - aspects related to GC AS
Aspects related to GC AS
In TR 23.757 v1.3.0 (2.0.0), the following states are proposed in 5GC:
  8.2.2.2 Multicast session
  ….
  The following states are proposed:
  - Configured multicast session: No multicast data are transmitted. Some information about the multicast session is configured, but no resources are reserved. For instance, TMGIs can be allocated but no complete session information be provided UEs may be allowed to join (subject to authorization check and configuration), but the first accepted UE join request will trigger the multicast session establishment.
  - Inactive multicast session: Established multicast session in inactive state. No multicast data are transmitted. UEs that joined the multicast session may be in CM CONNECTED or CM IDLE state. UEs are allowed to join the multicast session (subject to authorization check).
[Observation-5] AF is expected to establish multicast session in inactive state.
Implication-2: AF triggering establishment of multicast session in inactive state and activating the multicast session later impose new requirement to legacy Public Safety application.
Implication-3: If the AF establishes an inactive MBS Session and activates it later, the (preliminary) service requirement provided during establishment may be updated during activation, which may be modification of existing MBS QoS Flow as well as adding new MBS QoS Flow. This is not addressed yet.
  Q1: How is the (preliminary) service requirement determined by the AF?
  Q2: Correspondingly, if AF requested MBS Session deactivation, does it also imply some existing MBS QoS Flow may be removed ?
[Proposal-4] Keep the legacy GC AS behavior (i.e. allocate TMGI, start MBS Session which is active) to avoid new logic in the legacy AS.

## Slide 8
Proposed way forward
[Proposal-0] For shared delivery, continue to work on improving signaling efficiency.
[Proposal-1] Involve AMF in MBS Session deactivation for shared delivery. Maintain the same principle as for unicast delivery, i.e. MB-SMF handles only NG-RAN’s tunnel entity (when applicable) without being aware of the global IDs of NG-RAN.
[Proposal-2] Involve AMF in MBS Session management for shared delivery, so that the functions inherent in AMF (e.g. managing UE’s state and awareness of NG-RAN nodes) can be utilized for MBS Session activation.
[Proposal-3] It’s proposed to address MB Session Update.
[Proposal-4] Keep the legacy GC AS behavior (i.e. allocate TMGI, start MBS Session which is active) to avoid new logic in the legacy AS.
[Conclusion-1] AMF is aware of the connected RAN nodes and is responsible for connection management. If there is requirement based on knowledge of NG-RAN node list and/or UE IDLE/CONNECTED state, any solution bypassing AMF would require workaround to solve issues due to not being aware of RAN nodes and not being aware of UE state.
[Conclusion-2] Without AMF involvement, the SMF may not be able to know that the target NG-RAN support 5MBS in Xn HO thus not possible to switch Individual Delivery to Shared Delivery.
Based on the above, to have consistent handling for different procedures (e.g. MBS Session Start/Stop, Activate/Deactivation and MBS Session Update), to avoid situation that the attempt to resolve one issue will create more issues, and to have a framework that is future proof (e.g., to support network deployment with multiple SMF Service Areas), the following is proposed (as in S2-2100343r01) as way forward:
  [Proposal-5] Enhance the solution and involve AMF in MBS Session management for shared delivery, but UE join is still received in the SMF and informs AMF, and AMF interacts with MB-SMF so that the MBS Session management for shared delivery is on per MBS
  Session level. See 23.247 pCR S2-2102291 for the joining procedure.

## Slide 9
Thank You!

## Slide 10: Statement machines in 5GC from 23.757 v1.3.0
Configured multicast session: No multicast data are transmitted. Some information about the multicast session is configured, but no resources are reserved. For instance, TMGIs can be allocated but no complete session information be provided. UEs may be allowed to join (subject to authorization check and configuration), but the first accepted UE join request will trigger the multicast session establishment.
Active multicast session: Established multicast session in active state. Multicast data are transmitted to UEs that joined the multicast session. 5GC resources for the multicast session are reserved. Corresponding Radio resources are reserved depending on participating UE locations. UEs that joined the multicast session are in CM CONNECTED state. UEs are allowed to join the multicast session (subject to authorization check)
Inactive multicast session: Established multicast session in inactive state. No multicast data are transmitted. UEs that joined the multicast session may be in CM CONNECTED or CM IDLE state. UEs are allowed to join the multicast session (subject to authorization check).

## Slide 11
Info from S2-2101017
Option 2
AMF
UE
SMF
MB-SMF
MBS activate
NG-RAN
MBS data delivery
Group Paging (all RAs)
N_smf-update (PDU session activate)
Activate list of UEs
Service Request
PDU session Setup Req (MBS session ID)
MBS Activate (MBS session ID + mcast qos info)
Timer Expiry
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)

## Slide 12
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)
Info from S2-2100343r01

## Slide 13
The following slides are from conference call among interested companies
Source: Shared delivery establishment and subsequent signalling-vivo+Eric.pptx

## Slide 14
Shared delivery establishment and subsequent signalling - For discussion

## Slide 15: Related TDOCs
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.2.1.3 | 7.2.1.x (shared path establishment) | 7.2.1.y path release | 7.2.1.z (deactivation) |  | 
S2-2102291 | 23.247: Update [7.2.1.3] MBS join and Session establishment procedure | Ericsson |  |  |  |  |  | Should be merged into one
S2-2102387 | 23.247: MBS Session Join and Establishment | Huawei |  (7.2.1 a few) |  |  |  |  | 
S2-2102434 | 23.247: MBS Join and Session Establishment Procedure | Tencent |  |  |  |  |  | 
S2-2102438 | 23.247: Multicast session join procedure | CATT |  |  |  |  |  | 
S2-2102675 | 23.247: [7.2.1]-UE requested session join | vivo |  |  |  |  |  | 
S2-2102797 | 23.247: Modification to MBS session join procedure | ZTE |  |  |  |  |  | 
S2-2102941 | 23.247: Shared delivery establishment and support of subsequent signalling from MB-SMF | Nokia |  |  |  |  | 7.2.1.x/y/z: should consider together with related docs. | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.2.3.1 | 7.2.3.2 | 7.2.3.3 | 7.2.3.4 | 4.2.x |  | 
S2-2102290 | Signaling efficiency for Shared Delivery and others | Ericsson |  |  |  |  |  | Discussion paper, (update of the docs submitted to CC#1) | 
S2-2102393 | Discussion on Signalling Efficiency for MBS solutions | Huawei |  |  |  |  |  | Discussion paper (update of the docs submitted to CC#1) | 
S2-2102356 | 23.247: Multicast session start/stop/update&activation/de-activation/modification procedures | Samsung |  |  |  |  |  | Basic procedure: activation involve SMF. | Should be merged into one
S2-2102772 | 23.247: MBS Session Activation and Deactivation | Huawei |  |  |  |  |  | Basic procedure. | 
S2-2102942 | 23.247: MBS session activation. | Nokia |  |  |  |  |  | Session activation based on option 2 of 1017: SMF provides UE list to AMF | 

## Slide 16
Shared delivery establishment
Slide added by Ericsson
We would have expected an overall discussion on the scenarios from previous meetings, e.g. how to activate a session for joined UEs in IDLE and CONNECTED, UEs joining active and inactive in sessions.
The scenario picked for comparison in this part is activation of resources for a UE joining an already ongoing (i.e. active or inactive) MBS session, which is only one aspect among many to be looked at, therefore we have major concern to take this as basis for decision.

## Slide 17: Different proposed options
Option 1: Shared delivery establishment triggered by RAN, no RAN nodes and SMFs stored in MB-SMF (Huawei)
All subsequent signalling from MB-SAMF related to multicast session (e.g. for activation and deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 18: Different proposed options
Option 2: Shared delivery establishment triggered by RAN, MB-SMF stores RAN node IDs (Nokia)
signalling from MB-SMF for activation via AMF to enable that radio areas for UEs are taken into consideration
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 19: Different proposed options
Option 3: Shared delivery establishment triggered by RAN, AMF stores RAN node IDs
In a variant of Option 2, AMF also stores GTP Tunnel endpoint for multicast transport and avoids signalling to MB-SMF if multicast transport is used and additional RAN nodes request shared delivery for that multicast session.
signalling from MB-SMF for activation via AMF to enable that radio areas for UEs are taken into consideration
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 20: Different proposed options
Option 4: AMF centric approach: AMF triggers establishment of shared delivery and stores UEs and RAN nodes in multicast session
(Ericsson)
signalling from MB-SMF for activation also via AMF
Insert SMF, AMF, MB-SMF interaction during PDU Session Modification, and use separate procedure for handling RAN response.
AMF centric for Xn/N2 HO?

## Slide 21: Different proposed options
Option 5: Signalling Piggybacked in PDU session signalling (Vivo)
All subsequent signalling from MB-SMF related to multicast session (e.g. for activation, deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.
Signalling piggybacked in Xn/N2 HO

## Slide 22: Comparison of Options
 | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
State about multicast session in AMF | Not required | Not required | RAN nodes | RAN nodes, UEs, MB-SMF | Not required
State about multicast session in MB-SMF | SMFs, RAN node addresses | SMFs, AMFs RAN nodes, RAN node adresses, UEs | SMFs, AMFs, RAN node addresses, UEs | SMFs, AMFs, RAN node addresses | SMFs, RAN node addresses
State about multicast session in SMF | MB-SMF, UEs, RAN nodes | MB-SMF, UEs | MB-SMF, UEs | Not required | MB-SMF, UEs, RAN nodes
subsequent direct signalling for multicast session (e.g. deactivation) from MB-SMF to RAN nodes possible | yes | Yes | Yes | Yes | yes
activation for multicast session from MB-SMF to RAN nodes | Via SMF and AMF | Via SMF and AMF | Via SMF and AMF | Via AMF | Via SMF and AMF
deactivation for multicast session from MB-SMF to RAN nodes | Via SMF and AMF | Via AMF | Via AMF | Via AMF | Via SMF and AMF
Possibility of dublicated signalling from different AMFs for same MBS session at RAN node | Only session activation | Only session activation | Only session activation | Yes (Ericson: handling straightforward) | Only session activation
Reliable exchange of unicast transport address via acknowledged messages | yes | yes | yes | no (Ericson: why not reliable?) | yes
AMF involved in session management of multicast session | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | Yes (Ericsson: at session activation the AMF is relieved from UE list processing. So, this is a big advantage and along decent engineering principles. And, currently, AMF already has PDU Session info, EBI etc) | no
Same solution for shared delivery establishment when first UE is handed over to RAN node | yes | yes | yes | yes | yes
Ericsson: UE joined state in AMF can avoid UE list sent by SMF during activation and solves the scaling issues in case of large UE lists.
Ericsson: The cost is that AMF needs to be always contacted to calculate paging areas from a potentially large UE list. This is rather cumbersome design
Ericsson: The decisive comparison aspect is not how to establish finally resources but how to get into this situation
Ericsson: This was identified in the first RAN3 MBS meeting and is a stage 3 issue
Ericsson: This is a bit far-fetched aspect with some very arbitrary grounding
Eric: RAN talking to different entities !!!
Eric: RAN talking to different entities !!!
Eric: RAN talks to same entity for act and de-act

## Slide 23
subsequent signalling and other aspects
Slide added by Ericsson
In the following slides:
Option-SMF refers to SMF handling MBS Session
Option-AMF refers to AMF handling MBS Session

## Slide 24: MBS Session Activation
Option-SMF (Nokia S2-2102942)
Slide added by Ericsson
Option-AMF: MB-SMF -> AMF -> RAN (see red rectangle below)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)
Q1: If joined UEs does not have UP in SMF, but in CONNECTED state for other reason, how would such UE be added in MBS Session in RAN?
Q2: If all joined UEs in SMF have UP activated, does it mean that no MBS Session activation message will be sent to the NG-RAN? If so, how to bring the “inactive” MBS Session in RAN to Active again?

## Slide 25: MBS Session Deactivation
Option-SMF (from S2-2101017)
Slide added by Ericsson
Option-AMF: (see red rectangle below)
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)

## Slide 26: MBS Session Update (adding/deleting/modifying MBS QoS Flow)
Option-SMF: Which path to follow ?
  Path: MBS Session Activation, or
  Path: MBS Session Deactivation?
Slide added by Ericsson
Option-AMF: same path as for MBS Start/Activate/Deactivate
UE
NG-RAN
AMF
SMF
MB-SMF
NRF
MBS Session Update Request/Response
MBS Session Update
Update

## Slide 27: Other aspects
Alignment/misalignment between handling of PDU Session and handling of MBS Session ?
  SMF and MB-SMF discovery
    AMF discovers SMF for PDU Session (based on DNN, S-NSSAI, location…), while Option-SMF discovers MB-SMF for MBS Session => misalignment?
      Not future proof for ETSUN scenario, as SMF is not aware of other SMF service areas (although it’s moved out of Rel-17)
  NG-RAN info in CN
    SMF is only aware of NG-RAN tunnel entity for PDU Session, while in Option-SMF, MB-SMF will have knowledge of NG-RAN node (in addition to NG-RAN’s tunnel info) => misalignment?
  SM/MM split but AMF is already aware of session info, e.g.
    AMF handles EBI associated with QoS Flow (which is SM info),
    In NB-IoT case, AMF needs to know whether PDU Session’s UP has been established to limit the max no. of radio bearers
Slide added by Ericsson

## Slide 28: Comparison of Options considering subsequent signalling and other aspects
 | Option-SMF | Option-AMF | Comment
Consistent logic of different procedures (involved entities, failure handling possibilities etc) | No, every procedure is different, unless signaling efficiency is not considered | Consistent and signaling efficient | 
Potential issues with MBS Session activation | Yes, see Q1 and Q2 in slide “MBS Session Activation” | Not identified so far | 
UE join with only TMGI allocated | How UE can be associated with MBS Session when it’s started/estalbished is not clarified | Supported | 
Complexity to support foreseen future scenarios (e.g., ETSUN scenarios, roaming) | Expected to be very complicated unless AMF is involved | AMF selecting MB-SMF follows the same logic as for I-SMF selection | 
Slide added by Ericsson

## Slide 29
The following slides are from conference call among interested companies
Source: 5MBS_PCFinteraction_r2.pptx

## Slide 30
PCF authorizing MBS Session policy - For discussion

## Slide 31
MB-PCF authorizing MBS Session for both broadcast and multicast MBS Session
PCF
MB-SMF
NEF/MBSF
AF
MB Session Start (service requirement)
MBS Policy Association Req/Resp
Currently message flow (concluded in TR 23.757)
  MB-SMF optionally interacts with PCF at MBS Session Start/Stop
    Using similar approach as SMF interacting PCF at PDU Session establishment
  MBS Session policy expected to be very simple
    E.g. MBR/GBR/5QCI/ARP authorized for a certain application
Ericsson comment in r1:
Brought back this slide (removed by Nokia) to show what is the current status, and Ericsson’s understanding what policy/QoS could be authorized by PCF for MBS Session.

## Slide 32: Related TDOCs
Tdoc number | Title | Source | Affected clauses |  |  |  |  |  | Note | WF proposal
 |  |  | Annex A | 9.X (General description) | 9.Y (PCF service with SMF) | 9.Z (PCF service with NEF) | 7.1.1 | 6.6 |  | 
S2-2102726 | 23.247: MBS Application and Service Configuration Options | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102439 | 23.247: Policy control for Multicast and Broadcast services | CATT |  |  |  |  |  |  | General description | 
S2-2102946 | 23.247: PCF service for Interactions between MB-SMF and PCF. | Nokia |  |  |  |  |  |  | Interaction between MB-SMF and PCF | Separate one
S2-2102724 | 23.247: Requested MBS QoS and Dynamic PCC | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102725 | 23.247: MBS Session-AMBR | Tencent |  |  |  |  |  |  | Session AMBR for MBS should be considered for individual delivery | Separate one
S2-2102947 | 23.247: NEF PCF interactions. | Nokia |  |  |  |  |  |  | Interaction between NEF and PCF | 
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.3.1 | 7.3.2 | 7.3.3 | 7.3.x |  | 
S2-2102728 | 23.247: Update MBS Session Establishment for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102729 | 23.247: Update MBS Session Update for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102730 | 23.247: Update MBS Session Release for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.1.1 | 7.1.2 | 7.1.1.x de-configuration | 7.1.1.y configuration update | 7.2.1.3 |  | 
S2-2102354 | 23.247: Update on common procedures for multicast and broadcast services | Samsung |  |  |  |  |  | Adding de-configuration and configuration update procedure | Should be merged into one
S2-2102392 | 23.247: Updates for MBS session configuration | Huawei |  |  |  |  |  | Timing of establishing N6 connection | 
S2-2102437 | 23.247: Procedures of configuration for MBS | CATT |  |  |  |  |  |  | 
S2-2102673 | 23.247: [7.1.1]-Update to configuration procedures | vivo |  |  |  |  |  | Separate the “big” configuration procedure. | 
S2-2102727 | 23.247: Update the MBS Session Configuration Procedure | Tencent |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102338 | 23.247: Clause 7.1.1: Clarification on MBS service area | LG Electronics |  |  |  |  |  |  | 

## Slide 33: Different proposed options
Option 1 (currently concluded in TR 23.757 Ericsson proposal, no CR)
  Service requirements are included in message from NEF to MB-SMF and then forwarded to PCF
PCF
MB-SMF
NEF/MBSF
AF
MB Session Start (service requirement)
MBS Policy Association Req/Resp
Ericsson comment in r1:
Ericsson reminds Nokia (Thomas) that the PCF interaction illustrated here is also proposed in Nokia Sol#3 in TR23.757 and included in conclusion (clause 8.2.3)

## Slide 34: Different proposed options
Option 2 (Tencent)
  If PCF is used, it triggers establishment of MBS context at MBS

## Slide 35: Different proposed options
Option 3 (2947 (Nokia), 2673(Vivo)?, 2439 (Intel, Lenovo, Tencent, Motorola Mobility)?)
  Similar to existing PCC
  Session binding based on MBS session context at PCF
  For initial configuration, NEF can store session information in database and/or establish PCC authorization session
  For updates, direct interaction between NEF and PCF
  PCF retrieves stored configured session information from database (Nokia: UDM, Vivo: UDR)
  BSF used to discover PCF with MBS session context
Tencent: Why does the NEF need to store the Session information in a DB ?
And retrieve from the DB ?

## Slide 36: Comparison of Options
Option 1
  Unclear how policy authorization requests can be rejected
  Large containers might be required for service decription
  MB-SMF would be affected for service informnation updates even if PCF does not updated authorized QoS
  Unclear how PCF can use preconfigurede input for policy decisions (without database access)
Option 2
  Substantial change of MB-SMF PCF interactions compared to existing PCFSmPolicyControl (might become an MB-SMF service)
  Unclear how PCF can use preconfigurede input for policy decisions (without database access)
Option 3
  Aims for alignment with existing PCC procedures

## Slide 37
Answers to Questions by Ericsson
S2-2102947 NEF PCF interactions
Q2: why is BSF is needed?
Nokia reply: BSF enables AF and or MB-SMF to detect PCF. (Depending on what entity contacts PCF first, the other needs to contact same PCF for session binding)
MB-PCF
MB-SMF
AF
MB Session Start (service requirement)
Authorizing MBS Session
MB Session Start Response
Q1: For trusted AF, NEF may not be needed. If so, public safety AS would be impacted to do authorization first and then do MBS Session start ?
Nokia Reply: Public safety would use MB2 interface and MBSF. Thus, no impact
Ericsson comment in r1:
Nokia seems to assume that 5MBS can only be used for Public Safety via MB2 and there is no possibility to adapt to SBI architecture, which in my view is a severe limitation of 5MBS.
Ericsson comment in r1:
What do we want to achieve with PCF for MBS Session management ? Why introducing such complexity?

## Slide 38
Answers to Questions by Ericsson
S2-2102727 Update the MBS Session Configuration Procedure
Q: Establishment or Notify?
Notify does not work as there is no MBS policy association established yet.
Nokia: Agree, would need to be establishment
Tencent: Agree, the MBS Policy Association should be first established from the NEF/MBSF to the MB-SMF, then a notify message is sent from the NEF/MBSF to the MB-SMF. For simplicity, the establish steps are not show here

## Slide 39
Answers to Questions by Ericsson
S2-2102439 Policy control for Multicast and Broadcast services
Q1: Why is Session binding needed?
Nokia: AF and MB-SMF both establish connections towards the PCF
Q3: MB-SMF interacts with PCF when AF started the MBS Session, but not at UE join.
Nokia: I agree. MB-SMF is unaware of UUs joining
Q2: Do we have some examples what PCRT may be needed?
Nokia: I left that FFS in my service proposal. Might be that we have nothing in the first release. Also depends on information provided by AMFs and SMFs
Ericsson comment in r1:
Why should both AF and MB-SMF establish connection towards the PCF?