## Slide 1: 5GS Assisted AIML Services and Transmissions (FS_5GAIML)
Prepared by OPPO
Notes: R18 SID proposal UE Assistant Application Layer Analytics AI capable UE assistant analytics R18 SID proposal on architecture enhancements to support UE involved AI services
R18 SID proposal on architecture enhancements to support vertical AI services

## Slide 2: Rel-18 SA1 Study on AI/ML Model Transmission (AMMT)
NOTE: SA2 has been focused on AI based analytics work to support network automation, but not much on how the service providers could leverage 5GS as the platform to assist the implementation and transmission to support their AI/MI operation.
The study of the use cases and the potential performance requirements for 5G system support of Artificial Intelligence (AI)/Machine Learning (ML) model distribution and transfer (download, upload, updates, etc.), and identifies traffic characteristics of AI/ML model distribution, transfer and training for various applications, e.g. video/speech recognition, robot control, automotive, other verticals.
          The aspects addressed in SA1 study include:
            AI/ML operation splitting between AI/ML endpoints;
            AI/ML model/data distribution and sharing over 5G system;
            Distributed/Federated Learning over 5G system.
Proposed Rel-18 SA2 study is to focus on enabling the AI/ML Services & Mobile Transmissions via 5GS assistance to support AI/ML model distribution, transfer, training and real-time control for various applications as defined by SA1 Rel-18 AMMT requirements,
e.g. video/speech recognition, robot control, automotive etc.
Notes: Bring more requirement when SA1 AMMT is concluded

## Slide 3: Widely used AI services
Image recognition
The AI model has been widely used for image recognition. Different AI model applies to different scenarios.
Real-time control (e.g. robot)
The real-time control helps to realize the unmanned services like auto-driving, automatic industry
Video streaming
AI model can be trained to realize/replace some functionalities of video/voice coding/encoding
……
Notes: How much the AF influence is used

## Slide 4: Key Aspects when enabling AI/ML services & transmission with 5GS assistance
High-level Key Aspects in this study to enable AI/ML service & transmission with 5GS assistance:
QoS enhancement, AF influence bandwidth control transmission (for unicast or multicast) and policy control in 5GS
5GC analytical information exposure extension to provide environmental (e.g. UE’s geographic location) and performance (e.g. QoS, load congestion) predictive analysis and forewarning to application server when implementing AI/ML analytic operation
Enabling UE and application server to support collaborative Federated Learning (FL) operation with the assistant from 5GS to implement Federated Learning operations and to support different models of FL
Each of the above considerations is further explored in next few slides
PCF
NWDAF
NEF
AF
SMF
AMF
UPF
gNB
UE
1) QoS enhancement, AF influence bandwidth control transmission & policy control
2) 5GC analytical information exposure extension to support application server AI/ML analytic operation
3) Collaborative analytic operation with the assistant from 5GS to support data pre-processing, model downloading, learning, training and reporting for various distributed learning operations (e.g. Federated Learning).
UE-side
Model
Partition
Network-side
Model
Partition
End Device
Network Server

## Slide 5: Potential issue: 1) QoS enhancement to support AI/ML services & transmission with 5GS assistance
  Enhancement to support asymmetric QoS
    For many AI enabled services, like Augmented Reality, the round-trip latency mostly matters. e.g. figure below shows the size of UL intermediate data can be much larger than DL.
    Asymmetric QoS helps to properly schedule the AN/CN resources for data transmission as long as the round trip latency performance is maintained
  Content-type aware QoS for model transmission support over 5GS
  AI/ML model is composed of model topology data and weight factor data, where the topology data needs higher transmission reliability for some use cases to ensure the model can be utilized accurately. AI/ML model data may be tagged to enable ML flow classification.
  ML flow classification mechanism is to derive the characteristics of the ML flow (e.g. the size of the previous N packets, source IP address, protocols or flow arrival interval) rather than checking the payloads of the packets so that encrypted flows can be classified and therefore proper QoS can be applied.
  New 5QI for AI/ML service transmission
  For different variants of AI/ML services that employ AI model splitting, model transmission, federated/distributed learning, new 5QI may be needed to provide asymmetric QoS support.
  Potential policy control and charging
  Determine whether any impact to existing policy control and aspects (e.g. lower charging rate for AI/ML transmission)
Notes: Structure data / parameter data
Quote a AMMT table and based on the table it propose to study how the 5GS is enhanced to support asymmetric QoS

## Slide 6: Potential issue: 2) 5GC analytical information exposure extension support for AI/ML services & transmissions with 5GS assistance
  The information exposed by 5GS can be real time analytics/alert of situation of the communication, for example:
  - prediction and alert the 3rd party of the GBR that cannot be guaranteed and how soon it could happen
  - prediction and alert the 3rd party that UE is moving towards a certain area, e.g. in 30 seconds
  The environments of communication (e.g. QoS, Location) could lead to a change of the AI/ML operation (e.g. bandwidth adjustment) and affect user experience. It is proposed to study what analytical information exposed by 5GC to assist AI/ML analytic operation
Split point | Required UL data rate (Mbps)
Candidate split point 0 (Cloud-based inference) | 36
Candidate split point 1 (after pool1 layer) | 65
Candidate split point 2 (after pool2 layer) | 41
Candidate split point 3 (after pool5 layer) | 4.8
Candidate split point 4 (Device-based inference) | N/A
e.g. As shown in table, there is a mapping between splitting point (operational behavior) and UL data rate (communication quality). Splitting point could be changed when detecting the change of the UL data rate (For model spiting, see slide 10 for more background info)
Excerpt from TR 22.874
NOTE: Operational splitting is a common and effective technique to support AI/ML analytic. The intent of operational splitting is to offload computation-intensive and energy-intensive training parts to Network Endpoints, whereas leave the privacy-sensitive and delay-sensitive training parts at the End Device.

## Slide 7: Potential issue 3): Co-operative Analytic Operation via assistant from 5GC to support different models of Federated Learning
FL imposes additional challenges to be operated over the mobile network that need to be addressed:
Support for FL training candidate devices selection according to specified criteria (e.g. wireless link condition, memory, storage, computing resources, priority handling of training data vs. other user data etc.)
Training time should be minimized since mobile devices may only stay in an environment for a short period of time
Transmission scheduling and network resources scalability considerations to provide unicast or multicast support for FL operation including Synchronous FL model (e.g. “Flocking” use case)
Avoidance communication disturbance (e.g. learning and reporting data transfer) which degrades the Federated Learning performance
Support for adaptive scheduling according to increase or decrease of AI/ML traffic demands (e.g switching to different AI/ML mode, start/stop task splitting, change task splitting point etc.) requested by application.
Aggregated performance monitoring for training UEs participating in the given FL operation and alerting FL training organizer
Support for exposure of QoS information for group of UEs which are FL training candidates to the authorized 3rd party service provider which hosts the FL training.
Gradiant uploading
latency
+ Federated aggregation
latency
+ global/local model
downloading latency
GPU computing time
at device
Support for various models of Federated Learning as described in SA1 Rel18 AMMT requirements.

## Slide 8: Proposed Study
Trigger a study in R18 to investigate the feasibility of 5GS enhancement support for AI/ML services & transmissions with 5GS assistance (S2-2103758). ,
QoS enhancement, AF influence bandwidth control transmission (unicast & multicast) and policy control
Study asymmetric QoS/ Content-type aware QoS/ New 5QI/ adaptive bandwidth control for AI/ML service transmission as well as policy control and charging
5GC analytical information exposure extension
Study real time analytics/prediction/alert to provide environmental and performance predictive analysis and forewarning to application server to assist AI/ML operation
Enabling UE and Application Server to support collaborative Federated Learning operation with assistant from 5GS
  FL training candidate device selection,
  Minimizing FL training delay
  Avoidance FL communication disturbance,
  Support aggregated performance monitoring and measurement for a group of UEs
  QoS info exposure for group of UEs
  Transmission scheduling for unicast and multicast FL operation including the synchronous FL model
  Adaptive scheduling for increase or decrease of AI/ML traffic demand
NOTE: More detailed requirements corresponding to the objectives described here can be referred to SA1 AMMT study.
PCF
NWDAF
NEF
AF
SMF
AMF
UPF
gNB
UE
1) QoS enhancement, AF influence bandwidth control transmission & policy control
2) 5GC analytical information exposure extension to support application server AI/ML analytic operation
3) Collaborative analytic operation with the assistant from 5GS to support data pre-processing, model downloading, learning, training and reporting for various distributed learning operations (e.g. Federated Learning).
UE-side
Model
Partition
Network-side
Model
Partition
End Device
Network Server

## Slide 9: Estimated Time Units Requirements to Study FS_5GAIML
 | Target Study Completion | Total TU Requested in 2021-2022 (Study) | Oct-21 #147e | Nov-21 #148e | Jan-22 #ad hoc | Feb-22 #149 | Apr-22 #150 | May-22 #150 | Max TU that can be granted to finish study
Total TUs Available for Rel-18 work |  |  |  |  |  |  |  |  | 
FS_5GAIML | Jun-2022 | 7 | 1 | 1 | 1 | 1 | 1 | 2 | 
WT# | Descriptions of Work Tasks | Requested TUs
1 | QoS enhancement, AF influence bandwidth control on the transmission and policy control to support AI/ML operation Asymmetric, Content-type aware QoS support with New 5QI for AI/ML service transmission; Policy control/charging support for AI/ML service transmission | 2.5
2 | 5GC analytical information exposure extension to assist AI/ML operation Study real-time analytics extension in 5GC to provide environmental and performance prediction (e.g. location, QoS, load congestion etc.) and forewarning to application server to assist the AI/ML operation. | 1.5
3 | Enabling UEs and Application Server to support collaborative Federated Learning (FL) operation with the assistance from 5GS FL training candidate device selection Ability to minimize FL training delay Ability to avoid FL communication disturbance Support aggregated performance monitoring and measurement for a group of UEs Support QoS information exposure for a group of UEs Support transmission scheduling for unicast or multicast transport for FL operation including the synchronous FL model operation Adaptive scheduling to respond to the increase and decrease of the AI/ML traffic demand All the functionalities above should be applicable to different models of FL as identified in SA1 Rel18 AMMT study | 3

## Slide 10: Backup and Reference Slides
Notes: Party pooper?

## Slide 11: Model Splitting
The device executes the inference up to a specific CNN layer and sends the intermediate data to the network server. The network server runs through the remaining CNN layers.
The split AI/ML image recognition algorithms can be analyzed based on the computation and data characteristics of the layers in the CNN. The intermediate data size transferred from one CNN layer to the next depends on the location of the split point. Hence, the required UL data rate is related to the model split point and the frame rate for the image recognition.
Split point | Approximate output data size (MByte) | Required UL data rate (Mbps)
Candidate split point 0 (Cloud-based inference) | 0.15 | 36
Candidate split point 1 (after pool1 layer) | 0.27 | 65
Candidate split point 2 (after pool2 layer) | 0.17 | 41
Candidate split point 3 (after pool5 layer) | 0.02 | 4.8
Candidate split point 4 (Device-based inference) | N/A | N/A
Required UL data rate for different split points of AlexNet model for video recognition @30FPS

## Slide 12: Main Use Cases on AI Imaging Recognition – Business Opportunity for Mobile Network Service Offerings for OTT Application
Logo Detection in Social Media Analytics
  Social listing (via social media posts) and brand monitoring support for marketing research and competitive analysis
  Business are using logo detection to calculate ROI from sponsoring sport events or to define whether their logo was misused
Medical Image Analysis
  Software powered by deep learning models help medical practitioners (e.g. radiologists) to deal with huge workload of interpreting various medical images: computed tomography (CT), ultrasound scans, magnetics resonance imaging (MRI) or x-rays etc.
  Medical images account for ~90%of all medical data.
Visual Product Sales & Marketing
  Improvement for online shopping experience to get detailed descriptions which could lead to instant order.
  Empowering marketing research opportunity to identify customer’s interests on fabric,style, color and to enable in-store personalization and product promotion.
Facial Recognition enabling Enterprise services and Private/Public Safety to streamline routine operations
  Additional biometric technology to enhance efficiency and security on routine operations.
Plus many more ……
Notes: Bring more requirement when SA1 AMMT is concluded

## Slide 13: AL Training vs. AI Inference
Puppy
Kitty
Untrained
Neural Network Model
Trained Model
New Information
“Puppy”
???
DEEP Learning
framework
App or New Service
Featuring New Data
Training Model
Optimized for Performance
Puppy
DEEP Learning
Training
Learning new information for Editing data
Inference
Applying this information to new data captured
Training
Dataset
New
Data
Puppy

## Slide 14: Machine Learning as a Process
Define Objectives
Data Preparation
Model Building
Model Deployment
Model Evaluation
- Define measurable and quantifiable goals
- Use this stage to learn about the problem
- Normalization
- Transformation
- Missing Values
- Outliers
- Data Splitting
Features Engineering
Estimating Performance
Evaluation and Model Selection
Study models accuracy
Work better than the naïve
approach or previous system
Do the results make sense in the context of the problem
Cite from Cern - Machine Learning with Spark MLlib

## Slide 15: ML as a Process: Data Preparation
Needed for several reasons
  Some Models have strict data requirements
    Scale of the data, data point intervals, etc
  Some characteristics of the data may impact dramatically on the model performance
Time on data preparation should not be underestimated
Raw Data
Data Trans-formation
Data Ready
Scaling
Centering
Skewness
Outliers
Missing Values
Errors
Missing Values
Dimensionality
Types Problems
Error Values
Different Scales
Many others
Modeling phase
Cite from Cern - Machine Learning with Spark MLlib

## Slide 16: ML as a Process: Model Building
Data Splitting
  Allocate data to different tasks
    model training
    performance evaluation
  Define Training, Validation and Test sets
Feature Selection (Review the decision made previously)
Estimating Performance
  Visualization of results – discovery interesting areas of the problem space
  Statistics and performance measures
Evaluation and Model selection
  The ‘no free lunch’ theorem no a priory assumptions can be made
  Avoid use of favorite models if NEEDED
Cite from Cern - Machine Learning with Spark MLlib

## Slide 17: Thanks!