## Slide 1
CATT, Thales
Support of Satellite Backhauls in 5GS

## Slide 2: Satellite backhauling scenarios
s1. gNB connects to 5GC via a single GEO satellite
s2. gNB connects to 5GC via a single NGSO satellite
s3. gNB connects to 5GC via a single satellite with ISL
s4. gNB connects to 5GC with backhaul connections over different satellites
s5. gNB connects to 5GC with hybrid backhauls (e.g., satellite and terrestrial backhauls)
s6. gNB on-board connects to 5GC via satellites
Supported In Rel-17

## Slide 3: Some other scenarios of using wireless backhauling
gNB connects to 5GC with backhaul connections provided by UAV(s)
gNB connects to 5GC with backhaul connections provided by HAPS (High Altitude Platform Station)

## Slide 4: Works in Rel 17 to support s1 and s2
Satellite backhaul category determination by SMF;
Event report from SMF to PCF on change of the backhaul;
Policy determination based on satellite backhaul category;
Notifying the AF on changes of the satellite backhaul category;
No new 5QI defined for services over satellite backhaul

## Slide 5: More backhauling scenarios to be considered in Rel 18
Backhaul with dynamical changed packet delivery latency, e.g. satellite backhaul with ISL;
A gNB connects to 5GC with multi-types of satellite backhauls
A gNB connects to 5GC via hybrid backhauls (e.g., satellite backhaul and Terrestrial backhaul)
A gNB on board connects to 5GC via backhaul(s) over satellite/HAPS

## Slide 6: Possible issues for study (1)
QoS related:
  Packet delivery latency: In rel 17, the packet delivery latency in the 5GS is indicated by satellite backhaul category, which is applicable when the backhaul connection only involves a single satellite, but doesn’t work if the backhaul connection involves ISL(s), since the ISL introduce extra transmit latency.
  E2E PDB: In rel 17, if a satellite backhaul is used, as no new 5QI is defined, an AF can only guess the real E2E PDB based on the satellite backhaul category reported by the PCF, and the UE application layer will not know the real E2E PDB, which may cause troubles for data transmission, e.g. unexpected latency.
  Bandwidth: Due to different satellite capability, e.g., working on different frequency bands, satellites may have different data transmission rates, which brings different backhaul bandwidth.

## Slide 7: Possible issues for study (2)
N2/N3 connection related:
  Backhaul change: Due to satellite movement, gNB movement or gNB internal logic to switch the backhaul connection between terrestrial network and satellite network, a gNB may be subject to backhaul link change, which may lead to the interruption of signalling/data transmission.
  N3 connection update: the N3 tunnel in use may not be available any longer when the under layer backhaul connection changes, e.g. the gNB IP address changes due to the backhaul being switched from terrestrial network to satellite network.
  TNLA characteristics awareness: A gNB may establish multi-type of backhaul connections towards the 5GC, when it serves a UE, the AMF can not know which type of backhaul connection is used to serve the UE, so that the AMF can not know whether the protocols on N1/N2 interface need to be adjusted.

## Slide 8: Possible issues for study (3)
Regulatory requirements related:
  A gNB on board may connect to 5GC via backhaul over satellite/HAPS. When the gNB moves out of home country (the country where the operator who deploys the gNB belongs), how does the gNB work:
    Which PLMN should be broadcasted?
    Which AMF should gNB selects?
    ….

## Slide 9: Rel 18 SID proposal
Objectives:
  Architecture enhancements for support of a backhaul with long/dynamical delay and/or limited bandwidth:
    Policy/QoS control enhancements based on the detection of packet delivery latency and/or backhaul bandwidth [3TU]
  Architecture enhancements for support of gNB with multi-types of backhauls:
    Awareness of the characteristics of each TNLA (e.g. latency) for protocol adaption on N1/N2 interface [2TU]
    UP connection management in case of backhaul connection change [2TU]
  Architecture enhancements for support of moving gNB using backhaul over, e.g., satellite/HAPS:
    Support of regulatory services if the gNB using backhaul over satellite/HAPS moves across the country boundary [2TU]

## Slide 10
Thank You!