## Slide 1: New SID on Enhancement to the 5GC LoCation Services Phase 3
CATT, Huawei
May 17th, 2021
SA2 Meeting #145 (e-meeting) S2-2103835
17-28 May 2021, Electronic meeting

## Slide 2: Motivation#1: location data security
Use case / problem to resolve
  An overwhelming pattern for vertical network deployment is as figure (left below):
    Only RAN, UPF, MEC(supporting LMF functionality) is deployed in the enterprise network;
    Control plane functions in Center Cloudlike AMF, co-operate with MEC for getting UE location;
  Location signaling and UE location data are exposed to the public network(right below figure), a big concern to the enterprise
  Objectives
  Define new LCS procedure for vertical network use case, where the location data is not exposed to public network.

## Slide 3: Motivation#2: support of LPHAP
SA1 work item on low power high accuracy positioning (LPHAP) has challenging requirements on 5G system, in terms of UE power saving, and positioning accuracy.
Existing positioning mechanism cannot satisfy these requirements, and in the meantime 5GS needs to support both the “normal” positioning and the LPHAP. Therefore it is necessary to introduce a new UE type i.e. “LPHAP UE”.
System level enhancement consideration:
  AMF identifies the LPHAP UE, and manages it with “low power” mechanism.
  LMF identifies the LPHAP UE, and determine a specific positioning method, coordinated with RAN.

## Slide 4: Motivation#3: Uu+PC5 combined positioning
The accuracy of positioning heavily relies on Line of Sight (LoS) paths.
Objects can potentially block the LoS paths in the indoor positioning cases, e.g., high big shelters in the warehouse.
Additional low complexity node is required to create more potential LoS paths, i.e., UE-type nodes is deployed as complementary nodes to assist positioning.
UE type nodes
LMF
RAN
CN
LMF
RAN
CN
PC5
Uu